## Slide 1: NON-LABORATORY STAFF BLOOD CULTURE PHELBOTOMY
OSCAR G. JOHNSON
VA MEDICAL CENTER
NOVEMBER 2015

## Slide 2: Volume of Blood Cultures
Concentration of organisms in most cases of bacteremia is low, especially if the patient is on antimicrobial therapy
  One set of blood cultures is defined as two SPS tubes
Draw blood into SPS (glass, rubber-toped tubes)
  8-10 mL per tube recommended (16-20 mL/set cultures)
  Creates blood-to-medium ratios of 1:5 to 1:10
    Underfill consequences (<6.5 mL):
      Pathogen may not be present
    Overfill consequences (>10 mL):
      Insufficient space for nutrients
      and chemicals to support
      pathogen growth

## Slide 3: Blood Culture Phlebotomy Preparation
Cleanse hands and don appropriate PPE
2 forms of patient identification
Choose phlebotomy site(s)
  Tourniquet applied to select site, released once determined
    NEVER LEAVE THE TOURNIQUET ON FOR LONGER THAN 1 MINUTE
  Preferred veinipuncture sites
Assemble needle
Cleanse rubber
tops of SPS tubes
with Chloraprep One-Step
Applicator (or Iodine is
acceptable)

## Slide 4: Cleansing the Site
ChloraPrep One-Step Frepp Applicator
  2% chlorhexidine gluconate, 70% isopropyl alcohol
  Sterilizes area up to 2.5 in. x 2.5 in.
  Latex free
  Discard after single use

## Slide 5: Cleansing the Site (cont.)
  Pinch wings to break ampule and release antiseptic
    Do not touch sponge
    Wet sponge by repeatedly pressing and releasing sponge against site until liquid visible on skin
    Use repeated back-and-forth strokes of applicator for approx. 30 sec
    Do not re-palpate site; touch above actual entry site to anchor vein
  Allow site to air dry for approximately 1 min
      Do not blot or wipe away
      Critical! If needle enters vein before prep has dried, normal flora of skin may not have been killed, and can enter culture
      Most common cause of contamination

## Slide 6: Direct Draws Into SPS Tubes
Place SPS tube into needle, pressing down to penetrate septa and obtain blood flow
Monitor blood flow closely to assure proper flow is obtained and to avoid backflow of tube contents into tubing
Release tourniquet as soon as blood starts to flow
into bottle, or within 1 min

## Slide 7: Blood Culture Venipuncture Overview
Choose site(s)
Assemble equipment
Sterilize tops of SPS Tubes and site(s)
  ChloraPrep One-Step Frepp Applicator
    One for tubes, one for site
  Scrub site for 30 sec, allow 1 min for drying
Perform Veinipuncture
  ALWAYS draw blood cultures first, following Order of Draw
  Draw into SPS tubes
  8-10 mL blood per tube
Label Tubes
  Gently invert tubes 5-10 times

## Slide 8: Labeling Blood Cultures
Verify patient name and SSN
Initial and note date & time of draw
Indicate on each label the # of sets
  Example: Culture set #1 drawn from Right Antecubital
  by AB on
  11/5/15
  at 0800
  Label should
  look like:
ZZZTEST, PATIENT
111223333
OCT 10, 1910
AB
11/5/15
0800
#1

## Slide 9: Options for Collecting Two Sets of Cultures
  Option #1 – One set from each arm (no IV in place)
  Option #2 – One set from arm without IV, one set
  from arm with non-antibiotic IV
  (Most likely scenario for UC)
  Option #3 – One set from arm without IV, one set
  from central or PICC line
  *Taking two blood culture sets from the
  SAME SITE at the SAME TIME
  is not recommended*