## Slide 1: Instrument Manager Job Aid CHEMISTRY
DCW V8

## Slide 2: Purpose
To ensure hemolyzed specimen result comments (e.g., "Interpret result with caution due to hemolysis which may affect result") are visible in KP HealthConnect (KPHC) when results are released.

## Slide 3: Index Ranges: Hemolysis, Icteria, Lipemia (HILs)
See HIL Interpretation Guide below:

## Slide 4: Step 1: Identify Hemolyzed Specimen
Instrument Manager will hold all electrolyte results when the potassium hemolysis index is >= 100. Pull specimen to confirm hemolysis.
  Use the “Rack Column” to identify the rack number

## Slide 5: Step 1-2: Identify Hemolyzed Specimen
If specimen is hemolyzed and H>=250, reject specimen in DI and cancel order in Cerner using cancel reason “Hemolyzed Specimen, Test not performed’.

## Slide 6: Step 1-2: Identify Hemolyzed Specimen
If specimen is hemolyzed and H>=250, reject specimen in DI and cancel order in Cerner using cancel reason “Hemolyzed Specimen, Test not performed’.

## Slide 7: Step 1-2: Identify Hemolyzed Specimen
If specimen is hemolyzed and H>=250, reject specimen in DI and cancel order in Cerner using cancel reason “Hemolyzed Specimen, Test not performed’.

## Slide 8: Step 2: If Hemolysis = 100-249
Instrument Manager will hold all electrolyte results when the potassium hemolysis index is >100 and <249. Pull specimen to confirm hemolysis.
  Use the “Rack Column” to identify the rack number

## Slide 9: Step 2-1: Update K Result Comment
Select the Potassium (K) row under the test worksheet

## Slide 10: Step 2-2: Update K Result Comment
Click on the “Edit Comment(s)” button

## Slide 11: Step 2-3: Update K Result Comment
Select the pre-attached Potassium result comment

## Slide 12: Step 2-4: Update K Result Comment
Enter the approved comment “Interpret result with caution due to hemolysis which may affect result”

## Slide 13: Step 2-5: Update K Result Comment
Click “OK” to proceed with accepting the new result comment

## Slide 14: Step 2-6: Update K Result Comment
Click “Yes” to accept the new comment

## Slide 15: Step 2-7: Update K Result Comment
Verify that the Potassium result comment was updated correctly

## Slide 16: Step 2-8: Update K Result Comment
Release results to Cerner

## Slide 17: Step 3: Verify in KPHC
Confirm the results and hemolyzed comment are visible in KPHC immediately after releasing.

## Slide 18: Step 4: If Comment Is Missing in KPHC
Confirm the results and hemolyzed comment are visible in KPHC immediately after releasing.

## Slide 19: Key Reminders
Potassium results are the most susceptible to hemolysis (false elevation).
Release order matters, the last test released will have its test comment applied.
Comments may not automatically cross to KPHC
Always review in KPHC after releasing electrolyte results for hemolyzed specimen.