## Slide 1
CELL-DYN Sapphire™ Software-Navigation

## Slide 2
CELL-DYN Sapphire™ - Software
  The Cell-DYN Sapphire™ uses a Linux designed Software.
  The benefits of this approach include:
    Flexible Operating System upgrades
    Improved functionality
    On-line Operator’s Manual
    Ease of navigation and support
    Flexible printer options
    Data archiving

## Slide 3
Status Panel
The Status Panel consists of four distinct regions:
Provides the on-off status of each Quality Control program.
QC/X-B Status
White Means turned-ON
Provides suggestions of subsequent action the Operator can take with respect to the present status of the System.
Ready, Busy, Not Ready, Offline, Online: Initializing status
Autoloader or Open Tube mode status
Host Computer up/down Status and LIS Work List Download and Host Query Setup on-off Status
Auto-Transmit and Printer Setup on-off status
White Means turned - ON
Displays the data station system date and time, and allows for entering, checking, or changing the Operator ID
Select a four character ID

## Slide 4
Control Panel
The four distinct regions in the Control Panel area on the CELL-DYN Sapphire Main Screen Console provide access to major Analyzer, Administrative, and Setup functionality, management of saved System Initiated Messages, and access to initiate specimen processing in the Run Loader and Run Open Tube modes.
Displays the level and number of System Initiated Messages currently saved in the System and allows for reviewing and clearing the stored saved messages
Displays the Next Open Tube Setup Mini-Window when the System is in Run Open Tube mode.
Allows the Operator to select Run Loader or Run Open Tube System modes.
Displays the current CELL-DYN Sapphire software version and provides Operator access to the major Analyzer, Administrative, and Setup functionality of the System.

## Slide 5
Analyzer Menu
Functions included under the Analyzer > button support administrative and maintenance aspects of the instrument.
Reagent Log
  To create Log Entries and Print Logs
Special Protocols
  Maintenance Procedures
Calibration
  Calibration Factors, Calibration Logs
List Mode On/Off
  Turns On/Off List Mode Collection
STD Ref. Particles
  Service Use Only
Setpoints
  Service Use Only, Access Optical Setpoints
Extended Optical Count
  Service Use Only
Optical Signature File
  Service Use Only
Prepare for Data Station Power Down
  Prepares Data Station Software for Power Down

## Slide 6
Analyzer Menu - Special Protocols Window
The SPECIAL PROTOCOLS window is where the operator can activate important activities including Autoclean, Prime, and To Standby.
Special Protocols for the following are activated in this window:
  System
  Reservoirs
  Sample Processor and Autoloader
  Transducers
  Vacuum and Pressure System
  Tubing (Sample Transfer Pump)
  Prepare for Shipment

## Slide 7
Shared Region Panel Buttons
Data Log
QC >
    QC Files 1-20
    Moving Average
    Paired Difference
Work List
Run View
Print…
Transmit..
To view the Data Log
To Add/View tests Requests
To Print
View QC Files 1-20
View Moving Average Files
View Paired Difference
Displays Results after each cycle
Transmit