## Slide 1
May Safety Presentation
5.2022 | Department of Lab & Pathology

## Slide 3: Deviations Reported via RLs
108 Deviations in April

## Slide 4: Most Common Deviation in April
23 Deviations in April

## Slide 5: 2nd Most Common Deviation
14 Deviations in April

## Slide 6: 3rd Most Common Deviation
11 Deviations in April

## Slide 7: Lab Employee Hazard Awareness
May’s Topic
– Emergency Eyewash

## Slide 8: Why you need them?
Even with the best engineering controls, PPE and safety precautions, chemical/biohazard exposure can still happen
They give employees the ability to immediately wash hazardous substances from their eyes
          Preventing potential harm
          Particularly with…
            Corrosives

## Slide 9: How to use them
After exposure it is important to reach the eyewash station within…
10-15 seconds
The exposed area needs to be flushed for no less than…
15 minutes
Call for immediate medical assistance

## Slide 10
Hold eyes open when flushing
Remove contact lenses

## Slide 11: Eyewash QC
Eyewash should be activated weekly for a period long enough to verify operation and ensure that flushing fluid is available
Activating the eyewash weekly also clears sediment and bacteria from the stagnate water

## Slide 12: Regulation
Eyewash stations need to be located such that an exposed employee could reach them within…
10 seconds
Or no more than 55 feet from location of exposure

## Slide 13: Eyewash Bottles
Eyewash bottles are NOT to be used as a substitute for flushing your eyes after exposure
They are for immediate use while in transit to a stationary eyewash where you should then flush your eyes for 15 minutes

## Slide 14: Eyewash Bottle QC
Eyewash bottles must be examined weekly and be discarded if...
  Seal is broken
  Expiration date is exceeded
  Solution is turbid
      - this could indicate bacterial growth
EH&S will provide replacements upon request

## Slide 15: April Safety Topic of the Month Quiz
96 respondents
76 people scored 100%
Winner of the drawing
  Monique Patten
  from Central Processing

## Slide 16: Good Catches in March
Great Work! Thank you!

## Slide 17: Good Catch Recipient for April Mary Miller Central Processing Lab

## Slide 18: Cross Check & Assist

## Slide 19: Thank you for your participation!