## Slide 1: Blood Bank / BMT General Safety, Power Failure, Chemical Hygiene
Larry Waldron MT(ASCP)CM
BB Specialist Technologist / Education Coordinator
Georgia Kontos MS, MLS(ASCP) CM
Blood Bank/SCTCT Safety Representative

## Slide 2: Emergency Phone Numbers
Fire
Security
Chemical Spill
Sudden Illness
Call
6-9111
Call 6-3305

## Slide 3: Where to find important information
Hospital Fire/Disaster/Safety Manual
  The Fire/Disaster/Safety Manual has moved to the Sharepoint site.
  https://wakehealth.sharepoint.com/sites/ehs/SitePages/FDS.aspx
Infection Control
  Intranet > Tools > Policies > Patient Care > Infection Control > BBF Exposure Control Plan
Chemical Safety
  Chemical Hygiene Plan, Lab Safety Manual in laboratory

## Slide 4: Blood and Body Fluid Spill
When treating any blood and body fluid
  Wear gloves
  Wear protective eye wear / mask if splashing to face is possible
  Wear protective clothing (barrier gown, apron, coveralls) if splashing onto the body is possible.

## Slide 5: Blood and Body Fluid Spill
Blood spills <20mL
  Mop with High Dilution 256 (1oz/gallon)
Blood spills >20mL
  Place wet floor signs in area
  Utilize towels to prevent spreading
  Cover blood spill with High Dilution 256 (1oz/gallon), mop up
  Sanitize floor with new mop head and High Dilution 256 (1oz/gallon)
  Place saturated linen in soiled linen bin.
  Disinfect equipment / remove PPE
  Or Call Housekeeping at 64901

## Slide 6: Blood Bank/ SCTCT Task List
Review the Blood Bank and Stem Cell Transplant and Cellular Therapy Lab Task Lists in Section 18 of the Laboratory Safety Manual.
  Familiarize yourself with the required PPE for the tasks listed.

## Slide 7: Laboratory Chemicals
Review the list of chemicals found in Section 4 of the Laboratory Safety Manual.
  Annual Chemical Review: Attachment A
  Familiarize yourself with the Chemical Names, Common Names, Exposure Limits and Toxic / Carcinogenic nature of the chemicals found in the BB and SCTCT.

## Slide 8: Chemical Spills
Your spill is >300 ml
  Don’t clean it up! Call 6-9111
Your spill is <300 ml
  Use your spill kit to clean it up.
  Call EH&S 6-9375
How do I know if my spill is > or < 300 mL?
300 mL is a pretty big spill! A can of soda is 355 ml. Picture what it would look like if you poured a can of soda onto the floor and compare that to your spill.

## Slide 9: Chemical Spills
IF the chemical spill is either a Carcinogenic, a Reproductive Toxin or Highly Toxic: Evacuate Immediately! Call 6-9111

## Slide 10: Hand Hygiene
WFBH adheres to the Center for Disease Control and Prevention’s “Guideline for Hand Hygiene in Health Care Settings”
  Implements procedures to remove transient microbial flora and reduce transmission of microorganisms in the health-care setting

## Slide 11: Follow CDC Guidelines for Handwashing with Soap and Water

## Slide 12: Follow CDC Guidelines for Hand Hygiene using Alcohol Based Waterless Antiseptic Agent

## Slide 13: Eye Wash Stations
Eye wash stations are available for use when caustic materials are splashed into the eye
Blood Bank: at CP sink
SCTCT: at hand washing sink in the processing room
New eye wash in the BB coming soon!

## Slide 14: Employee Occurrence Reporting
An employee occurrence is any undesirable incident an employee experiences while at work. Examples include, but are not limited to:
  Injury on the job
  Inadvertent exposure to biohazardous materials
To Report an Employee Occurrence Incident:
  Intranet > Tools > Occurrence Reporting > Employee Occurrence Reporting

## Slide 15: SCTCT Oxygen Sensor
    There are two Oxygen sensors in the SCTCT cryo room. One on each side of the middle dividing wall.
    This sensor is monitored by the Rees system node number 89 and 92.
    There will be an audible alarm from the sensors themselves when the Oxygen is to low in the cryo room.
    When you hear the alarm exit the cryo room immediately.
    You can monitor the Oxygen levels in the cryo room from the Rees system.
    You can safely check the reservoirs for LN2 leaks by observing the video monitoring system which shows both sides of the cryo room
    Do not enter the cryo room until the Rees detects Oxygen levels of >19%.

## Slide 16: Hospital Power Failure Policies
In the event of a power failure, any equipment plugged into a red outlet should continue to function.
  Refer to Lab Safety Manual / Power Failure section / Power Failure Policies for Hospital wide guidelines on how to handle specific power failure problems.

## Slide 17: BB/SCTCT Power Failure Policies
Blood Bank/SCTCT Specific Power Failure Policies
  Blood Bank Protocol Manual or SCTCT Miscellaneous Manual
    BB.Policies.0056
    SCT-Misc-1018
  Refrigerators and freezers on red emergency power outlets
  Workstations, Instrumentation on emergency power

## Slide 18: BB/SCTCT Power Failure Policies
3 categories of power loss
  Some emergency power outlets in BB / SCTCT failed
    Call Engineering (6-4841) and On Call BB Mgmt
  Most of the outlets in BB / SCTCT failed but other areas of Med Center are operable
    On Call BB Mgmt, Manager, Medical Director, and Call Engineering (6-4841)
  Total Med Center wide power failure
    On Call BB Mgmt, Manager, Medical Director, and Call Engineering (6-4841)

## Slide 19: Chemical Hygiene Plan
All employees should review the Chemical Hygiene Plan
  Refer to: Lab Safety Manual / Chemical Safety Chemical Hygiene Plan section for specific information pertaining to:
    General Operations
    Lab section operations
    Training
    Labeling of hazardous chemicals
    Storage
    Equipment inspection and maintenance
    PPE
    Chemical and Contaminated waste removal and disposal

## Slide 20: SDS Sheets
SDS (Safety Data Sheets) are accessible via the Intranet
  Intranet > Tools > Software > SDS
    You will be prompted for your Med Center username and password before you can access the form.
    Enter the product name for which you desire the SDS sheet into the electronic form.
  SDS sheets are also available in the SDS notebooks in the Blood Bank and SCTCT Lab.

## Slide 21: Blood Bank Irradiation Safety
“The Gammacell Irradiator uses caesium-137 as a radiation source. The two types of ionizing radiation emitted by the decay of unstable atoms of caesium-137 are Beta and Gamma radiation. The encapsulation of the caesium-137 in the Gammacell Irradiator prevents the Beta radiation from reaching the sample. However, the Gamma radiation emitted is very penetrating and does reach the sample. Gamma radiation is composed of electromagnetic waves that travel much like light, x-rays or microwaves. It is important to recognize that when a sample receives Gamma radiation, no transfer of radioactive material takes place. Your sample does not become radioactive”

## Slide 22: Blood Bank Irradiation Safety
The Gammacell Irradiator protects the user through the use of the steel-encased lead shield that reduces the radiation levels to acceptable levels for those working around the unit. When compared with typical radiation fields found in day-to-day life, the levels emitted from the Gammacell Irradiator, values are comparable.
  Review section 18 of the Laboratory Safety Manual

## Slide 23: A few noteworthy names….
Director of Environmental Health and Safety
  Feodor Bijkersma
    716-5576
Laboratory Compliance, Safety and Quality Officer
  Melanie Haire
    713-4285
Transfusion Safety Coordinator
  Bobbi Jo Tutterow
    713-4108
Blood Bank / SCTCT Safety Representative
  Georgia Kontos