## Slide 1: Updates to Flow Cytometry Math

## Slide 2: Background
Flow cytometry is transitioning to using two new analyzers, the Aquios and the Lyric.
These new analyzers will allow Flow Cytometry to perform FDA approved testing in a single platform format, the gold standard for their industry.
The new testing also minimizes the number of steps involved where user error can be introduced, for example in dilution or timing of incubation.

## Slide 3: White Count
Part of moving to a single platform is using the white count performed by the flow cytometer to perform our WBC product calculations
We will retain a printout of the WBC from Flow in the patient chart.
This might change our timing on performing CD34 counts – we will likely get both of these values at the same time.
We will still perform a Sysmex WBC so we are still able to freeze cells in a timely manner (so we will know the concentration is less that 5 x 108)
When calculating WBC for our product, we will need to factor in the dilution of the tube that we gave to Flow (Pre = 10x; Post = 100x)

## Slide 4: How will this affect SCTCT Lab?
Flow results in EPIC will be resulted in the units cells/µL.
For now, the CD3 will remain the same, only CD34 will be affected.
Math will be changing, only when calculating CD34 doses.
We will also be using the WBC that Flow performs in our worksheets.
We will still perform a Sysmex WBC for comparison.
The Autologous Cryoprocessing Worksheet will be updated and validated prior to the conversion.
The Autologous procedure will also be updated.

## Slide 5: New Calculations – CD34
Cells/µL x 1000 x volume of product (mL) x dilution of tube given to flow= Total CD34
Example: Cells/µL = 200 (This is the value in EPIC from Flow Lab)
Product volume = 318mL
Pre-processing, so 10x dilution
200 x 1000 x 318 x 10 = 6.36 x 108 = Total CD34
You would then divide by the patient weight to obtain CD34+/kg.

## Slide 6: Next Steps
Go-Live is April 28th
We will practice with the new worksheet next week as part of validation.
After Go-Live, everyone should be aware and make sure you have multiple techs review results (or Dr. Fadeyi) prior to reporting.
Complete this training, and immediately report any problems!