## Slide 1: Part VIII
Principles of Serological Testing

## Slide 2: Chapter Overview
Blood specimen preparation and measuring
Simple dilutions
Compound dilutions
Testing parameters

## Slide 3: Blood Specimen Preparation and Measuring
Serology
  Study of fluid components in the blood, especially antibodies
Serum
  Liquid portion of blood minus coagulation factors
  Most frequently encountered specimen in immunologic testing
  Separated from other components of a blood specimen via centrifuge

## Slide 4: Blood Specimen Preparation and Measuring
Ideally, use fresh serum that has not been heated
For certain tests, complement may need to be inactivated
  Complement may interfere with test results
  Heat sample to 56°C for 30 minutes

## Slide 5: Blood Specimen Preparation and Measuring
Storage (if testing is delayed)
  Between 2°C and 8°C for up to 72 hours
  Frozen at –20°C or below
Pipettes
  Volumetric—deliver only one volume
  Graduated—marked to allow for varying amounts
    Serological
    Blowout
  Micropipettes—deliver small volumes

## Slide 6: Blood Specimen Preparation and Measuring
Notes: Figure 9-3. (A) Steps in accurately measuring a liquid with a serological pipette. (B) How to read a meniscus.

## Slide 7: Blood Specimen Preparation and Measuring
Notes: Figure 9-3. (A) Steps in accurately measuring a liquid with a serological pipette. (B) How to read a meniscus.

## Slide 8: Dilutions
Solute is the material being diluted
Diluent is the medium making up the rest of the solution
Relationship between the two is expressed as a ratio or fraction
Equations are used to determine:
  Total volume of a solution
  Amount of solute needed
  Amount of diluent needed

## Slide 9: Simple Dilutions
1/Dilution = Amount of Solute/Total Volume
1/(Dilution – 1) = Amount of Solute/Amount of Diluent
Notes: The instructor may choose to include class-specific examples.

## Slide 10: Compound Dilutions
Are made when large dilutions are needed
Require several steps of making several smaller dilutions (serial dilutions)
Notes: Figure 9-6. Serial dilution. Each tube contains the same amount of diluent and a blue dye (food coloring). Each time a dilution is made, the amount of dye is cut in half in each successive tube. The final volume of each tube should be exactly the same. The color becomes visibly lighter with each dilution.

## Slide 11: Compound Dilutions
Plan the number and size of simple dilutions necessary to reach the desired end point
Calculate each simple dilution, keeping the dilution factor the same at each step
Set up the series of tubes
Obtain the final dilution
  Count the number of tubes used
  Set up a multiplication series in which the original dilution factor is raised to a power equal to the number of tubes

## Slide 12: Compound Solutions
Titer
  The last tube in which a positive reaction is visible
  An indicator of an antibody’s strength

## Slide 13: Test Parameters
Sensitivity
  Proportion of people who have a disease or condition and who have a positive test
  Indicates how small an amount can be measured and still produce a positive test result
  % = × 100

## Slide 14: Test Parameters
Specificity
  Proportion of people who do not have a disease or condition who have a negative test
  Measures the substance that it is designed to measure, not interfering substances
  % = × 100

## Slide 15: Test Parameters
Positive predictive value
  The probability that a person with a positive screening test actually has the disease
  % = × 100

## Slide 16: Test Parameters
Negative predictive value
  Probability that a person with a negative screening test does not have the disease
  % = × 100

## Slide 17: Summary
Serum for serological testing is obtained by allowing a sterile tube to clot at either room temperature or 4°C and then removing the serum from the clot after centrifugation.
Pipette types include volumetric, graduated, serological, and micropipettes.
A dilution is the addition of a liquid to make a weaker solution of either a reagent or a patient specimen.

## Slide 18: Summary
Patient serum, the solute, is made weaker by adding diluent so that the antibody present is not as concentrated.
The relationship between the serum and the total volume can be expressed as a ratio or as a fraction.
A serial dilution involves making several dilutions in which the dilution factor is the same.

## Slide 19: Summary
Serial dilutions are used to determine the titer, or strength, of an antibody.
Sensitivity is the proportion of people who have a specific disease or condition and have a positive test for that disease or condition.
Specificity is the proportion of people who do not have the disease or condition and who have a negative test for that disease or condition.

## Slide 20: Summary
The positive predictive value is the likelihood that a person with a positive screening test actually has the disease.
The negative predictive value is the probability that a person with a negative screening test does not have the disease.