## Slide 1: Chapter 15
Blood Component Preparation and Therapy

## Slide 2: Objectives (1 of 3)
Explain the benefits of component separation
Define storage lesion, and list the elements that change during blood storage
Compare the anticoagulant and preservative solutions with regard to expiration and content
Illustrate the steps in blood component preparation

## Slide 3: Objectives (2 of 3)
Given certain patient clinical conditions, state the blood component most appropriate for their transfusion needs
State the storage temperature and storage limits for each blood component
Given laboratory quality control test measurements, determine which component products meet acceptable AABB standards and Food and Drug Administration (FDA) guidelines

## Slide 4: Objectives (3 of 3)
Explain the intent and activities of the FDA in regulating blood component preparation, storage, and distribution
List the labeling requirements common to all blood components and the International Society of Blood Transfusion (ISBT)128 advantages
Discuss the importance of monitored storage equipment for blood components and the alarm requirements
Describe essential aspects of safe blood administration

## Slide 5: Blood Collection and Storage
Blood is collected in a primary bag containing anticoagulants and preservatives
The blood collection set is sterile and considered a closed system
If ports or other areas are exposed to air, the system becomes an open system

## Slide 6: Anticoagulant–Preservative Composition
Table 15.1 Anticoagulant-Preservative Composition: Purpose and Storage Limits | 
Chemical | Purpose
Dextrose | Supports ATP generation by glycolytic pathway
Adenine | Acts as substrate for red cell ATP synthesis
Citrate | Prevents coagulation by chelating calcium, also protects red cell membrane
Sodium biphosphate | Prevents excessive decrease in pH
Mannitol | Osmotic diuretic acts as membrane stabilizer
Red cell anticoagulant/preservative | Storage limit (days)
CPD/citrate-phosphate-dextrose | 21
CP2D/citrate-phosphate-2-dextrose | 21
CPDA-1/citrate-phosphate-dextrose-adenine | 35
AS-1 (Adsol); AS-5 (Nutricel)/dextrose, adenine, mannitol, saline | 42
AS-3 (Optisol)/dextrose, adenine, saline, citrate | 42
AS-7 (SLOX)/dextrose, adenine, mannitol, saline, citrate, sodium bicarbonate | 42
ATP, Adenosine triphosphate. | 

## Slide 7: Anticoagulant-Preservatives
CPD
  Citrate-phosphate-dextrose; 21-day expiration time
CP2D
  Citrate-phosphate-2-dextrose; 21-day expiration time
CPDA-1
  Citrate-phosphate-dextrose-adenine; 35-day expiration time
Additive solutions: AS-1, AS-2, AS-5
  Must be added within 72 hours of whole blood collection
  Extend storage time to 42 days

## Slide 8: Component Preparation
Whole blood is centrifuged at a LIGHT spin
  Platelet-rich plasma (PRP) is expelled into a satellite bag
  Additive solution is added to red blood cells (RBCs), followed by leukoreduction (optional)
PRP is centrifuged at a HEAVY spin
  Platelets are separated from plasma (pH 6.2)
  Plasma can be further processed as fresh frozen plasma (FFP)
  FFP can be processed into cryoprecipitate

## Slide 9: Component Storage
Table 15.2 Storage Temperature, Expiration Limits, and Quality Control Requirements of Selected Blood Components |  |  | 
Component | Storage temperature | Expiration limits | Quality control: minimum requirements4
Whole Blood | Storage: 1–6° C; Shipping: 1–10° C | CPD, CP2D: 21 days CPDA-1: 35 days | 
RBCs | Storage: 1–6° C; Shipping: 1–10° C | CPD, CP2D: 21 days CPDA-1: 35 days AS-1, AS-3, AS-5, AS-7: 42 days | Hematocrit: ≤80% in CPDA-1 units
Frozen RBCs | ≤–65° C | CPD, CPDA-1: 10 yr | None
RBCs, Deglycerolized or Washed (open system) | 1–6° C | 24 hr | Visual hemoglobin check; Method known to provide a ≥80% RBC recovery
Irradiated RBCs | 1–6° C | 28 days from irradiation or original outdate, whichever is first | Irradiator QC applied 2500 cGy/rad in center of unit
RBCs Leukocytes Reduced | 1–6° C | Depends on anticoagulant/preservative | <5.0 × 106 residual leukocytes and 85% of original red cells retained
Plasma, Frozen Within 24 Hours After Phlebotomy (PF24) | ≤–18° C | 1 yr | None
Fresh Frozen Plasma | ≤–18° C ≤–65° C | 1 yr 7 yr | None
FFP, PF24, thawed | 1–6° C | 24 hr | None
Thawed Plasma | 1-6° C | 5 days from thawing | Not FDA-licensed product
Cryoprecipitated AHF | ≤–18° C | 1 yr | Factor VIII: ≥80 IU and ≥150 mg fibrinogen
Pooled Cryoprecipitated AHF (after thawing) | 20–24° C | 4 hr | Factor VIII: ≥80 IU and ≥150 mg fibrinogen times number in pool
Platelets | 20–24° C with continuous agitation | 5 days | ≥5.5 × 1010 platelets in 90% of units tested; pH ≥6.2
Pooled Platelets (open system) | 20–24° C with continuous agitation | 4 hr | None
Apheresis Platelets Leukocytes Reduced | 20–24° C with continuous agitation | Open system: within 4 hr Closed system: 5 days | <5.0 × 106 residual leukocytes in 95% of units; ≥3.0 × 1011 platelets in 90% of units tested; pH ≥6.2
Apheresis Granulocytes | 20–24° C | 24 hr | ≥ 1.0 × 1010 granulocytes in 75% of units tested
CPD, Citrate-phosphate-dextrose; CP2D, citrate-phosphate-2-dextrose; CPDA-1, citrate-phosphate-dextrose-adenine; RBCs, red blood cells; As, additive solution; FFP, fresh frozen plasma; CRYO, cryoprecipitated antihemophilic factor; PF24, plasma frozen within 24 hours of phlebotomy; QC, quality control. Source: Fung MK, editor: Technical manual, ed 18, Bethesda, MD, 2014, AABB. |  |  | 

## Slide 10: Whole Blood
Consists of all components
Indicated for patients who are:
  Actively bleeding
  Undergoing exchange transfusion
Increases hemoglobin by 1 g/dL
Increases hematocrit by 3%
Must be ABO identical and crossmatched

## Slide 11: RBC Components
One unit of RBCs increases the hemoglobin by 1 g/dL and the hematocrit by 3%
Indicated for:
  Patients undergoing chemotherapy or irradiation
  Trauma victims
  Patients undergoing cardiac, orthopedic, or other surgeries
  End-stage renal disease
  Premature infants
  Sickle cell patients

## Slide 12: Leukocyte-Reduced RBCs (1 of 2)
Reactions to leukocytes can cause fever, shaking, and chills
Cytokines produced by leukocytes can cause febrile reactions
An in-line filter is used to remove leukocytes before storage

## Slide 13: Leukocyte-Reduced RBCs (2 of 2)
Leukoreduction also removes cytomegalovirus (CMV), which resides in white blood cells (WBCs)
Removing leukocytes does not prevent graft-versus-host (GVH) disease
Final unit must contain less than 5 x 106 WBCs

## Slide 14: Apheresis RBCs
Automated collection allows:
  1 unit every 8 weeks
  2 units every 16 weeks (double RBCs)
Saline replaces the lost fluid in the donor
Final component must have:
  Hemoglobin of at least 51 g
  Minimum volume of 153 mL
Double units are separated into 2 units

## Slide 15: Frozen RBCs (1 of 2)
High-glycerol method
Glycerol concentration is 40%
Initial freezing is at –80° C or –65° C
Storage is at –65° C for up to 10 years
More common method used
Low-glycerol method
Glycerol concentration is 20%
Initial freezing is at –196° C
Maximum storage of –120° C for 10 years

## Slide 16: Frozen RBCs (2 of 2)
Deglycerolization
  After thawing, the unit is washed with a series of saline solutions to remove glycerol
  Considered “open system”; expiration time is 24 hours

## Slide 17: Washed RBCs
  Washing with normal saline may remove plasma proteins that cause allergic, febrile, or anaphylactic reactions
  Unit has a 24-hour outdate

## Slide 18: Deglycerolization

## Slide 19: Irradiated RBCs
Irradiation prevents transfusion-related (GVH) disease
GVH disease is a reaction toward human leukocyte antigens (HLAs) on T cells
RBCs and platelets must be irradiated if the unit is from a blood relative, if the unit is HLA matched, or if the patient is immunocompromised
Dose
  Middle of canister: 2500 cGy or 25 Gy
  Lowest dose is 1500 cGy
Irradiated RBCs have an expiration time of 28 days

## Slide 20: Platelets (1 of 2)
Platelets
  Maintain vascular integrity
  Initiate formation of the platelet plug
  Stabilize the platelet plug by contributing to fibrin formation
Indications for use
  Chemotherapy or irradiation
  Posthematopoietic progenitor cell transplant
  Postoperative bleeding

## Slide 21: Platelets (2 of 2)
Platelet concentrate should contain at least 5.5 x 1010 platelets
One unit increases the platelet count by 5,000 to 10,000/μL
Pooled platelets
  Considered an “open system”; expires in 4 hours
Apheresis platelets
  Each unit must contain at least 3 × 1011 platelets
Leukoreduced platelets
  Prevent febrile reactions and HLA alloimmunization

## Slide 22: FFP
FFP and PF24 contain all coagulation factors (PF24 may have less factor VIII)
Indicated for:
  Patients needing factor II, V, X, or XI, when concentrates are not available
  Abnormal coagulation assays from mass transfusion
  Patients taking warfarin who are bleeding
  Replacement solution for therapeutic plasmapheresis
  Patients with liver disease with factor deficiencies
  Disseminated intravascular coagulation when fibrinogen is low (<100 mg/dL)

## Slide 23: FFP and PF24
Thaws in 30 to 45 minutes
Stored at 1° to 6° C
Transfuse within 24 hours
  If not transfused within 24 hours, relabel as “thawed plasma” and store at 1° to 6° C for up to 5 days
  Thawed plasma cannot be used to replace factor VIII
Should be ABO compatible
10 to 20 mL/kg is given for factor replacement

## Slide 24: Cryoprecipitated Antihemophilic Factor (CRYO) (1 of 3)
CRYO is the cold precipitate that forms when FFP is thawed at between 1° and 6° C
  CRYO is refrozen within 1 hour of preparation and stored at –18° C for up to 1 year
  Must demonstrate 150 mg of fibrinogen and 80 international units of factor VIII per unit

## Slide 25: Cryoprecipitated Antihemophilic Factor (CRYO) (2 of 3)
CRYO contains:
  von Willebrand factor
  Fibrinogen
  Factor VIII
  Fibronectin (for wound healing)
  Factor XIII
CRYO is a secondary treatment for hemophilia A and von Willebrand’s disease
  CRYO-reduced plasma
    Plasma left over after removing CRYO
    Can be refrozen within 24 hours of removing CRYO
    Treatment for thrombotic thrombocytopenic purpura
    Once thawed, store at 1° to 6° C for up to 5 days

## Slide 26: Cryoprecipitated Antihemophilic Factor (CRYO) (3 of 3)
Pooled cryoprecipitated AHF
  Pooled CRYO is kept at room temperature and administered within 4 hours (or within 6 hours if pooled by a “closed system”)
Fibrin sealant from CRYO
  CRYO is mixed with thrombin to control surface bleeding during surgery

## Slide 27: Apheresis Granulocytes
Contain leukocytes and platelets (some RBCs)
Each unit contains 1.0 x 1010 or more granulocytes
Kept at 20° to 24° C (without agitation) for up to 24 hours
Should be crossmatched because of RBC content
Must be irradiated
The use of apheresis granulocytes is rare

## Slide 28: Labeling
AABB Standards required each facility to convert to ISBT 128 by May 1, 2008
In addition to standard labeling:
  Irradiated components must have the name of the facility performing irradiation
  Pooled components must have the final volume listed and the name of the facility preparing the pool
  Autologous units must be labeled “For Autologous Use Only”

## Slide 29: Standard Labeling Requirements

## Slide 30: Storage
Refrigerators, freezers, and platelet incubators should have:
  Recording devices
  Audible alarms
  Alarm checks
  Emergency backup procedures
  Calibrated thermometers
Stored blood should be examined for hemolysis and abnormal color or clots

## Slide 31: Transportation
Whole blood or RBCs should be kept at 1°C to 10° C
Frozen units are shipped on dry ice
Platelets are maintained at 20°C to 24° C
Containers should be validated periodically