## Slide 1: Chapter 10
Blood Bank Automation for Transfusion Services

## Slide 2: Objectives (1 of 2)
Compare and contrast the forces driving the move to automation in the transfusion service
Identify the potential benefits and challenges associated with a change to automation
Define the characteristics of an ideal instrument for blood bank testing
Evaluate a vendor, base technology, and instrument for desired features

## Slide 3: Objectives (2 of 2)
Compare and contrast gel technology and solid-phase red cell adherence (SPRCA) assays
Compare and contrast the automated platforms available for a transfusion service
Select an automated platform for a transfusion service

## Slide 4: Benefits of Automation
Potential opportunities:
  Reduction in operating costs
  Redesign of work processes and support systems
  Increased productivity
  Enhanced total quality

## Slide 5: Challenges of Automation
Concerns among staff
  Job replacement
  Involvement in decision making
Cost justification issues
  Capital investment plan should be developed
Automation implementation issues
  Time investment
  Training and validation may require extra staff

## Slide 6: Important Criteria
Automation should meet the criteria for testing, sample handling, and data handling
Testing
Random-access mode
Simultaneous multiple analyses
Sample Handling
Clot detection
Bar code reader
Data Handling
Flexible software
Laboratory information system interface
Liquid detection
Closed tube sampling
Precise sampling
Extensive test menu
Automated reader
Accepts multiple samples
Precise pipetting
Flags discrepancies
Automatic patient updates to laboratory information system

## Slide 7: Selection of Automation
Vendor assessment
  Determine vendor’s experience with customer support, training, and service
Base technology assessment
  Investigate the reliability and accuracy of technology
Instrument assessment
  Consider the adaptability, availability, and cost-effectiveness of the automation to assess the instrument’s performance

## Slide 8: Automated Systems
Automated systems have been developed for:
  SPRCA assays
  Gel technology
  Microtiter plates
Instruments can perform:
  ABO and Rh testing
  Antibody detection and identification
  Crossmatching

## Slide 9: Hemagglutination Assays
Assays are performed on microplates using the same principles as in tube agglutination
Bar-coded samples and reagents are used
Plates are automatically read using a camera reader

## Slide 10: SPRCA Assays (1 of 2)
SPRCA assays are used for both indirect antiglobulin tests (IATs) and direct antiglobulin tests (DATs)
Microtiter wells have RBC membranes bound to the surface
  Patient antibodies (if present) will attach to the corresponding antigen covering the well
  Negative results form a button at the bottom of the well
  Capture-R Select® assay system immobilizes RBCs other than screen or panel cells

## Slide 11: SPRCA Assays (2 of 2)

## Slide 12: Solidscreen II (1 of 2)
Solid-phase assay that detects RBC antibodies in serum or plasma
Wells are precoated with protein A, which has a high affinity for the Fc portion of immunoglobulins
  Positive test: RBCs and antibody to immunoglobulin G (anti-IgG antibody) bind with protein A, forming a smooth monolayer
  Negative test: RBCs form a button at the bottom of the well

## Slide 13: Solidscreen II (2 of 2)

## Slide 14: Erytype S
Hemagglutination assay
ABO, D, and other RBC antigen testing
Monoclonal antisera are dried in microwells

## Slide 15: Automated SPRCA Systems
TANGO™ Infinity (Bio-Rad)
  Combines Erytype® S and Solidscreen® II
Capture™ system (Immucor)
  Microtiter plates accommodate SPRCA or hemagglutination testing

## Slide 16: Automated Gel Systems
ID-MTS™ Gel Test (Ortho Clinical Diagnostics)
  Automated instrument is ORTHO Vision®
  Microprocessor controlled unit
  Stand-alone or interfaced unit
  Uses gel cards and digital image processing

## Slide 17: ORTHO Vision® (1 of 3)
Components: computer, software, instrument, bar-code scanner, printer
Tests
  Agglutination: ABO and D, Rh phenotyping, IS crossmatching
  DAT: anti-IgG, anti-IgG-C3d antibodies
  IAT: antibody screening and identification, IAT crossmatching
Benefits
  Eliminates time-consuming processes
  Increases productivity
  Enhances process control

## Slide 18: ORTHO Vision® (2 of 3)
Carousel holds
  48 patient samples-outer ring
  Up to 18-33 reagents vials ( 3 mL vs 10mL vials)-inner ring
  2 diluents
Utilizes a high-resolution imaging system
  Reads both sides of the cassette
36-position-capacity card block
  24 positions at Room temp
  12 positions at 37˚C
Probe performs dilutions
Gel card gripper transports cards to centrifuge, imaging system, or service rack

## Slide 19: ORTHO Vision® (3 of 3)