## Slide 1: Histology & Cytology Chemical In-service:
Park Nicollet Health Services
Methodist Hospital Laboratory

## Slide 2: In-service Objectives
Learn about SDS’s
Understand NFPA chemical hazard labels as defined in SDS
Detect and explain signs and symptoms of exposure to formaldehyde, xylene, & alcohol
Understand how to limit exposure to hazardous chemicals, and how to relieve acute symptoms
Know who to notify or contact for help
Understand spill clean-up procedures
Understand the use of monitoring devices.
Learn proper disposal of chemicals (hazardous/non-hazardous) and storage requirements
Know where resources are located
Learn how to use the PAPR for chemical spill clean up.

## Slide 3: SDS - What is it?
Safety Data Sheets (SDS) contain specific information on the chemical properties and health hazards of the chemical you are using.
  All chemical containers must be labeled with chemical name, manufacturer name and address, and appropriate hazard warnings.
  Each SDS includes the hazard warning code for the four color coded hazard areas of the NFPA diamond.

## Slide 4: Safety Data Sheets (continued)
SDS’s for chemicals are written by the manufacturer of the chemical
The technical specialist obtains an SDS sheet from the manufacturer for each chemical used
  The SDS is sent to Environmental Services Safety Officer to be placed on Facets Damarco

## Slide 5: SDS-How to obtain
Contact Damarco (on-line SDS service)
  Phone: 1-877-451-6919
  Damarco web site: www.Damarco.com
  Facets Home Page (Left tree) under Medical Clicks
  Facets Home Page (Right tree) under Quick Clicks, Demarco Solutions
  Facets. Lab Page (bottom of page)

## Slide 6: NFPA Color-Coded Diamond
A commonly used hazard warning for chemicals is the National Fire Prevention Association (NFPA) diamond label. The diamond is divided into 4 sections, each having a designated color rating and a number.
Color Codes:
  Blue = health section
  Red = flammability rating
  Yellow = reactivity
  White = special symbols

## Slide 7: NFPA Chemical Hazard Label
The chemical manufacturer uses the NFPA
0 to 4 rating system to number the appropriate color coded hazard area
  4 = severe
  3 = serious
  2 = dangerous
  1 = minor
  0 = none

## Slide 8: Storage-Chemicals
Formalin, xylene, and alcohol are to be stored in a flammable liquid safety cabinet when not in use.
Excess chemicals are stored in the hazardous waste storage room.

## Slide 9: Formaldehyde facts:
Formalin is a colorless, aqueous solution containing not less than 37% of formaldehyde.
Formaldehyde & formalin should be stored in tightly closed containers at room temperature.
Most formalin used in the laboratory is a 10% formaldehyde which contains methanol.
  PEL (Permissible Exposure Limit) is 0.75 ppm/8hr day
  STEL(Short-Term Exposure Limit) is 2.0 ppm
  NFPA Rating: Health 2, Fire 2, Reactivity 0
Probable carcinogen (mainly nasopharyngeal cancers)

## Slide 10: Formaldehyde: Signs and Symptoms of Exposure
Exposure to concentrated liquid can cause serious corneal burns.
Can cause eczema and dermatitis.
Irritation of upper respiratory tract can occur.
Levels above 10ppm can cause severe reactions such as coughing and chest tightness.
Sensitization in some people when exposed to formaldehyde vapors, even at very low concentrations, leads to respiratory sensitization resulting in an allergic reaction similar to asthma. This can be triggered at any time, even in individuals who have worked with formaldehyde in the past with no apparent reaction.

## Slide 11: Xylene
Colorless, highly flammable liquid with aromatic, benzene-like odor.
Xylene is immiscible with water.
  PEL is 100 ppm/8 hr day
  STEL is 150 ppm/15min
  NFPA Rating: Health 2, Fire 3, Reactivity 0

## Slide 12: Xylene Health Hazards:
Inhalation may result in nausea, vomiting, headache, ringing of the ears, and severe breathing difficulties.
Chronic inhalation can cause headaches, loss of appetite, nervousness, and pale skin.
Repeated or prolonged skin contact may cause a skin rash.
Severe eye irritation may occur.
May affect CNS.
Small amounts aspirated into the lungs can produce severe hemorrhagic pneumonitis and severe pulmonary injury or death.

## Slide 13: Alcohol - Methanol, Ethanol, Isopropanol facts:
Colorless, flammable liquid
  PEL is 1000ppm/8hr day
  NFPA Rating: Health 1, Fire 3, Reactivity 0

## Slide 14: Alcohol Health Hazards:
Mild irritation, redness, cracking and drying of skin
Eye irritation, redness, blurred vision
Harmful vapor causes irritation of the respiratory tract.
High concentrations of vapor may cause CNS depression, with weakness, drowsiness, nausea, vomiting, diarrhea, fatigue.

## Slide 15: Limiting exposure to chemicals:
Make sure you have proper ventilation
PPE--use gloves and eye protection and apron (where splashing is possible)
Know safe spill cleanup procedures:
  C360: Spill Cleanup Procedure
  Posted by spill kits in histology processor room, cytology hood room and at the MOHS clinic by the #2 cryostat.
  Spill kits are checked quarterly for expiration date during the safety audit.

## Slide 16: Limiting Exposure-Work Practices
  No eating, drinking, gum chewing, applying cosmetics (including lip balm) in lab work areas.
  Wash all areas of exposed skin thoroughly prior to leaving work area.
  Never leave an instrument unattended that could present a health or safety accident.
  Any unsafe acts should be reported to supervisor

## Slide 17: Limiting Exposure-Housekeeping
  Clean all spills immediately and discard waste properly.
  Keep workspaces orderly and reasonably clear of unnecessary chemicals and equipment.
  Clean work area at the end of each shift.
  Keep all labels facing front so they are visible.
  Keep chemical containers clean, properly labeled, and return them to storage after use.

## Slide 18: Hazardous Waste-Definition
A chemical or substance, or mixture of chemicals or substances regulated by the Federal OSHA, MN OSHA, or Hennepin County Environmental Services.
Chemicals or substances determined by the commissioner that presents a significant risk to employee health and safety or imminent danger of death or serious physical harm to an employee are:
  Toxic (carcinogen, teratogen, mutagen, or a reproductive toxic agent).
  Corrosive
  Flammable
  Reactive

## Slide 19: Chemical Disposal
Recycling of 10% formalin, xylene and alcohol keeps need for disposal to a minimum.
Xylene and alcohols that cannot be recycled are discarded in a hazardous waste container.
Hazardous waste satellite containers are located at the site of generation and are emptied into the permanent waste containers.

## Slide 20: Chemical Waste – Storage Area
Bring chemical waste to the hazardous waste storage room for disposal. Follow the “Chemical Waste Definitions and Disposal” chart to determine how to dispose of the chemical. Types of waste are:
  Hazardous Waste-Flammable
  Other Chemical Waste
  Liquid-Non hazardous thimersol Waste
  Solid Mercury Waste
  Hazardous Waste-Trace metals

## Slide 21: Chemical Waste Definitions and Disposal
Waste Type | Chemicals | Disposal Method
Hazardous Waste | Still bottoms, paraffin waste, alcohols, IHC stainers, Alcohol and combined dyes, DAB, contaminated xylene, acetone, stains, Cytology density reagent waste from SurePath vacuum centrifugation step | Red and white hazardous waste label and includes: Description of the waste and the date that the drum is put into service (date that hazardous waste is first added to the drum) Disposed of by Clean Harbors
Non-Hazardous Waste – Thimersol (Mercury derivative) | Chemistry Electro-phoresis waste | 55 gallon drum labeled Non-hazardous waste – Mercury label (Thimersol) Disposed of by Clean Harbors
Other Chemicals | Chemical reagents in their original containers. An SDS must be provided. Do not label as Hazardous Waste | Place chemicals and SDS in plastic container labeled Chemical Disposal container. Disposal method determined by Clean Harbors staff. Disposed of by Clean Harbors
Solid Mercury Waste | Broken or unused Mercury devices | Place chemicals in plastic container labeled Mercury Disposal container Disposed of by Clean Harbors
Trace Metal Waste | Trace Metal waste from the Dako Artisan instrument or from manual special stain procedures. | Place trace metals in the 4 liter, container, with yellow Hazardous Waste label designated trace metals. Disposed of by Clean Harbors

## Slide 22: Histology Hazardous Waste: Generate, Collect and Transfer
Waste Type | Source | Satellite Container
Chemical reagent waste from Leica autostainer and manual run down | Alcohols contaminated with xylene, acid alcohol, ammonia water, and stains | Red flammable container located under the hood.
Still bottoms and paraffin waste | Waste from recycler and tissue processors | Red flammable container located in the processing room
Alcohol and combined dyes | Dako Artisan dyes, Artisan alcohols, acetone (Pneumo), methyl alcohol (BM), solutions from manual staining | Combined dye container located in the special stains area.
Trace Metals | Dako Artisan trace metal waste, uranyl nitrate, heavy metal solutions from manual stains | Plastic gallon container label Trace metals
IHC Chromogen | Leica Bond and Dako Autostainer in IHC area. | Separate container attached to each stainer

## Slide 23
Product name | Where waste is generated | Disposal
Acetone | Cytology – for removal of tape coverslip | Hazardous waste barrel
Cytoseal-60 – mounting media | No waste usually generated, used for coverslipping slides with glass coverslips | Hazardous waste barrel
Gill III Hematoxylin – Surgipath & Richard Allen Heme II | Leica Auto-Stainer | Hazardous waste barrel
EA-50 – Surgipath & Richard Allen Eosin | Leica Auto-Stainer | Hazardous waste barrel
Orange-G (OG) - Surgipath | Leica Auto-Stainer | Hazardous waste barrel
Xylene | Manual staining line and last step prior to coverslipping for Liquid Paps | *Recycle or Hazardous waste barrel
Density Reagent – TriPath | Vacuum waste bottle from centrifugation step for SurePath Pap processing | Hazardous waste barrel
*Recycle alcohol and Xylene per procedure.
Hazardous waste & non-hazardous waste barrels are located in the flammable storage room – hallway between Histology and Surgery. Find key in Histology (or call Security x35101 if needed).
Cytology Hazardous Waste
Chemical Disposal Chart

## Slide 24: Employee Responsibility Handling and Storage
Keep containers closed when not in use.
Separate incompatible waste.
Visually inspect the satellite containers/ containers at site of generation daily.
Ensure that the containers are properly labeled.
Document the volume (in gallons) of waste that is being disposed.
Correct unsafe situations immediately.
Know where to find universal spill procedures.

## Slide 25: Hazardous Waste Storage Drum
For hazardous waste
  Labeled with a red and white hazardous waste label and includes:
    Description of the waste and the date that the drum is put into service (date that hazardous waste is first added to the drum)
  Hazardous waste drum must be clamped with the grounding wire (flammable liquids)
  Record the amount of chemical discarded in the hazardous waste drum in the “Hazardous Waste Procedure and Log Book” under the Hazardous waste tab.
    Record the amount dumped into the drum in gallons

## Slide 26: Flammable Storage Room - PPE
A chemical resistant apron and mask are available for use in the Flammable Storage Room when disposing chemicals.

## Slide 27: Non-Hazardous Waste Storage Drum
55 gallon drum for Non-Hazardous waste:
  Mercury (Thimersol)
Label with a Non-Hazardous mercury waste label and include:
  Date the drum is put into use.
  The barrel will be labeled by Clean Harbors with the appropriate Waste Label.
  Clean Harbors only, is authorized to add mercury waste to the drum.
  Clean Harbors checks the levels of the drum weekly and does not keep a log for this drum.

## Slide 28: Discarding Waste
Double check to verify that the amount to be added to drum does not exceed its capacity.
Remove cap from drum and attach the appropriate funnel
  yellow for hazardous waste
  Black with red cover for Non-Hazardous waste –Mercury (Thimersol)
Dispose of chemicals by pouring slowly so as to not splash.
Remove funnel and screw lid back on.
If drum overflows, clean up with towels and dispose in designated bucket. The towels are now considered hazardous waste.

## Slide 29: Chemical Waste Disposal Containers
The Chemical Waste Disposal Container (plastic container) is located in the hazardous waste storage room.
  Chemicals must be in their original containers
  An SDS must be provided
  DO NOT label as hazardous waste
  Record discarded chemicals into the “Hazardous Waste Log Book” under the Other Chemical tab
  Clean Harbors will determine which chemicals are hazardous and dispose of them appropriately.

## Slide 30: Solid Mercury Waste Containers
Solid Mercury Disposal Container (Plastic container) in the hazardous waste storage room
  For disposal of broken or unused mercury devices
  Log chemicals into the “Hazardous Waste Procedure and Log Book” under the Mercury Waste tab.

## Slide 31: Trace Metal Container
Satellite Trace metal containers are stored by the Dako Artisan instrument in Histology.
  Satellite Accumulation label:
    Label container with a red and white hazardous waste label. Write on the label the date you first add waste to the container and a description of the waste. Write the date the container is filled on the label This is referred to as the “accumulation start date”. You have 3 days from the accumulation start date to move the container to the explosion room.
  Transfer filled 4 liter containers (1 gallon) to the explosion room.
  Log discarded chemicals into the “Hazardous Waste Procedure and Log Book” under the Trace Metal Waste tab

## Slide 32: Hazardous Waste Storage – Weekly Inspection Procedures
Weekly inspections of hazardous waste are performed by Clean Harbors because of the potential effect of these materials.
Inspections are in compliance with Minnesota hazardous waste regulations.

## Slide 33: Hazardous Waste – Satellite Accumulation Procedures
Allows a hazardous waste generator (our lab) to slowly accumulate at the site of waste generation.
Satellite-accumulation containers that are under direct control of an operator and are visually inspected daily by that operator do not need documented weekly inspections during waste accumulation.
Satellite accumulation containers that are located away from the operator during waste accumulation, or that have been filled and moved into the
permanent storage area must be inspected weekly. These inspections must be
documented.
Attach an Accumulation label to the satellite container if you are NOT dumping into a Drum (I.e. trace metal waste)
  Record the contents of the container.
  Record the date you first add waste
  Record the date you fill (accumulation start date) the container.
  The “accumulation start date” is the date the container is full.

## Slide 34
You have 3 days from the accumulation start date to move the container to the permanent storage area (hazardous waste disposal room)
Clean Harbors has 90 days to move the container of waste off site.
Clean Harbors is responsible for the shipping.
If waste is shipped more than 200 miles from the generating facility (Methodist Hospital), you have 270 days to move waste off site.
Accumulation Storage & Shipping

## Slide 35: Hazardous Waste – Shipping/Manifest and Land Disposal
Clean Harbors is responsible for the shipping and completion of manifests.
Clean Harbors will supply the Land Disposal Restriction form with the manifest for disposal.
Contact Clean Harbors on-site at #3-5116 with questions or concerns with hazardous waste and spills.

## Slide 36: Chemical Spill Clean-Up
Refer to the Safety section of C360
SMALL SPILL OR LEAK (less than 500ml)
  Isolate spill area and restrict entry.
  Immediately don PPE, and bring spill response Pak to the spill area.
  Place the Universal Sorbent Pads, and/or the Hazorb Pint or Lab pillows (depending on the size of the spill) on top and around the spill. This helps contain the liquid. Pick up the saturated pads/pillows and place the pads in the enclosed yellow disposal bags. Secure the bags with ties supplied and label according to content. Take bag labeled with type of hazardous waste to the explosion room to await disposal by Clean Harbors.

## Slide 37: Chemical Spill Clean-Up (continued)
LARGE SPILLS (500 ml/0.5 liter or greater)
  Isolate hazard area and restrict entry.
  Notify supervisor, and call Safety and Security at ext. 35101
  Obtain and put on a chemical PAPR.
  With the appropriate PPE in place bring the Spill Response Pak to the spill site. Place the universal sorbent pads, and/or lab pillows (depending on the size of the spill) on top and around the spill. This helps to contain the liquid. Pick up the saturated pads/pillows and place them in the enclosed yellow disposal bags. Secure the bags with the twist ties supplied and label contents. Take the bag to the explosion room to await disposal by Clean Harbors.

## Slide 38: First Aid - What to do if you are exposed:
  For inhalation: move to fresh air immediately.
  For a splash or spill on skin or in eye(s):
    Remove contaminated clothing ASAP.
    Flush area continuously for at least 15 minutes under a safety shower, faucet, or eye wash.
    Wash chemical off with soap.
    Do not use neutralizing agents, cream, lotions, or salves on the skin.
  You MUST report the exposure to EOHS (Employee Occupational Heath Services) within 24 hours at 952-993-5080.
  If you have a serious or life-threatening exposure, go immediately to the ER, bringing a copy of the SDS with you if possible.

## Slide 39: Location of Safety Shower and Eye Washes
Safety Shower
  Located in the H&E staining area
  Shower is checked weekly by Histology.
Eye Washes
  Located in the clean sink in the Histology special stain area and is close the grossing area
  Located by the freezer in the Histology cutting area
  Located in the cytology prep lab
  Eye washes are checked weekly by Histology/Cytology staff, including cleaning of the covers with 10% bleach solution
Note: Procedure for checking safety shower and eye washes can be found in the safety section of C360.

## Slide 40: Chemical Monitoring
Levels of formaldehyde and xylene are monitored for Histotechs and Cytology Prep staff whenever:
  Problems with the levels are suspected
  A new instrument is acquired
  A new employee is hired
  An employee’s exposure is above the action level; the monitoring is repeated every 6 months until the monitoring falls below the STEL or action level
Refer to “Employee Monitoring for Xylene/Formaldehyde Exposure” in the Pathology/Histology section of C360.
Chemical Hygiene Plan is located in the Safety section of C360.

## Slide 41: EMERGENCY CONTACTS
Safety and Security: 3-5101 or 113
Employee Occupational Health Services: 3-5080
Clean Harbors: 1-800-483-3718
Damarco SDS service: 877-451-6919

## Slide 42: Procedure Resources
Compliance 360
  Pathology / Histology section
  Safety section

## Slide 43: Resources
The following documents related to this topic are available to all employees:
  Chemical Hygiene Plan--describes policies, procedures, equipment, PPE, and work practices that are capable of protecting employees from the health hazards presented by hazardous chemicals used in laboratories. It is located in the Laboratory Safety Manual.
  Occupational Exposure to Hazardous Chemicals In the Laboratory (OSHA Standard)
  SDS—Safety Data Sheets provide information about a specific chemical, including general information, health data, symptoms of exposure, preventive measures, first aid measures, and storage information.

## Slide 44: Quiz time!