## Slide 1: 2018 Histology & Cytology Chemical In-service:
Park Nicollet Health Services
Methodist Hospital Laboratory

## Slide 2: In-service Objectives
Learn about SDS’s
Understand NFPA and GHS chemical hazard labels as defined in SDS
Detect and explain signs and symptoms of exposure to formaldehyde, xylene, & alcohol
Understand how to limit exposure to hazardous chemicals, and how to relieve acute symptoms
Know who to notify or contact for help
Understand spill clean-up procedures
Understand the use of monitoring devices.
Learn proper disposal of chemicals (hazardous/non-hazardous) and storage requirements
Know where resources are located
Learn how to use the PAPR for chemical spill clean up.

## Slide 3: SDS - What is it?
Safety Data Sheets (SDS) contain specific information on the chemical properties and health hazards of the chemical you are using.
  All chemical containers must be labeled with chemical name, manufacturer name and address, and appropriate hazard warnings.
  Each SDS includes the hazard warning code for the four color coded hazard areas of the NFPA diamond or the GHS pictogram/signal word.

## Slide 4: Safety Data Sheets (continued)
SDS’s for chemicals are written by the manufacturer of the chemical
The technical specialist obtains an SDS sheet from the manufacturer for each chemical used
  The SDS is sent to EOHS Safety Officer to be placed on Facets Damarco

## Slide 5: SDS-How to obtain
Contact Damarco (on-line SDS service)
  Phone: 1-877-451-6919
  Damarco web site: www.Damarco.com
  Facets Home Page (Left tree) under Medical Clicks and then Safety Data Sheets
  Facets Home Page under EOHS department, Quick Clicks, Damarco Solutions (SDS)
  Facets, Lab Home Page (bottom of page)

## Slide 6: NFPA Color-Coded Diamond
A commonly used hazard warning for chemicals is the National Fire Prevention Association (NFPA) diamond label. The diamond is divided into 4 sections, each having a designated color rating and a number.
Color Codes:
  Blue = health section
  Red = flammability rating
  Yellow = reactivity
  White = special symbols

## Slide 7: NFPA Chemical Hazard Rating
The chemical manufacturer uses the NFPA
0 to 4 rating system to number the appropriate color coded hazard area
  4 = severe
  3 = serious
  2 = dangerous
  1 = minor
  0 = none

## Slide 8: GHS Secondary Label
A commonly used hazard warning for chemicals in the OSHA Globally Harmonized System of Classification of Chemicals (GHS). This system uses pictograms and signal words to classify chemicals.

## Slide 9: GHS Chemical Hazard Rating

## Slide 10: Storage-Chemicals
Xylene and alcohol are to be stored in a flammable liquid safety cabinet when not in use.
Up to one gallon of flammable liquid may be stored outside of a fire-resistant safety cabinet per 100 ft2 of defined space.

## Slide 11: Formaldehyde facts(see SDS for complete data):
Formalin is a colorless, aqueous solution containing not less than 37% formaldehyde.
Formaldehyde & formalin should be stored in tightly closed containers at room temperature.
Most formalin used in the laboratory is a 10% formaldehyde solution which contains methanol.
  PEL (Permissible Exposure Limit) is 0.75 ppm/8hr day
  STEL(Short-Term Exposure Limit) is 2.0 ppm
  NFPA Rating: Health 3, Fire 2, Reactivity 0
  GHS Rating: Signal Word = DANGER; Pictograms =
  Known carcinogen

## Slide 12: Formaldehyde: Signs and Symptoms of Exposure
Exposure to concentrated liquid can cause serious corneal burns.
Can cause eczema and dermatitis.
Irritation of upper respiratory tract can occur.
Levels above 10ppm can cause severe reactions such as coughing and chest tightness.
Sensitization in some people when exposed to formaldehyde vapors, even at very low concentrations, leads to respiratory sensitization resulting in an allergic reaction similar to asthma. This can be triggered at any time, even in individuals who have worked with formaldehyde in the past with no apparent reaction.

## Slide 13: Xylene facts(see SDS for complete data):
Colorless, highly flammable liquid with aromatic, benzene-like odor.
Xylene is immiscible with water.
  PEL is 100 ppm/8 hr day
  STEL is 150 ppm/15min
  NFPA Rating: Health 3, Fire 3, Reactivity 0
  GHS Rating: Signal Word = DANGER; Pictograms =
  Suspect carcinogen

## Slide 14: Xylene Health Hazards:
Inhalation may result in nausea, vomiting, headache, ringing of the ears, and severe breathing difficulties.
Chronic inhalation can cause headaches, loss of appetite, nervousness, and pale skin.
Repeated or prolonged skin contact may cause a skin rash.
Severe eye irritation may occur.
May affect CNS.
Small amounts aspirated into the lungs can produce severe hemorrhagic pneumonitis and severe pulmonary injury or death.

## Slide 15: Methanol facts(see SDS for complete data):
Colorless, flammable liquid
  PEL is 200ppm/8hr day
  NFPA Rating: Health 3, Fire 3, Reactivity 0
  GHS Rating: Signal Word = DANGER; Pictograms =

## Slide 16: Ethanol facts(see SDS for complete data):
Colorless, flammable liquid
  PEL is 1000ppm/8hr day
  NFPA Rating: Health 1, Fire 3, Reactivity 0
  GHS Rating: Signal Word = DANGER; Pictograms =

## Slide 17: Isopropanol facts(see SDS for complete data):
Colorless, flammable liquid
  PEL is 400ppm/8hr day
  NFPA Rating: Health 2, Fire 3, Reactivity 0
  GHS Rating: Signal Word = DANGER; Pictograms =

## Slide 18: Alcohol Health Hazards:
Mild irritation, redness, cracking and drying of skin
Eye irritation, redness, blurred vision
Harmful vapor causes irritation of the respiratory tract.
High concentrations of vapor may cause CNS depression, with weakness, drowsiness, nausea, vomiting, diarrhea, fatigue.

## Slide 19: Limiting exposure to chemicals:
Make sure you have proper ventilation
PPE--use gloves and eye protection and apron (where splashing is possible)
Know safe spill cleanup procedures:
  C360: Refer to Lab Spill Cleanup Procedure
  Spill kits are checked quarterly, during the Safety Audit, for expiration date and to ensure all components are intact and usable.

## Slide 20: Limiting Exposure-Work Practices
  No eating, drinking, gum chewing, applying cosmetics (including lip balm) in lab work areas.
  Wash all areas of exposed skin thoroughly prior to leaving work area.
  Never leave an instrument unattended that could present a health or safety accident.
  Any unsafe acts should be reported to supervisor

## Slide 21: Limiting Exposure-Housekeeping
  Clean all spills immediately and discard waste properly.
  Keep work spaces orderly and reasonably clear of unnecessary chemicals and equipment.
  Clean work area at the end of each shift.
  Keep all labels facing front so they are visible.
  Keep chemical containers clean, properly labeled, and return them to storage after use.

## Slide 22: Hazardous Waste-Definition
A chemical or substance, or mixture of chemicals or substances regulated by the Federal OSHA, MN OSHA, or Hennepin County Environmental Services.
Chemicals or substances determined by the commissioner that presents a significant risk to employee health and safety or imminent danger of death or serious physical harm to an employee are:
  Toxic (carcinogen, teratogen, mutagen, or a reproductive toxic agent).
  Corrosive
  Flammable
  Reactive

## Slide 23: Chemical Disposal
Recycling of 10% formalin, xylene and alcohol keeps need for disposal to a minimum.
Xylene and alcohols that cannot be recycled are discarded in a hazardous waste container.
Hazardous waste satellite containers are located at the site of generation and are transported to the temporary hazardous chemical waste storage area in histology.

## Slide 24: Hazardous Chemical Waste – Storage Area
Bring chemical waste to the hazardous waste storage area for disposal. Follow the “Chemical Waste Definitions and Disposal” chart (see next slide) to determine how to dispose of the chemical. Types of waste are:
  Hazardous Waste-Flammable
  Other Chemical Waste
  Hazardous Waste-Trace metals

## Slide 25: Chemical Waste Definitions and Disposal
Waste Type | Chemicals | Disposal Method
Hazardous Waste | Still bottoms, paraffin waste, alcohols, IHC stainers, Alcohol and combined dyes, DAB, contaminated xylene, acetone, stains, Cytology density reagent waste from SurePath vacuum centrifugation step | Place waste in carboys labeled for hazardous waste. Disposed of by Clean Harbors
Non-Hazardous Waste – Thimersol (Mercury derivative) | None currently | Disposed of by Clean Harbors, if future needs
Other Chemicals | Chemical reagents in their original containers. An SDS must be provided. Do not label as Hazardous Waste | Place chemicals and SDS in plastic container labeled Chemical(s) for Evaluation bin. Disposal method determined by Clean Harbors staff. Disposed of by Clean Harbors
Solid Mercury Waste | Broken or unused Mercury devices | Place chemicals in plastic container labeled Mercury Disposal container Disposed of by Clean Harbors
Trace Metal Waste | Trace Metal waste from the Dako Artisan instrument or from manual special stain procedures. | Place trace metals in the 4 liter, container, with yellow Hazardous Waste label designated trace metals. Disposed of by Clean Harbors

## Slide 26: Histology Hazardous Waste: Generate, Collect and Transfer
Waste Type | Source | Satellite Container
Chemical reagent waste from Leica autostainer and manual run down | Alcohols contaminated with xylene, acid alcohol, ammonia water, and stains | Local Satellite Container
Still bottoms and paraffin waste | Waste from recycler and tissue processors | Flammable container located in the processing room
Alcohol and combined dyes | Dako Artisan dyes, Artisan alcohols, acetone (Pneumo), methyl alcohol (BM), solutions from manual staining | Combined dye container located in the special stains area.
Trace Metals | Dako Artisan trace metal waste, uranyl nitrate, heavy metal solutions from manual stains | Plastic gallon container label Trace metals
IHC Chromogen | Leica Bond and Dako Autostainer in IHC area. | Separate container attached to each stainer

## Slide 27
Product name | Where waste is generated | Disposal
Acetone | Cytology – for removal of tape coverslip | Hazardous waste carboy
Cytoseal-60 – mounting media | No waste usually generated, used for coverslipping slides with glass coverslips | Hazardous waste carboy
Gill III Hematoxylin – Surgipath & Richard Allen Heme II | Leica Multi-Stainer | Hazardous waste carboy
EA-50 – Surgipath & Richard Allen Eosin | Leica Multi-Stainer | Hazardous waste carboy
Orange-G (OG) - Surgipath | Leica Multi-Stainer | Hazardous waste carboy
Xylene | Manual staining line and last step prior to coverslipping for Liquid Paps | *Recycle or Hazardous waste carboy
Density Reagent – TriPath | Vacuum waste bottle from centrifugation step for SurePath Pap processing | Hazardous waste carboy
*Recycle alcohol and Xylene per procedure.
Hazardous waste & non-hazardous waste carboys are located in the permanent hazardous chemical storage room – hallway between Histology and Surgery. Find key in Histology (or call Security x35101 if needed).
Cytology Hazardous Waste
Chemical Disposal Chart

## Slide 28: Employee Responsibility Handling and Storage
Keep containers closed when not in use.
Separate incompatible waste.
Visually inspect the satellite containers/ containers at site of generation daily.
Ensure that the containers are properly labeled.
Correct unsafe situations immediately.
Know where to find universal spill procedures.

## Slide 29: Chemicals for Evaluation Bin
The Chemicals for Evaluation Bin (plastic container) is located in the permanent hazardous waste chemical storage room.
  Chemicals must be in their original containers
  An SDS must be provided
  DO NOT label as hazardous waste
  Clean Harbors will determine which chemicals are hazardous and dispose of them appropriately.

## Slide 30: Chemicals for Evaluation Bin Continued
  For disposal instructions of broken mercury devices contact Clean Harbors at 3-5116
  Place intact mercury devices into the Chemicals for Evaluation Bin

## Slide 31: Trace Metal Container
Satellite Trace metal containers are stored by the Dako Artisan instrument in Histology.
  Satellite Accumulation label:
    Label container with a red and white hazardous waste label. Write on the label the date you first add waste to the container and a description of the waste. Write the date the container is filled on the label. This is referred to as the “accumulation start date”. You have 3 days from the accumulation start date to move the container to the permanent hazardous chemical waste storage room.
  Transfer filled 1 gallon containers to the temporary hazardous chemical waste storage room located in histology.

## Slide 32: Hazardous Chemical Waste Storage Room– Weekly Inspection Procedures
Weekly inspections of hazardous waste are performed by Clean Harbors because of the potential effect of these materials.
Inspections are in compliance with Minnesota hazardous waste regulations.

## Slide 33: Hazardous Waste – Satellite Accumulation Procedures
Allows a hazardous waste generator (PN lab) to slowly accumulate at the site of waste generation.
Satellite accumulation containers that are under direct control of an operator and are visually inspected daily by that operator do not need documented weekly inspections during waste accumulation.
Satellite accumulation containers that are located away from the operator during waste accumulation, or that have been filled and moved into the
permanent hazardous chemical waste storage area must be inspected weekly. These inspections must be documented.
Attach an Accumulation label to the satellite container if you are NOT dumping into a carboy (I.e. trace metal waste)
  Record the contents of the container.
  Record the date you first add waste
  Record the date you fill (accumulation start date) the container.
  The “accumulation start date” is the date the container is full.

## Slide 34
You have 3 days from the accumulation start date to move the container to the permanent hazardous chemical waste storage area
Clean Harbors has 90 days to move the container of waste off site.
Clean Harbors is responsible for the shipping.
If waste is shipped more than 200 miles from the generating facility (Methodist Hospital), you have 270 days to move waste off site.
Accumulation Storage & Shipping

## Slide 35: Hazardous Waste – Shipping/Manifest and Land Disposal
Clean Harbors is responsible for the shipping and completion of manifests.
Clean Harbors will supply the Land Disposal Restriction form with the manifest for disposal.
Contact Clean Harbors on-site at #3-5116 with questions or concerns with hazardous waste and spills.

## Slide 36: Chemical Spill Clean-Up
  For Trained Chemical PAPR Team Members:
    Upon evaluation of initial spill, if any symptoms occur evacuate area, notify supervisor, and call Safety and Security at ext. 3-5101
    If further evaluation of spill is needed or trained personnel determine clean up is feasible, obtain and put on a chemical PAPR from the EC along with other necessary PPE.
    With the appropriate PPE in place bring the appropriate Spill Kit to the spill site. Place the absorbent material on top and around the spill. This helps to contain the liquid. Place the saturated absorbent material in the enclosed disposal bags. Secure the bags with the twist ties supplied and label contents. Notify Clean Harbors at 3-5116 and place bag in the permanent hazardous chemical waste storage room to await disposal by Clean Harbors.
    NOTE: Check Spill Kit expiration date as part of quarterly Lab Safety Audit. If no expiration date is present, make sure each kit component remains intact and useable.

## Slide 37: Chemical Spill Clean-Up (continued)
Refer to the Lab Spill Clean Up Policy in C360
Routine SPILL OR LEAK
  Minimal exposure symptoms
  Low impact agent
  Clean up may be managed with existing Lab resources
  No Lab occupant safety/health issues
  No evacuation needed
  No indoor air quality compromised

## Slide 38: Chemical Spill Clean-Up (continued)
Urgent SPILL OR LEAK
  Response is Required
  There is no reported physical or health endangerment to lab occupants
  Manageable exposure symptoms
  Medium impact agent
  Clean up may need additional internal resources
  Manageable Lab occupant safety/health issues
  Lab evacuation may be temporarily needed
  Indoor air quality may be impacted

## Slide 39: Chemical Spill Clean-Up (continued)
Emergency SPILL or LEAK
  The situation is immediately dangerous to the life, health or personal safety of occupants
  Intense exposure symptoms.
  High impact agent
  Clean up may need external resources (Clean Harbors, Fire HazMat team)
  Immediate team member issues
  Evacuation required
  Indoor air quality is hazardous or impacting personal health or comfort

## Slide 40: First Aid - What to do if you are exposed:
  For inhalation: move to fresh air immediately.
  For a splash or spill on skin or in eye(s):
    Remove contaminated clothing ASAP.
    Flush area continuously for at least 15 minutes under a safety shower, faucet, or eye wash.
    Wash chemical off with soap.
    Do not use neutralizing agents, cream, lotions, or salves on the skin.
  Employee MUST report the exposure to EOHS (Employee Occupational Heath Services) within 24 hours at 952-993-5080.
  If you have a serious or life-threatening exposure, go immediately to the EC, bringing a copy of the SDS with you, if possible.

## Slide 41: Location of Safety Shower and Eye Washes
Safety Shower
  Located by the rear door of the AP lab.
  Shower is checked weekly by Histology.
Eye Washes
  Located in the clean sink by the front and rear doors of the AP lab.
  Eye washes are checked weekly by Histology/Cytology staff.
Note: Procedure for checking safety shower and eye washes can be found in the safety section of C360.

## Slide 42: Chemical Monitoring
Levels of formaldehyde and xylene are monitored for Histotechs and Cytology Prep staff whenever:
  Problems with the levels are suspected
  A new instrument is acquired
  A new employee is hired
  An employee’s exposure is above the action level; the monitoring is repeated every 6 months until the monitoring falls below the STEL or action level
Refer to Formaldehyde and Xylene Monitoring in the Pathology/Histology section of C360.
Chemical Hygiene Plan is located in the Safety section of C360.

## Slide 43: EMERGENCY CONTACTS
Safety and Security: 3-5101 or 111
Employee Occupational Health Services: 3-5080
Clean Harbors: 952-993-5116 (on-site rep, days)
1-800-645-8265 (after hours)
Damarco SDS service: 877-451-6919

## Slide 44: Procedure Resources
Compliance 360
  Pathology / Histology section
  Safety section

## Slide 45: Resources
The following documents related to this topic are available to all employees:
  Chemical Hygiene Plan--describes policies, procedures, equipment, PPE, and work practices that are capable of protecting employees from the health hazards presented by hazardous chemicals used in laboratories. It is located in the Laboratory Safety Manual.
  Occupational Exposure to Hazardous Chemicals In the Laboratory (OSHA Standard)
  SDS—Safety Data Sheets provide information about a specific chemical, including general information, health data, symptoms of exposure, preventive measures, first aid measures, and storage information.

## Slide 46: Quiz time!