## Slide 1: Scenes from an assessment visit
This scenario mimics an actual assessment visit and describes actual findings by assessors.

## Slide 2
How many non-compliances to OLA Standards can you find?
How many inappropriate behavior from the assessors can you find?

## Slide 3: Act One: Lab Tour
An assessment team is visiting a community hospital laboratory whose scope of testing includes chemistry, POCT, hematology and transfusion medicine. The laboratory does not have an laboratory director and medical director on site – it is managed remotely by a larger organization – OMNI Hospital. After the opening meeting, the team is taken on a tour of the laboratory. While touring, they note that a staff member leaves the bench from uncapping tubes to answer the phone but doesn’t remove his gloves and another staff member removes lip balm from her lab coat pocket and applies it while at the bench.

## Slide 4: The Answers

## Slide 5: Act One: Lab Tour
An assessment team is visiting a community hospital laboratory whose scope of testing includes chemistry, POCT, hematology and transfusion medicine. The laboratory does not have an laboratory director and medical director on site – it is managed remotely by a larger organization – OMNI Hospital. The opening meeting the team is taken on a tour of the laboratory. While touring, they note that a staff member leaves the bench from uncapping tubes to answer the phone but doesn’t remove his gloves and another staff member removes lip balm from her lab coat pocket and applies it while at the bench.

## Slide 6
“a staff member leaves the bench from uncapping tubes to answer the phone but doesn’t remove his gloves”
when answering the phone it is important to remove your gloves in order not to contaminate the phone. Phones are placed at a very close proximity to people’s eyes, nose, mouth and face. Precautions should be taken when answering them. The following listed items are from the OLA requirements and the other from the IHL Safety manual.
III.10 There shall be effective separation between adjacent laboratory sections in which there are incompatible activities, such as to control noise, contain hazards, and prevent cross-contamination or to maintain sterility. [122]
This means that there should be a separation between analytical and clerical activities.
The IHL SAF-III – BIOHAZARD RISK ASSESSMENT AND PERSONAL PROTECTIVE EQUIPMENT GUIDELINES
The above document indicates that gloves should not be worn when answering phones. The lab could also be cited for not following the procedure as written.

## Slide 7
“staff member removes lip balm from her lab coat pocket and applies it while at the bench“
It is a safety hazard to apply cosmetics in a biohazardous area. This is in violation of the following OLA requirement and the IHL safety manual policy.
X.E.4 Application of cosmetics (other than hand creams) and the handling of contact lenses shall be prohibited in laboratory work areas.[410]
Lip balm in this case is considered cosmetics and should not be used in laboratory work areas.
IHL-SAF– I LABORATORY SAFETY PRACTICES – States “Do not eat, drink or smoke in the laboratory; apply lip salve or cosmetics; insert fingers, pencils, etc., in the mouth; lick envelopes or labels.
The above document is an IHL document which clearly states that lip salve or cosmetics should not be apply within the lab. The lab could also be cited for not following the procedure as written.

## Slide 8: Act Two: POCT Performed in the Emergency Room
After the tour the assessment team splits up to conduct their assigned technical assessments. Susie, the assessor assigned to point-of-care heads off to the emergency department with the POCT technologist to view the area. The POCT technologist informs Susie that they only do POCT glucose testing. Susie notes that there are initial training records from five years ago but there are no on-going training records. Susie then reviews recorded POCT glucose results. Several results are missing the reference interval. She proceeds to check reagents in the supply cupboard and a very helpful nurse points out the fecal occult blood kits Dr. Dick brought in from his office so nursing staff could test for that in the emergency room, too.

## Slide 9: The Answers

## Slide 10: Act Two: POCT Performed in the Emergency Room
After the tour the assessment team splits up to conduct their assigned technical assessments. Susie, the assessor assigned to point-of-care heads off to the emergency department with the POCT technologist to view the area. The POCT technologist informs Susie that they only do POCT glucose testing. Susie notes that there are initial training records from five years ago but there are no on-going training records. Susie then reviews recorded POCT glucose results. Several results are missing the reference interval. She proceeds to check reagents in the supply cupboard and a very helpful nurse points out the fecal occult blood kits Dr. Dick brought in from his office so nursing staff could test for that in the emergency room, too.

## Slide 11
“no on-going training records“
XI.B.13 Records of trainers, trained operators, retraining and date of
completion/certifications for point-of-care testing shall be maintained.
The OLA requirement above clearly indicates retaining records must be maintained with the date of completion.
IHL-POC-IV Point of Care Recertification Program & IHL-POC-I Point of Care Testing Roles, Responsibilities and Scope
The above IHL documents clearly states when retraining is warranted, records must be maintained.
Any training or re-training requires documentation, this is how we can prove that the staff performing the POCT is competent.

## Slide 12
“missing the reference range“
XI.J.3 The patient record shall include the point-of-care test result in clearly defined units, the date and time the test was performed, and the reference interval for the test.[611]
The above OLA requirement indicates that the reference interval for the POCT test must be clearly defined.
IHL-POC-IV Point of Care Recertification Program & IHL-POC-I Point of Care Testing Roles, Responsibilities and Scope
The above IHL documents states when reporting a POCT result it must also be accompanied by the reference interval.
Any POCT results must be documented along with the relevant reference range.

## Slide 13
“the fecal occult blood kits “
When a department or physician decides that they want to perform point of care testing, it must be approved by the appointed POCT committee, validation must be performed and documented, processes and procedures must be created and documented, training must be developed, implemented and documented. Not doing any of these steps is in violation of MANY OLA requirements. There are too many requirement to list. The IHL also has strict guidelines, processes, procedures, training and documentation in place to ensure quality results are being yield.
Any POCT testing must be approved by the management of the laboratory and hospital. No department can begin testing until all the checks and balances are in place.

## Slide 14: Act Three: Transfusion Medicine Practices
Red, the transfusion medicine assessor goes to the operating room to look at the blood warmers located there. She notes that the are not monitored for temperature and to ensure they meet applicable safety standards. Back in the laboratory, while reviewing transfusion medicine instructions, she notes that several printed procedures related to antibody identification, dealing with transfusion reactions and performing crossmatches have sections blacked out with a marker. When Red asks the bench technologist why, she is told “OMNI Hospital lab managers maintain our procedures but won’t alter them to match our practices, so we just cross out whatever isn’t done here, on our printed copies”. At the end of the day team meeting Red shares this observation with the rest of the team and discovers this practice of making authorized changes to printed procedures is also carried out in chemistry and hematology.

## Slide 15: The Answers

## Slide 16: Act Three: Transfusion Medicine Practices
Red, the transfusion medicine assessor goes to the operating room to look at the blood warmers located there. She notes that the are not monitored for temperature and to ensure they meet applicable safety standards. Back in the laboratory, while reviewing transfusion medicine instructions, she notes that several printed procedures related to antibody identification, dealing with transfusion reactions and performing crossmatches have sections blacked out with a marker. When Red asks the bench technologist why, she is told “OMNI Hospital lab managers maintain our procedures but won’t alter them to match our practices, so we just cross out whatever isn’t done here, on our printed copies”. At the end of the day team meeting Red shares this observation with the rest of the team and discovers this practice of making unauthorized changes to printed procedures is also carried out in chemistry and hematology.

## Slide 17
“blood warmers - not monitored for temperature and to ensure they meet applicable safety standards“
IV.14 Maintenance of laboratory equipment shall ensure proper performance and assure accurate and reliable test performance.[159]
TM138 All equipment used to warm blood components shall include
a temperature sensing device and an audible alarm system. The temperature during use shall be documented. Blood warmers shall be verified and shall meet applicable national safety standards. [1245]
The above OLA requirement indicates that the temperature must be monitored.
IHL-TMD-VI Duties and Maintenance-WRH
The above IHL documents states in section 2.2 that temperatures must be monitored and documented.
The blood warmers need to be monitored for temperature to ensure the product it is warming is at optimal temperature..

## Slide 18
“several printed procedures have sections blacked out with a marker “
II.F.11 Document control processes shall ensure that obsolete documents are removed and only currently authorized versions of appropriate documents are available for active use at relevant locations.[95]
Because the document control process does not compensate for sites performing processes differently, they are not ensuring that current documents exist.
VI.3 All laboratory technical procedures, including manufacturer's instructions used as procedures and electronic instructions, shall be documented and available at the workstation for relevant staff
The procedures are not available for relevant staff because they do not reflect the current practice. Therefore the staff do not follow the procedures are written.
Any alterations done to a procedure should be done with the use of a document control system. The procedures with the blacked out section are not considered “current” and therefore should not be used.

## Slide 19
“making unauthorized changes to printed procedures is also carried out in chemistry and hematology. “
IHL-OPS-VIII Establishing and Maintaining a Document Control System
The above IHL document clearly states that the document control system makes provisions to ensure the most current document is available to staff to correctly perform their duties. It also states that the staff have a responsibility to bring forth any revision that are required on a document.
The previously noted nonconformance must be upgraded as a “major” because it was found in more than one department and obviously an institution wide issue.

## Slide 20: Act Four: Chemistry Lab
Sugar, the chemistry assessor, discovers several reagents that do not have a recorded “in use” date or expiry date. She also notes several duplicate procedures in the laboratory manual and when she quizzes the technologists working in the area, they tell her that one of the procedures is obsolete and the one with the most recent date is the current procedure.
While assessing the specimen collection area she notes that the pneumatic tube system was installed earlier in the year, but there are no validation records. When she asks the laboratory manager about the validation records, the laboratory manager, an OLA assessor, waits until she is alone and then steps into Sugar’s personal space and starts shouting at her, trying to intimidate her.

## Slide 21: The Answers

## Slide 22: Act Four: Chemistry Lab
Sugar, the chemistry assessor, discovers several reagents that do not have a recorded “in use” date or expiry date. She also notes several duplicate procedures in the laboratory manual and when she quizzes the technologists working in the area, they tell her that one of the procedures is obsolete and the one with the most recent date is the current procedure.
While assessing the specimen collection area she notes that the pneumatic tube system was installed earlier in the year, but there are no validation records. When she asks the laboratory manager about the validation records, the laboratory manager, an OLA assessor, waits until she is alone and then steps into Sugar’s personal space and starts shouting at her, trying to intimidate her.

## Slide 23
“several reagents that do not have a recorded “in use” date or expiry date. “
IV.14 Maintenance of laboratory equipment shall ensure proper performance and assure accurate and reliable test performance.[159]
TM138 All equipment used to warm blood components shall include
a temperature sensing device and an audible alarm system. The temperature during use shall be documented. Blood warmers shall be verified and shall meet applicable national safety standards. [1245]
The above OLA requirement indicates that the temperature must be monitored.
IHL-TMD-VI Duties and Maintenance-WRH
The above IHL documents states in section 2.2 that temperatures must be monitored and documented.
The blood warmers need to be monitored for temperature to ensure the product it is warming is at optimal temperature..

## Slide 24
“duplicate procedures in the laboratory manual“ and “one of the procedures is obsolete and the one with the most recent date is the current procedure
IV.14 Maintenance of laboratory equipment shall ensure proper performance and assure accurate and reliable test performance.[159]
TM138 All equipment used to warm blood components shall include
a temperature sensing device and an audible alarm system. The temperature during use shall be documented. Blood warmers shall be verified and shall meet applicable national safety standards. [1245]
The above OLA requirement indicates that the temperature must be monitored.
IHL-TMD-VI Duties and Maintenance-WRH
The above IHL documents states in section 2.2 that temperatures must be monitored and documented.
The blood warmers need to be monitored for temperature to ensure the product it is warming is at optimal temperature..

## Slide 25
“no validation records “
IV.14 Maintenance of laboratory equipment shall ensure proper performance and assure accurate and reliable test performance.[159]
TM138 All equipment used to warm blood components shall include
a temperature sensing device and an audible alarm system. The temperature during use shall be documented. Blood warmers shall be verified and shall meet applicable national safety standards. [1245]
The above OLA requirement indicates that the temperature must be monitored.
IHL-TMD-VI Duties and Maintenance-WRH
The above IHL documents states in section 2.2 that temperatures must be monitored and documented.
The blood warmers need to be monitored for temperature to ensure the product it is warming is at optimal temperature..

## Slide 26
“steps into Sugar’s personal space and starts shouting at her, trying to intimidate her.“
IV.14 Maintenance of laboratory equipment shall ensure proper performance and assure accurate and reliable test performance.[159]
TM138 All equipment used to warm blood components shall include
a temperature sensing device and an audible alarm system. The temperature during use shall be documented. Blood warmers shall be verified and shall meet applicable national safety standards. [1245]
The above OLA requirement indicates that the temperature must be monitored.
IHL-TMD-VI Duties and Maintenance-WRH
The above IHL documents states in section 2.2 that temperatures must be monitored and documented.
The blood warmers need to be monitored for temperature to ensure the product it is warming is at optimal temperature..

## Slide 27: Act Five: Hematology Lab
Ivan Attitude, the hematology assessor starts asking the busy medical laboratory technologist running the automated instrument questions. Before she can answer Ivan asks another question in a very demanding tone of voice. He asks the technologist to see the procedure for the instrument maintenance. After looking at it Ivan states “This is a piece of garbage: - This isn’t what we do in our lab – so it isn’t right. This is going to be a non-conformance for sure!”. He then asks to see the routine procedure for a aPTT assays and asks “how do you ensure that these specimens are tested within 4 hours of collection – I will need to see 100 records to be sure you do what you say. We were cited for this at my lab so I am making sure that you do it.
While making notes on his checklist the senior MLT asks Ivan what he is writing and he replies “none of your business – it’s a secret. By the way can you tell me the name of the technologist running the automated instrument – I need to add her name to the non-conformance”.

## Slide 28: The Answers

## Slide 29: Act Five: Hematology Lab
Ivan Attitude, the hematology assessor starts asking the busy medical laboratory technologist running the automated instrument questions. Before she can answer Ivan asks another question in a very demanding tone of voice. He asks the technologist to see the procedure for the instrument maintenance. After looking at it Ivan states “This is a piece of garbage: - This isn’t what we do in our lab – so it isn’t right. This is going to be a non-conformance for sure!”. He then asks to see the routine procedure for a aPTT assays and asks “how do you ensure that these specimens are tested within 4 hours of collection – I will need to see 100 records to be sure you do what you say. We were cited for this at my lab so I am making sure that you do it.
While making notes on his checklist the senior MLT asks Ivan what he is writing and he replies “none of your business – it’s a secret. By the way can you tell me the name of the technologist running the automated instrument – I need to add her name to the non-conformance”.

## Slide 30
“steps into Sugar’s personal space and starts shouting at her, trying to intimidate her.“
IV.14 Maintenance of laboratory equipment shall ensure proper performance and assure accurate and reliable test performance.[159]
TM138 All equipment used to warm blood components shall include
a temperature sensing device and an audible alarm system. The temperature during use shall be documented. Blood warmers shall be verified and shall meet applicable national safety standards. [1245]
The above OLA requirement indicates that the temperature must be monitored.
IHL-TMD-VI Duties and Maintenance-WRH
The above IHL documents states in section 2.2 that temperatures must be monitored and documented.
The blood warmers need to be monitored for temperature to ensure the product it is warming is at optimal temperature..