## Slide 1: Sharps Safety
Training Module for Corewell Laboratory Phlebotomists
Updated: September, 2018

## Slide 2: Making Safe Choices
This module provides critical information/steps needed to ensure that our patients consistently receive safe care. It is your responsibility to notify your supervisor/educator if you have questions about the information in this module, or if you are unable to complete the steps as described.
Not following these steps may cause harm to our patients, ourselves or others and is called at-risk behavior. You should expect to be coached if you misstep, or drift, from the described procedures.
Should you choose to not follow this procedure (after being coached on the correct procedure) that may be considered reckless behavior and may result in punitive action.

## Slide 3: The purpose of this module is to provide:
Incidence and risks of sharps injury
Work practices to prevent sharps injuries
Instructions/demonstrations on the proper use and safe handling of currently used needle products including:
  Single use blood collection needle
  Blood collection set
  Blood transfer device
  Fingerstick lancets
  Infant heel lancets
  Urine collection kits
Current sharps disposal practices

## Slide 4: Incidence of Injuries
CDC estimates ~385,000 sharps injuries annually among hospital-based healthcare personnel (>1,000 injuries/day)
  Many more in other healthcare settings (e.g., emergency services, home care, nursing homes)
Increased risk for bloodborne virus transmission
Costly to personnel and healthcare system

## Slide 5: High Risk Situations
Injuries can occur….
During patient care:
  Inserting or withdrawing a needle
  Using a lancet
  Using a urine collection container
Immediately after sharp use:
  Activating a needle safety shield
During and after sharp disposal:
  Disposing of sharps into sharps containers
  Cleaning up after a procedure
  Sharps left on floors and tables, or found in linen, beds or waste containers

## Slide 6: Sharps Safety:
Be Prepared
Be Aware
Dispose with Care

## Slide 7: Sharps Safety:
Be Prepared:
  Organize your work area with appropriate sharps disposal containers within reach:
    Sharp containers should be in locked cabinets, with keys removed, when located in areas where patients are left unattended
    Sharps containers should not be located on the floor where a patient or child can gain access
  Work in well-lit areas
  Learn how to properly use the BD sharps safety devices that we currently use.
    Read the manufacturer’s educational literature and
    Watch a demonstration (see the following slides)

## Slide 8: BD Vacutainer®needles

## Slide 9: BD Vacutainer® needles

## Slide 10: IMPORTANT!
To avoid an accidental needle stick, activate the Vacutainer needle safety shield immediately upon removal from the vein.
Do NOT hold the needle up in the air before activating!

## Slide 11: BD Safety-LokTM Blood Collection Set (aka Butterfly)
Butterflies are one of the most common sources of needle stick and blood splash injuries for phlebotomists.
To minimize your risk, activate the butterfly safety shield during removal from the vein following the recommended steps demonstrated in the photos on the next few slides.

## Slide 12: Safety-LokTM Activation
Upon completion of collection, apply gauze over site with free hand but do not apply pressure yet.
While gripping the base of the yellow safety shield with thumb and index finger, position the tubing between your middle and ring finger.
2.
1.

## Slide 13: Safety-LokTM Activation
Grasp tubing tight between both fingers and then .....
Close fingers into a tight fist until the safety shield is completely locked in place over the needle.
Apply pressure over site and dispose of collection set and adapter (hub) into sharps container.
3.
4.

## Slide 14: Video: Safety-LokTM Activation
Be patient while the Video start paying.

## Slide 15: IMPORTANT!
Do NOT hold a needle up in the air before activating!
Do NOT use two-handed techniques to activate the Safety-Lok safety shield!

## Slide 16: BEWARE!
Do NOT place fingers into a hub (adapter) connected to a Vacutainer needle, butterfly or blood transfer device.
  Remember, there is a needle under the rubber sheath!
Do NOT gather up remaining blood collection equipment in one hand.
  It’s possible the butterfly needle may not be fully retracted into safety shield!

## Slide 17: BEWARE!
When dealing with agitated or combative patients, do not try to continue the venipuncture.
STOP the procedure and step back to avoid risk of injury.
  Tip: If possible, stick the needle into the sheet or nearby object to secure it until patient is back under control.

## Slide 18: Blood Transfer Device

## Slide 19: Capillary Blood Lancets – Pediatric/Adult Finger Sticks (Royal Oak, Troy, Grosse Pointe)

## Slide 20: Capillary Blood Lancet – Newborns (Royal Oak, Troy, Grosse Pointe)

## Slide 21: Capillary Blood Lancets – Pediatric/Adult Finger Sticks (Dearborn, Taylor, Trenton, Wayne)
Owen Mumford Unistik® 3 lancets
Features Comfort Zone Technology® (CZT®) with eight raised pressure points to reduce pain for a more comfortable sampling experience.
Needle retracts immediately after use to reduce the risk of needlestick injuries
Lock out indicator prevents reuse
Indicator for targeted positioning

## Slide 22: Capillary Blood Lancets – Newborns (Dearborn, Taylor, Trenton, Wayne)
Accriva Tenderfoot™ lancets
Safe, easy to use, and virtually pain free Softsweep™ incision method controlled to a depth just above most nerve fibers
Less bruising as compared with traditional lancet devices
No need for heel warmers, repeat sampling, and excessive squeezing of the heel
Blade permanently retracts back into the device, eliminating any chance of an accidental stick and creates a high-quality incision resulting in a sample free of tissue contamination
Available in four different incision depths: micro-preemie, preemie, newborn, and toddler

## Slide 23: Accriva Tenderfoot™ method
YouTube Video link for tutorial: https://www.youtube.com/watch?v=w1v0B_9fOXI

## Slide 24: Urine Collection using BD cup with transfer device in lid
6. Repeat steps 1-5 for the yellow UA tube.
Review the steps below for proper specimen processing and safe disposal.
Remove patient identifiers on label with a Sharpie.
Dispose of empty cup in regular trash.
Discard remaining urine in sink.

## Slide 25: Urine Collection using BD transfer straw
Review the steps below for proper specimen processing and safe disposal.
Discard remaining urine in sink.
Repeat steps 1-5 for the yellow UA tube.
Remove patient identifiers on label with a Sharpie.
Discard empty cup in regular trash .

## Slide 26: Sharps Safety:
Be Prepared – continued:
  Before handling sharps, assess any hazards such as a combative or confused patient
    Explain to the patient the importance of avoiding sudden movement that could dislodge the needle and possible discomfort or injury
    Ask for assistance, if needed

## Slide 27: Sharps Safety:
Be Aware
  Activate safety feature immediately after use with one hand, not both
  Keep exposed sharp in view
  Be aware of other people around you as well as where you are pointing the sharp device
  Focus on task; stop if you feel rushed or distracted
  Avoid hand-passing sharps; use verbal alerts when moving sharps
  Watch for sharps in linen, beds, on the floor or in waste containers

## Slide 28: Sharps Safety:
Dispose of Sharps with Care:
  Dispose of devices into designated rigid biohazard sharps containers
  Keep fingers away from the openings of sharp containers
  Do NOT overfill sharps containers; replace when safe capacity level is reached

## Slide 29: Biohazard disposal containers currently in use:
PHLEBOTOMY AREAS:
  Dispose of the following items into the Stericycle red plastic, drop containers located on phlebotomy carts, in patient rooms and at phlebotomy draw sites:
    Vacutainer needles and holders
    Blood collection sets (butterflies)
    Lancets
    Blood transfer devices
    Syringes
    Urine straws/transfer needle

## Slide 30: Biohazard disposal containers currently in use:
TECHNICAL AREAS:
  Dispose of the following items into red plastic, drop containers on countertops -or- large metal, foot pedal controlled containers with retractable lid:
    glass slides
    glass coverslips
    glass pipettes
    wood sticks
    needles

## Slide 31: First Aid:
If you experience a needle stick or sharps injury or are exposed to the blood or other body fluid of a patient during the course of your work, immediately follow these steps:
  Wash needle sticks and cuts with soap and water
  Flush splashes to the nose, mouth, or skin with water
  Irrigate eyes with clean water, saline, or sterile irrigants
  Report the incident to your supervisor.
  Complete the on-line Employee Illness/Injury Form posted on the Occupational Health website.
  Immediately seek medical treatment from Occupational Health Service. Patient source testing will be performed.

## Slide 32: Summary:
Be Prepared
  Learn proper use and disposal of specimen collection devices
  Assess potential hazards
Be Aware
  Focus on task and keep exposed sharps in view
Dispose with Care
  Use safe techniques and correct biohazard disposal containers

## Slide 33: References:
Sharps Safety for Healthcare Professionals, www.cdc.gov/sharpssafety
Sharps Workbook – Appendix C www.cdc.gov/sharpssafety
BD Venous Blood Collection Product Literature http://www.bd.com/vacutainer/products/venous/
BD Capillary Blood Collection Product Literature http://www.bd.com/vacutainer/capillary/
BD Urine Collection Literature http://www.bd.com/vacutainer/products/urine/