## Slide 1: Anti-A1 and A2 or Weaker subgroups
Updated 12/2023
Let’s clear up the confusion!

## Slide 2: Anti- A1 and A2 or weaker subgroups
There are two principal subgroups of A
    A1 and A2
          Approximately 80% of group A individuals are A1 subgroup; the remaining 20% are A2 or weaker subgroup
          Several weaker A subgroups have been described:
              A3, Ax, Am, Ael, etc.
              We don’t differentiate between these A subgroups; they are just considered A2 weaker subgroup
          The Vision detects the subgroups better than tube testing with weaker forward A wells or mixed field A wells.
Subgroup

## Slide 3: When do we suspect that a patient’s RBCs are A2 subgroup?
There will be an ABO discrepancy…
  There is a problem in the forward “A” well
  The “A” well may be mf (mixed field), 2+ or less
Subgroup

## Slide 4: How do we prove that the patient’s RBCs are A2 or weaker subgroup?
The reagent Anti-A1 lectin made from the extract of the plant, Dolichos biflorus, has specific Anti-A1 specificity.
It will react with A1 cells, but not other subgroups of A.
The patient’s RBCs strongly agglutinate with Anti-A1 lectin if he or she is group A1.
The patient’s RBCs fail to agglutinate with Anti-A1 lectin if he or she is group A2. Note that patient’s A2 cells do agglutinate with the regular Anti-A in our TQ1 and TQ2 racks (and in ProVue forward A well)
Subgroup

## Slide 5: Where do I find the Anti-A1 lectin?
The Anti-A1 lectin is kept in the A1 rack located in the double door Helmer refrigerator beside the other antigen typing reagents.
Subgroup
The A1 rack contains: 3 sets of A1 cells (1 in-date and 2 expired) 3 sets of A2 cells (1 in-date and 2 expired)
Anti- A1 Lectin

## Slide 6: How do I type the patient’s A cells with Anti- A1 Lectin?
Subgroup
Follow the directions in the manufacturer’s insert
Make sure you DO NOT INCUBATE! You are instructed to read at immediate spin.
Anti-A1 lectin typing should not be performed on cord blood samples or on patients less than 2 years old due to incomplete development of the A antigen on these RBCs.
Document your results on the form, Resolution of ABO Discrepancies for A subgroups and Patients with Anti-A1

## Slide 7: What do I use as control cells when subtyping with Anti-A1 Lectin?
For positive control , use the in-date A1 cells in the A1 Rack
For the negative control, use the in-date A2 cells in the A1 Rack
Subgroup

## Slide 8
Document the results on the proper form
The results for the
Negative control cell
and the
Positive control cell
are documented here
Subgroup
Positive
Negative

## Slide 9: What’s next?
Add patient’s RBC A1 results in Soft:
  Patient / Edit / Antigen
Subgroup
This patient’s cells are positive with Anti-A1 Lectin

## Slide 10: Don’t forget the comment!
  Patient / Edit / Messages
  If the RBCs are A1 positive
  …that means there is agglutination when the
  RBCs are mixed with
  Anti-A 1 Lectin…
  Add the comment
  “ A1 subgroup”
Subgroup

## Slide 11: Don’t forget the comment!
  Patient / Edit / Message
  If the RBCs are A1 negative
  …that means there is
  NO agglutination
  when the RBCs are
  mixed with
  Anti-A 1 Lectin…
  Add the comment
  “ A2 or weaker subgroup”
Subgroup

## Slide 12
Keep in Mind…
To make Anti-A1, the patient’s RBCs must be A2 or weaker subgroup.
  Just like with any other antibody.
  For example: A patient should be negative for the Kell antigen to make Anti-Kell.
Not all A2 or weaker subgroups make Anti-A1. Only approximately 5% of A2 patients actually make the antibody.
The A1 antigen testing only needs to be performed once in a lifetime… just like Kell or other antigens.
A2B or weaker subgroup is just a patient who is type AB, but the A is an A2 or weaker subgroup.

## Slide 13: Remember, only 5% of A2 or weaker subgroups will make Anti-A1.
So… when do suspect Anti-A1?
When you detect unexpected reactivity in the Reverse A well in a patient who otherwise appears to be type A or type AB
(i.e. A discrepancy between the forward typing reactions and the reverse typing reactions).
Forward as an “A”
Unexpected reactivity in
“a reverse” well

## Slide 14: How do you prove Anti-A1?
First, do a test tube ABO.
        If the unexpected reactions are still present
        in the reverse tube typing, then…
  Do a tube panel to identify Anti-A1
        See procedure Resolution of ABO Discrepancies due to A subgroup or Anti-A1

## Slide 15: Tube Panel to ID Anti-A1
The A1 and A2 cells are from A1 Rack.
The O cells can be any panel cells

## Slide 16: How do you interpret the tube panel to ID Anti-A1?
If the patient has Anti-A1, expect the three A1 cells to be reactive and the A2 and O cells to be non-reactive.

## Slide 17: What if your panel is pan-reactive???

## Slide 18: Don’t PANIC!!!
It may be a cold reacting antibody.
See the procedure for Cold Antibodies

## Slide 19: How do you record your results in SOFT?
If the antibody screen is negative, the ABID is not automatically ordered.
  Order an ABID on the patient
    Patient / Order / Modify
Select ABID from the drop down menu

## Slide 20: How do you record your results in SOFT?
Answer the ABID
  Patient / Order / Results
  Result the antibody as Anti-A1
  Add the NEXM comment

## Slide 21: How do you crossmatch a patient with Anti-A1?
Immediate spin crossmatch
  See the Crossmatch Job Aid
Use group O donor RBCs
  or
You can antigen type group A donor RBCs for A2 or weaker subgroup (if you have a lot of extra time on your hands!)

## Slide 22: Keep in mind…
If a patient’s RBCs agglutinate in Anti-A1 lectin , then he/she is group A1.
Just like if a patient’s RBCs agglutinate in Anti-Kell, then they are Kell positive.
If a patient’s RBCs do not agglutinate in Anti-A1 lectin but agglutinate in Anti-A, then they are A2 or weaker subgroup.
Group A1 patient do not generally make Anti-A1.
Just like patients that are Kell positive generally do not make Anti-Kell.
A2 or weaker subgroups may produce Anit-A1.
The presence of Anti-A1 can cause ABO discrepancies between the forward and reverse typing.
A patient will forward type as a group A and reverse type as a group O.

## Slide 23: As a General Rule…
Forward typing discrepancies ARE NOT generally resolved in the tube method. They are resolved by the transfusion history or performing a subtype with Anti-A1 lectin.
Reverse typing discrepancies can be resolved by starting with a tube type.

## Slide 24: Any Questions?