## Slide 1: An Introduction to Patient Identification and Proper Sample Labeling for Blood Bank

## Slide 2: Proper Patient Identification
Use
Use at least 2 patient identifiers: Patient’s full name and date of birth.
For Blood Bank, verify patient’s medical record number as well.
Ask
Ask the patient to state and spell his/her first and last name and date of birth.
Simply asking the patient to affirm his or her name (“Are you John Smith”), is not acceptable.
DO NOT PROCEED
If the patient does not have a hospital armband, DO NOT PROCEED.
Notify the patient’s nurse and delay collection until proper identification has been affixed.
Resolve
Resolve all discrepancies in patient identification prior to collection.
Proceed
Proceed with sample collection only when patient identification is properly verified.

## Slide 3: Soft ID Procedure (Basic PDA Use)
Enter user ID and password.
Select assignment/role, then click OK.
Select “Collect” and wait for collection list.
Proceed to patient
Scan patient’s armband.
Verify patient ID with the patient, then click VERIFY.
Once patient order(s) appear, click PRINT to print out labels.
Draw patient’s blood.
Label tubes and scan the barcode label on each tube.
Click COLLECT, then click SUBMIT.

## Slide 4: General Rules Regarding Blood Bank Patient Samples
Draw two (2) 6 ml pink top tubes.
Label all tubes with the following information:
  Patient’s full name
  Date of birth
  Medical Record Number
  Date and time sample collected
  First initial and full last name of the person drawing the blood sample. (Example: B. Smith)
  Blood Bank 3 letter ID code (Commonly called BloodLoc codes). Example: XYZ
  BloodLoc codes are printed in duplicate. One code is placed on the patient’s hospital armband. The second code is placed on one of the pink top tubes. After that, the code is handwritten on any additional tubes(s) collected.
  All required information must appear on EACH tube submitted for testing.
  LIS or hospital chart labels are acceptable.

## Slide 5: General Rules Regarding Blood Bank Patient Samples
For inpatients, if Red Blood Cells (RBCs) are being requested, a new Type & Screen order and sample will be needed every three (3) days.
Blood Bank ID codes (BloodLoc codes), are to be used for the entire admission once assigned. That means you will not remove or switch to a new code, if the patient currently has a BloodLoc code on their armband. There can be only one code on the armband at any given time.
If a patient’s armband needs to be replaced for any reason, prior to discarding the current hospital band, two individuals should confirm the patient’s identity and immediately transfer the current BloodLoc code to the new hospital armband while at the patient’s bedside.
If the armband has been removed or the information is no longer legible, a new BloodLoc code must be assigned.
Improperly labeled tubes will be rejected. This includes samples submitted to Blood Bank with more than one patient label on the tube.
If you have any questions or concerns, contact the Blood Bank staff before you draw any blood samples.

## Slide 6
The End