## Slide 1: Disseminated Intravascular Coagulation (DIC) & PFA-100
By: Michell McAdams
02/2013

## Slide 2: DIC
Disseminated intravascular coagulation (DIC) is an abnormal activation of coagulation (blood clotting) mechanisms that can develop as the result of a variety of diseases and conditions.
It is associated with inappropriate blood clotting (thrombosis) inside the blood vessels throughout the body. Clotting consumes coagulation proteins and platelets causing small clots to form that disrupt normal blood flow to organs (such as the kidneys). It also causes excessive bleeding and organ failure to occur, ranging in severity from moderate to life-threatening.

## Slide 3: Test
PT/INR (Protime)
PTT (Partial Protime)
TT (Thrombin Time)
FIB (Fibrinogen)
D-DI (D-Dimer)
FDP (Fibrin Degradation Products)
FM (Fibrin Monomer)

## Slide 4: Running Test
PT/INR, PTT, TT, FIB, D-DI are ran on the Stago.
To run these test:
  Open Sample Drawer
    Make sure you are on Auto Mode
  Scan barcode
  Place sample in empty position
  Test run according to the barcode

## Slide 5: Fibrin Monomer
Reconstitute each vial (two controls and one reagent) with exactly 200µL of sterile water.
Using Glass Tubes ONLY
  Label three GLASS TUBES: Neg, Pos and Patient’s last 4 numbers of order
  Pipet 100µL of control/patient into labeled tubes
  Mix vial of test reagent well without causing bubbles, then add 50µL to each tube
  Incubate tubes in 37ºC water bath for 10 minutes.

## Slide 6: Fibrin Monomer (Cont.)
  Remove tubes from water bath. Insure all water is wiped from the outside and bottom of tubes
  Label a test card with appropriate labels
  Transfer entire contents of tube onto card in proper circle
  Rock or rotate in a circular motion to mix, (Mechanical rotator may be used at 80-100 rpms). Rotate for 6 minutes
  Compare patient to controls
  Report as Negative or Positive

## Slide 7: Fibrin Degradation Products
Bring reagents/controls to room temp
Using Polyurethane Tubes
  Label 3 tubes as A, B, C or 1:2, 1:4, 1:8 along with last 4 numbers of order
  Add 50µL of buffer to each tube
  Add 50µL of patient sample to tube A, vortex thoroughly
  Transfer 50µL from tube A to tube B, vortex
  Transfer 50µL from tube B to tube C, vortex

## Slide 8: Fibrin Degradation Products (Cont.)
  Mix reagent well
  Label a test card appropriately to include negative and positive controls
  Transfer 20µL of undiluted controls and 20µL of diluted patient samples slightly off-center in appropriately labeled red circle
  Transfer 20µL of reagent next to, but not touching, each test sample
  Using a clean disposable mixing rod with each sample mix the reagent into the sample

## Slide 9: Fibrin Degradation Products (Cont.)
  Spread the sample so it fills the entire circle
  Rotate slide for 3 minutes in a figure 8 motion
  Observe for agglutination by using the control reactions as a reference.
  See chart for reporting results.
Fibrin Degradation Product Interpretation |  |  |  | 
Serial Tube ID | A | B | C | Plasma FDP Results (µg/mL)
Dilution | 1:2 | 1:4 | 1:8 | 
Reaction Interpretation | = | = | = | <5
 | +++ | = | = | >5 to <10
 | +++ | +++ | = | >10 to <20
 | +++ | +++ | +++ | >20

## Slide 10: DIC
Record all DIC results in the Manual Result Logs Book
  Place a patient aliquot label on the sheet, record the lot # of reagent with expiration date, if your control is positive or negative, then initial.
  ***NOTE: Save ALL positive FM and FDP samples. They must be transferred into a polyurethane tube labeled and put into SP Coag freezer in appropriate place.

## Slide 11: Platelet Function Analysis (PFA)

## Slide 12: PFA
PFASCR is the test code that will appear on the patient label and in Soft
DO NOT SPIN this sample. This test is ran on whole blood

## Slide 13: PFA
For this test there are two cartridges: COLL/EPI and COLL/ADP
ALWAYS run the COLL/EPI cartridge first
The system identifies which cartridge is running by the slots on the cartridge
Cartridge is kept in the 3rd slide door of the Coag refrigerator
***NOTE: Cartridge must be at room temp before using.

## Slide 14: Starting a PFA
First you must do the daily maintenance (If not done)
Check to be sure specimen is properly collected
Check to make sure there is no clot. Do this gently, you do not want to agitate the sample
***Note: The allowable time from collection to testing the specimen is maximum 4 hours and should be at room temperature.

## Slide 15: PFA
Before each patient you MUST do a Self Test.
  Check trigger solution (Volume and Exp Date: 60 days opened)
  Be sure the blue cartridges are in place
  Press the soft key next to Menu
  Press #2 (Maintenance)
  Press #2 (Self Test)
  Press the soft key next to yes then next to continue
  The system will check for cartridges
  Place a sponge in the center of instrument when it comes around; add alcohol to the sponge. Press continue
  After removing sponge Press continue
  You are now ready to run a patient.

## Slide 16: PFA
How To Run:
    Place the COLL/EPI cartridge into cassette.
    Gently invert the patient sample 3-4 times
    Use reverse pipetting to sample 800µL of the patient sample. 900µL if PLT count is <150,00
    Without causing bubbles pipette into the small well closes to you

## Slide 17: PFA
  You will need to place the cassette with the test cartridge(s) into the incubation well
  Press the softkey located next to RUN
  The system will then recognize the cartridge
  For the patient ID use the MRN of the patient
  When testing is completed the system will print the results along with the patient ID

## Slide 18: PFA
  Interpreting Results for COLL/EPI:
    If there are any errors you MUST repeat test
    If result it <90 you can report result
    Normal results: 90-193
    If >193 you MUST run a COLL/ADP cartridge
    Report and verify your result for the COLL/EPI. A canned message will appear automatically
    This will reflex the COLL/ADP

## Slide 19: PFA
  Interpreting Results for COLL/ADP:
    If there are any errors you MUST repeat test
    Normal results: 61-135
    Report and verify your result for the COLL/ADP. A canned message will appear automatically

## Slide 20: PFA
  When completely finished with testing place the blue cartridges back in the cassette and place on the instrument.
***NOTE: It does not matter which cartridge goes first.

## Slide 21
~ THE END~
