## Slide 1: Patient Differential Slides, Spun hematocrits & Leukocyte alkaline phosphatase (LAP)
By: Tina Gorup

## Slide 2: Patient Differential Slides

## Slide 3: Patient Differential Slides
Differential Slides or Blood Smears are made from blood drawn in lavender (EDTA) tubes.
Differential slides are manually made when:
  Patient samples are drawn in bullets or oversized collection tubes that cannot be run through the blood analyzer in closed mode
  For determining if a patient is a possible “platelet clumper” (blood smears from ACD tubes are also made on these patients)
  When automated slides are not of an acceptable quality
  When albumin slides are required to obtain an accurate patient differential

## Slide 4: Making a slide
Obtain two clean glass slides.
  Slides with a white frosted end are for routine patient samples
  Slides with a colored frosted end (usually green in color) are for STAT patient samples.
On one slide the blood sample is placed, this is the "sample" slide. The second slide is used to smear the drop of blood, this is the "spreader" slide
Handle slides by edges only (any grease on the slide will cause the dried blood to flake off during staining).
Place a small drop of well mixed patient blood on sample slide by using a diff quick, capillary tube or applicator sticks.

## Slide 5: Making a slide
Place the end of the spreader slide on the sample slide so that the short sided edge of the spreader is just below the drop of blood.
Sample Slide
Spreader Slide

## Slide 6: Making a slide
The next two steps should be done quickly to avoid smears that are too thick. Holding the spreader at an angle of 30o (relative to the sample slide), push the spreader so that the edge just barely touches the drop of blood. By capillary action, a thin line of blood will spread along the edge of the spreader .

## Slide 7: Making a slide
Quickly drag the spreader along the entire length of the sample slide in one fluid motion. Note that the blood is being dragged by the spreader.
The smear should end before the end of the sample slide also it should end in a "feathered edge" - a region where the blood cells are well separated.

## Slide 8: Finishing touches
Place a patient aliquot label over the frosted end of the slide and write your initials in any space available on the label.
Allow the slide to dry and place in a stainer cassette to be stained.

## Slide 9: Stained slide
Note the feathered edge and how the smear is free of streaks or holes.
Name
Order #
MRN
Date
Initials

## Slide 10: Albumin slides
Some patient conditions create cells known as “smudge” cells (fractured or torn apart white blood cells). These are often associated with certain types of leukemia.
There are also some patients that have protein abnormalities present in their blood making it difficult to create good quality differential slides.
Both of these conditions require the making of Albumin Slides.

## Slide 11: Making albumin Slides
Place one drop of 22% Bovine Albumin Solution in a small glass tube.
Using a plastic pipette, add 4 drops of well mixed patient blood to albumin in the tube.
Gently mix blood and albumin together by lightly shaking the tube.
Make two blood smears from the blood and albumin mixture using the same steps for making differential blood smears.
Label both albumin slides with a patient aliquot label, and write your initials and the abbreviation, ALB in any open space on the label.
Allow the slides to dry for 5 minutes in the slide warmer and then place in slide cassette to be stained.

## Slide 12: Spun Hematocrits

## Slide 13: Spun Hematocrits
Spun Hematocrits are considered a manual procedure and can be performed on blood or body fluid specimens.
The purpose of the spun hematocrit is to determine the quantity of red blood cells as a percentage of the blood or body fluid. It may be expressed as a percentage (42%) or as a decimal fraction (0.42 L/L).

## Slide 14: Procedure
Using a microhematocrit tube (also called a capillary tube) fill tube approximately 3/4th full of well mixed blood or body fluid.
Seal one end of the tube with modeling clay.
Place filled tube into the radial grooves of the mico-capillary hematocrit centrifuge with the sealed end against the rubber gasket to prevent breakage.
Repeat process filling a 2nd capillary tube from the patient’s blood or body fluid sample.

## Slide 15: Procedure
Select a previously run patient specimen as a patient control.
Fill 2 capillary tubes with patient control blood.
Balance the centrifuge by placing the capillary tubes opposite one another in the radial grooves of the centrifuge.

## Slide 16: Procedure
Place inside lid over specimens and screw down.
Close the outside centrifuge lid down and set centrifuge timer for 3 minutes.
After the samples have been centrifuged place each capillary tube in the micro-capillary hematocrit reader and record hematocrit values.

## Slide 17: Procedure
Duplicate patient control samples should agree ±2 units from the automated blood analyzer.
Record both patient control and patient values in binder labeled Result and QC Manual Heme Back-up.

## Slide 18: Spun Hematocrits
Microhematocrit Centrifuge, Micro Hematocrit Capillary Reader, Capillary Tubes & Sealing Clay

## Slide 19: Spun Hematocrits
Balanced Capillary Tubes in Radial Grooves of Centrifuge

## Slide 20: Spun Hematocrits
Correct Placement of Capillary Tube in Micro-Hematocrit Capillary Reader

## Slide 21: Spun Hematocrits
Notes on Body Fluid Samples:
  Body fluids usually do not contain a significant number of red blood cells. A measurable hematocrit indicates the presence of bleeding or pooling of blood in the body cavity or location which normally doesn’t contain blood. In general, the higher the body fluid hematocrit the more extensive the bleeding is for the patient.

## Slide 22: Leukocyte Alkaline Phosphatase (LAP)

## Slide 23: methodology
The LAP test is a stain procedure that is performed to assess the amount of alkaline phosphatase enzyme found in the granules of white blood cells known as bands and segmented neutrophils.
LAP is most often used to distinguish between a leukemoid reaction (infections, toxic conditions, and other miscellaneous states) and chronic granulocytic (myelogenous) leukemia
LAP activity can be normal, increased or decreased in a variety of conditions.

## Slide 24: Specimen requirements
Collect Specimen in a Green Sodium Heparin Tube
Blood Collected in a Green Lithium Heparin Tube Is Not Acceptable Because it is Toxic to the Living Cells & Can Cease Cellular Functions That May Have Unexpected Effects on LAP Enzyme Activity
Blood Collected in Lavender Tubes with EDTA May Inhibit LAP Enzyme Activity & Can Produce Falsely Lower LAP Scores. It May Only Be Used in Non-Recoverable Circumstances with the Permission of a Pathologist

## Slide 25: Specimen stability
Blood Smears Must Be Made Within 24 Hours After Blood is Collected
After the Tube is Drawn, Protect the Specimen From Light.
  Aluminum Foil can be used to protect the specimen from light
Light Inactivates Alkaline Phosphatase Activity & May Cause a Falsely Decreased LAP Score

## Slide 26: supplies
Green Sodium Heparin Tube, Blood Slides & Tray for Holding Blood Smears

## Slide 27: procedure
Mix Blood in Sodium Heparin Tube Well
Make 7-8 thin, long blood smears that stretch across ¾ of the slide length.
Label slides with patient information in pencil on the frosted end of each slide.
If possible, make 4 thin, long blood smears from a known female patient on the postpartum floor of the hospital. These slides will serve as a positive control.
Place both patient slides and control slides in slide tray; allow slides to dry
Cover with towel and place in designated drawer in the bone marrow room. Leave note on board so first shift will know that a LAP needs to be performed. There is NO negative control.

## Slide 28: Leukocyte Alakaline Phosphatase (LAP)
Mix Green Sodium Heparin Tube Well

## Slide 29: Leukocyte Alakaline Phosphatase (LAP)
Place Drop of Blood on 7-8 slides

## Slide 30: Leukocyte Alakaline Phosphatase (LAP)
Use Pusher Slide to Make 7-8 Blood Smears for Patient & 4 Blood Smears for a Control
Make Both Patient & Control Slides Thin and Long

## Slide 31: Leukocyte Alakaline Phosphatase (LAP)
Place Both Patient & Control Blood Slide in Tray and Cover With A Towel

## Slide 32: Leukocyte Alakaline Phosphatase (LAP)
The LAP procedure is completed by counting 100 stained band or segmented neutrophils on a slide and scored on a 1-4 rating scale. The LAP score is the sum of the cell rating and represents a relative percentage of cytoplasmic volume describing the amount of LAP activity.

## Slide 33: ~The End~ 