## Slide 1: Annual Proficiency Testing Training

## Slide 2: What is Proficiency Testing (PT)?
The testing of unknown samples sent to a laboratory by a Health and Human Services (HHS) -approved PT program.
Most sets of PT samples are sent to participating laboratories on a scheduled basis (usually three times per year).
After testing, the laboratory reports its sample results back to their PT program. The program grades the results using the CLIA grading criteria and sends the laboratory their scores.
CMS and accreditation organizations routinely monitor their laboratories’ performance.

## Slide 3: Why is (PT) Important?
It is a tool the laboratory can use to verify the accuracy and reliability of its testing, and can also be used to validate the entire testing process, including competency of testing personnel.
Routine reviews of PT reports by the laboratory staff and the laboratory director will alert them to areas of testing that are not performing as expected, as well as indicate subtle shifts and trends that, over time, would affect patient results.

## Slide 4: Handling of PT
PT samples must be tested in the same manner you test patient specimens.
This means testing the PT samples the same number of times as you would patient specimens, at the same time as patient specimens, by the same personnel that routinely test the patient specimens, and using the same test system, including analyzer and reagents, that is routinely used for the patient specimens.
PT samples should not be analyzed in duplicate (repeated) unless patient samples are routinely analyzed in the same manner.
With respect to morphologic examinations (identification of cell types and microorganisms; etc.), group review and consensus identifications are permitted only for unknown samples that would ordinarily be reviewed by more than one person on an actual patient sample.
PT samples should be rotated among all testing personnel in your laboratory.

## Slide 5: Handling of PT, continued
Please note that some PT sample preparation may be necessary before testing.
It is important for you to read the specimen handling and preparation sections of the PT booklet that comes with each event to determine if PT samples require special treatment prior to testing.
In other words, after preparation, PT samples must be treated in the same manner as patient specimens.

## Slide 6: PT Referral
Never send PT samples out of your laboratory for any reason, even if you routinely send out patient specimens for additional testing.
PT referral is when one laboratory (Laboratory A) sends its PT samples to another laboratory (Laboratory B) or multiple laboratories (Laboratories B, C, D, etc.) for any reason.
Never accept PT samples from another laboratory for any reason.
Whether or not acts are authorized or even known by the laboratory’s management, a laboratory is responsible for the acts of its employees.
Your laboratory should only test the PT sample as it would a patient specimen up until the point it would refer a patient specimen to a second laboratory for any form of further testing (i.e., distributive, confirmatory, reflex testing).

## Slide 7: Discussing PT with Other Labs
Never discuss your PT results with another laboratory and never enter into discussion with another laboratory about their PT results before the PT event cut-off date.
This activity may result in sanction(s) taken against your Laboratory.

## Slide 8: Reporting PT
PT results must be reported by personnel at the laboratory where PT was performed.
BSWH Laboratories strictly prohibit personnel from accessing proficiency testing records from other BSWH laboratories.

## Slide 9: Record Retention of PT
You must keep a copy of all your records, such as the step by step PT sample preparation and handling, all the steps taken in the testing of the sample, instrument printouts, a copy of the PT program results form used to record and submit your PT results (includes the attestation statement), and the PT program’s evaluation of your laboratory’s performance, etc.
These copies must be maintained for a minimum of two years from the date of the PT event (five years for Transfusion Medicine).
If any corrective actions are taken as a result of an unsatisfactory or unacceptable score, records of these actions must also be maintained for two years (five years for Transfusion Medicine).