## Slide 1: Centrifuge Safety
Laboratory Services

## Slide 2: Objectives
At the completion of this module, the participant should be able to correctly:
Describe the physical and exposure hazards for a centrifuge
Discuss the guidelines for before, during, and after centrifugation
Identify how to balance a rotor with different number of tubes
Explain how to decontaminate a centrifuge

## Slide 3: Centrifuges
A centrifuge is a common tool in the laboratory.
It uses centrifugal force to separate substances according to particle size and density differences.
Has great potential for injuring users if not operated properly!

## Slide 4: Centrifuge Hazards
Hazards by centrifuges include:
Physical hazards
  Mechanical failure or stress
  Sample imbalance causing machine movement
  Metal fatigue
  Corrosion of rotor
Exposure hazards
  Sample container breakage causing aerosols that are harmful if inhaled
  Aerosolization of biological, chemical, or radioactive materials

## Slide 5: Centrifuge Safety
90% of all centrifuge accidents are the result of user error!
Each user should be properly trained on operating procedures

## Slide 6: Before Centrifugation Guidelines
Wear appropriate PPE
Inspect centrifuge
  Ensure centrifuge bowls & tubes are dry
  Ensure spindle is clean
  Use matching sets of tubes & buckets
  Ensure O-ring is not cracked or worn
Inspect tubes before use
  Check for cracks/defects
  Follow manufacturer’s filling limits
Inspect environment
  Ensure that work surface is level and firm enough to support equipment

## Slide 7: Before Centrifugation Guidelines
Balance tubes in rotor!
  Ensure that the rotor is balanced with equal and opposing tubes
Cap each tube &/or bucket before centrifugation
Close & lock lid before starting centrifuge

## Slide 8: Rotor Balancing
Frothingham, R. (1999, February). Centrifugation without a balance tube. American Biotechnology Laboratory, 17, 84/
NOTE: These images represent tubes with equal volume!

## Slide 9: During Centrifugation Guidelines
Keep lid closed at all times during operation
Don’t exceed safe rotor speed according to manufacturer
Don’t leave centrifuge until full operating speed is reached, and appears to be running safely without incident
Stop centrifuge immediately if an unusual condition (noises or shaking) begins and check load balances

## Slide 10: After Centrifugation Guidelines
Allow centrifuge to come to a complete stop before opening cover
Wear appropriate PPE
Check inside centrifuge for possible tube breakage or spills (leak), or if an open tube has been spun. If found,
  Leave lid closed and allow potential aerosols to settle for 30 minutes or open in a Biosafety Cabinet
  Wearing appropriate PPE (includes mask), clean spill thoroughly with appropriate disinfectant according to procedure
If spill occurs, use appropriate decontamination and cleanup procedures
Report all accidents to your supervisor immediately!
Rev. 7/6/16