## Slide 1: Hemoccult Sensa
Fecal Occult Blood Lab Test

## Slide 2: Supplies Needed: Hemoccult Cards Hemoccult Developer Applicator Stick

## Slide 3: ***Special Note***
All developers must have expiration dates checked before use
All cards must have expiration dates checked before use
All tests performed must be ordered and resulted in patient EMR

## Slide 4: Label each card with patient information

## Slide 5: Open front cover where patient information is written. Apply stool specimen to Area A & B. Close card cover. Wait 3-5 minutes before testing.

## Slide 6: To test, open back cover with instructions. Apply 2 reagent drops on each application area (A&B) on backside of card (not where initial specimen was applied). Add a (1) drop of reagent to the center of internal QC area. Interpret within 60 seconds.
2 drops per application area
1 drop for QC area

## Slide 7: After adding reagent look for a blue color which indicates a positive result, even if only on one side of the card.
One side has blue = Positive
Both sides have blue = positive

## Slide 8: No color indicates a negative patient result. QC must be positive
QC must be positive

## Slide 9: ED Supplies for Fecal Occult Blood and Gatric Occult Blood testing
Supplies must be ordered via Logi-D
Or contact Materials Management
POCT/Main Lab doesn’t keep ED supply