## Slide 1: CURRENT GOOD MANUFACTURING PRACTICES FOR BLOOD AND BLOOD COMPONENTS
TRANSFUSION SERVICE RECORDS –
REQUIREMENTS ACCORDING TO 21CFR606.160

## Slide 2: Requirements of 21CFR606.160
(a)(1) Records shall be maintained concurrently with the performance of each significant step in the collection, processing, compatibility testing, storage and distribution of each unit of blood and blood components so that all steps can be clearly traced. … (continued next slide)

## Slide 3: Requirements of 21CFR606.160
(a)(1) … All records shall be legible and indelible, and shall identify the person performing the work, include dates of the various entries, show test results as well as the interpretation of the results, show the expiration date assigned to specific products, and be as detailed as necessary to provide a complete history of the work performed.

## Slide 4: Requirements of 21CFR606.160
(a)(2) Appropriate records shall be available from which to determine lot numbers of supplies and reagents used for specific lots or units of the final product.
(b) Records shall be maintained that include, but are not limited to, the following when applicable: (2) Processing records: (ii) Component preparation, including all relevant dates and times.

## Slide 5: Requirements of 21CFR606.160
(b)(3) Storage and distribution records: (i) Distribution and disposition, as appropriate, of blood and blood products. (ii) Visual inspection of whole blood and red blood cells during storage and immediately before distribution.
(b)(3)(iv) Reissue, including records of proper temperature maintenance. (v) Emergency release of blood, including signature of requesting physician obtained before or after release.

## Slide 6: Requirements of 21CFR606.160
(b)(4) Compatibility test records: (i) Results of all compatibility tests, including crossmatching, testing of patient samples, antibody screening and identification.
(b)(5) Quality control records: (i) Calibration and standardization of equipment. (ii) Performance checks of equipment and reagents. (iv) Periodic tests of capacity of shipping containers to maintain proper temperature in transit. (v) Proficiency test results.

## Slide 7: Requirements of 21CFR606.160
(b)(6) Transfusion reaction reports and complaints, including records of investigations and followup.
(b)(7) General records: (ii) Responsible personnel. (iii) Biological product deviations. (iv) Maintenance records for equipment and general physical plant. (v) Supplies and reagents, including name of manufacturer or supplier, lot numbers, expiration date and date of receipt.