## Slide 1: NRL DISASTER MANAGEMENT

## Slide 2: OBJECTIVES OF THIS TRAINING
To provide a quick view on the OSH emergency response management
SCOPE OF THIS TRAINING
ensure a systematic approach to emergency management planning and response
facilitate harmonization of relevant Authority(s) requirements and provide a clear hierarchy of control in the event of significant emergencies.

## Slide 3: APPLICATION IMPLEMENTATION
Perform Risk management for analyzing risk and deciding on the most appropriate control measure(s) to manage and reduce risk. Although all reasonably practicable efforts to reduce risk may be taken, there will normally be some residual risk. It is this residual risk that may lead to emergencies. Anticipated emergency scenarios shall be identified during the process of risk assessment.
Emergency management involves the process of containing and controlling incidents so as to minimize the effects and to limit danger to persons and property.
An emergency management program may consist of a number of specific response plans.
Emergency response plans shall be simple and straightforward, flexible and achieve compliance with legislative requirements. Furthermore separate on-site and off-site emergency response plans shall be prepared if applicable.
Emergency response plans provide the basis for emergency preparedness.

## Slide 4: IDENTIFICATION OF POTENTIAL EMERGENCY SCENARIO(s)
identify all potential emergency scenarios based on the Risk Assessment that could have an impact upon their undertakings or cause danger to persons and property
Emergency scenarios must consider the following information:-Legal Requirements, Results of risk management activities, Previous incidents; and emergency situations that have occurred elsewhere, specifically in Referral laboratory operations.
Must consider emergency scenarios that can occur during: normal Operations; and abnormal conditions, including start up or shut down activities, construction and demolition.
Include all potential emergency scenarios
Access how identified scenarios will impact upon

## Slide 5: POTENTIAL EMERGENCY SCENARIOS INCLUDE (not limited)
Incidents leading to serious injuries/fatalities or ill health;
Explosion / fire;
Release of hazardous materials or gases;
Natural disaster (e.g. storm, flood, earthquake);
Bomb threat / terrorism / unrest;
Pandemic of communicable or infectious disease;
communications failure;
Chemical Spills
radiological accident; and
biological agent release

## Slide 6: PLANNING FOR EMERGENCY SCENARIOS
Prepare specific Emergency Response Plans (ERPs) which includes action execute documents that are produced and maintained for immediate implementation to safeguard people, property or business from foreseeable emergency scenarios.
NRL ERP format

## Slide 7: NRL DISASTER PLAN ACTIVATION
1.1 Coordinators
Notify the individuals that will coordinate the response to the incident in the event of a disaster.
An incident coordinator is defined as someone who will take charge of managing the situation that has caused the facility to activate its disaster plan – Safety Officer and Facility Officer
An operations coordinator is defined as someone who will take charge maintaining facility operations during the time period that the site has activated its disaster plan – Director-Technical Operations and Director- Operations, Quality Assurance Director.
1.2 Notification of Plan Activation
The incident coordinator must call emergency contacts (numbers are displayed in the emergency contact list) in order to report the plan activation regardless of the time of day or day of the week. The site representative that is making the call needs to have the following information on hand before making the call:
  The name and address of the facility or facilities involved.
  The name of the caller.
  The phone number(s) where the caller can be reached. THE CALLER IS TO STAY BY THE TELEPHONE, IF SAFE TO DO SO.
  A description of the event triggering the plan, including any injuries, hospitalizations, or fatalities to employees or third parties.
Incident coordinator is responsible for contacting the Operations Coordinator and inform about the event. The level of contact is as follows;
  Director – Operations: First level
  Director –Technical Operations: Second level
  Director –Quality Assurance : Third level

## Slide 8: INCIDENT COMMAND CENTER
Once this plan is activated, set up the Incident Command Center.
The incident command center is the location from which response to the incident is directed.
Operations Coordinator will lead the Disaster preparedness and its activities.
Director of Operations is the lead in Incident command center and in the absence Director of Technical operations and/or Director of Quality Assurance will take the charge. Operations Coordinators are responsible for notifying the updates regarding the disaster preparedness or the events.
The location of the primary incident command center is: NATIONAL REFERENCE LABORATORY –ICAD, ABU DHABI.
The location of the secondary incident command center is : NATIONAL REFERENCE LABORATORY- DUBAI (use this site if the primary location cannot be used)

## Slide 9: REQUIREMENTS OF EMERGENCY PLAN
Risk Assessments and the knowledge in the potential emergency scenarios
Written policies and procedures implemented
Emergency exit routes provided and marked
Emergency lighting of workplace and exit routes
Supervisors must inform workers of risk
Annual emergency drills
Inventory of substances that endanger firefighters/rescuers
Provide emergency wash facilities
Train workers in fire prevention
Toxic Gases
  Provide emergency ventilation
  Provide shutdown and containment
Emergency rescue - qualified workers
Personal Protective Equipment
Maintenance of equipment
Maintain effective communications with rescue and evacuation personnel
Any worker assigned to firefighting to be physically fit and trained annually
Provide rescue for workers entering a confined space

## Slide 10: EMERGENCY EVACUATION PROCEDURES
The emergency evacuation of the facility can be triggered by Activation of the building’s audible/visual fire alarm system and to the extent possible Security officers to inform the staff.
Once a disaster has been determined to have occurred, everyone in the facility must be notified. Employees with response roles are to be mobilized. Employees must take the following steps:
•All employees will evacuate the building in an orderly manner to the designated departmental meeting areas detailed in this plan.
•Floor wardens will sweep their departments to verify that their department has been evacuated.
•Floor wardens will report to the incident command center the evacuation status of their department.
If an employee has activated the emergency evacuation of a facility through pulling a fire alarm station or calling 999, he/she must report to their supervisor upon evacuation from the facility.
The employee will go with the supervisor to the incident command center to provide details regarding the event.

## Slide 11: EVACUATION OF THE DISABLED
An updated list of individuals with declared disabilities that require assistance in this facility is maintained by the site safety officer, Floor wardens and Human Resources.
NRL personnel are to assist in the evacuation of all persons with disabilities (e.g. disabled, contractors, visitors) in their respective areas.
Visually Impaired- Tell the person the nature of the emergency and offer guidance to the nearest emergency exit. Ask the disabled person to take your arm and follow you.
Hearing Impaired- Write a note telling what the emergency is and the nearest evacuation route. Turn the light switch on and off to gain attention, and then indicate what is happening through gestures and que-cards.
Mobility Impaired Persons- Mobility impaired people should be escorted to the nearest exit or stairwell. At least two people should assist if evacuation becomes necessary. Do not carry a mobility-impaired person unless the danger is imminent.

## Slide 12: DESIGNATED ASSEMBLY MEETING AREAS
Primary and secondary evacuation assembly points are established and are specified in the evacuation plan.
Two assembly points
  Front side of the laboratory building
  Back side of the laboratory building

## Slide 13: FOLLOWING ARE THE IDENTIFIED POTENTIAL EMERGENCY SCENARIOS (NRL-OHS-SOP-023)
Inclement weather
Fire
Earthquakes
Floods
Electricity/power outage
Loss of water
Loss of HVAC (heating and air conditioning) system
Loss of refrigeration capability
Loss of telephone service
Medical emergencies
Violent people / unauthorized visitors
Acts of terrorism
Acts of bioterrorism (NRL-OHS-SOP-021)
Bomb threats
Hazardous chemical and waste spill emergency response
Computer system emergency
Crash of contracted specimen transport carrier

## Slide 14: KNOW YOUR SAFETY OFFICER AND FLOOR WARDENS
Emergency contact numbers
POLICE | 999
Ambulance | 998
Fire- Civil Defense | 997
Electricity and water | 991

## Slide 15: EMERGENCY PHONE LISTINGS
INCIDENT COORDINATORS
Facility Name: NATIONAL REFERENCE LABORATORY-ICAD, ABU DHABI
Command Center Phone Numbers: 02-493-0500
Designation | Land Line | Mobile
Safety Officer | 0097124930417 | 00971501483087
Facility Officer | 0097124930481 | 00971544769996
Infection Controller | 0097124930487 | 
OPERATIONS COORDINATORS
Designation | Land Line | Mobile
Director-Technical Operations | 0097124930471 | 00971526995296
Director – Operations | 0097124930449 | 00971522382855
Quality Assurance Director | 0097124930439 | 00971526990686

## Slide 16: SUPPORT RESPONSE PERSONNEL
Designation | Issues/Events | Mobile | Shift
Director Operations | CID/CCTV | 052 238 2855 | Day and Night
Director-Technical Operations | CID/CCTV | 052 699 5296 | Day and Night
Security in-charge | CCTV Operator/Security | 0555153968 | Day
Security in-charge | CCTV Operator/Security | 0524490385 | Night
Director- Quality Assurance | CAP, DAC,HAAD,DHA | 0526990686 024930414 | Day/Night - only emergencies
Quality Assurance Coordinator & Safety officer designee | Quality and Safety Issues | 0501483087, 024930417 | Day/Night - only emergencies
Facility Officer | Utilities (Water/Electricity) | 0565247625 | Day & Night
Mechanical, Electrical and Plumbing in-charge | Utilities (Water/Electricity) | 0552872376 | Day
IT- Director | Phone or Internet | 052 249 0484 | Day & Night
IT – Manager | Phone or Internet | 055 800 9864 | Day & Night
Infection controller | Infection Control | 0563221449 | Day/Night - only emergencies

## Slide 17: NRL EMERGENCY RESPONSE PLAN
When the Fire Alarm sounds, act immediately to ensure your safety: Never ignore or assume the alarm is false or the result of a test. Everyone must evacuate the building by way of the safest and closest exit and/or stairway. Once outside the building, move away from the building. Do not obstruct the fire fighters and fire trucks access to the building. If there is an incident occurring on the upper floors and glass is being blown out of the windows, the area below is the hazard zone where serious personal injuries will happen. Do not remain in or near the hazard zone. Once outside, never re-enter the building until you are told to do so by the Safety officer.
When the fire alarm sounds, lab workers must EXIT the building, but first: 1. Turn off all flames and other ignition sources 2. Close all hazardous material containers 3. Close sash on all fume hoods 4. Turn off all electrical equipment (if possible) 5. Other:__________________________________________

## Slide 18
If your clothing catches on fire: 1. “STOP, DROP and ROLL” (if someone else is on fire, knock them to the ground, and instruct them to roll back and forth) or drench with water if safety shower is immediately available. 2. Cover your face with your hands. 3. Use a fire blanket (if available) or a coat to help smother the flames. Never use a fire extinguisher on someone. 4. Obtain medical attention, if necessary. 5. Report incident to supervisor and safety Officer
If there is a hazardous material spill: 1. Determine if this is a “major” or “minor” spill. 2. Assist anyone who may have been contaminated or injured during the spill. 3. Clean up minor spills using appropriate spill control equipment. 4. Call Safety officer and Facility officer for all major spills. Evacuate the area and do not let anyone enter until Emergency Responders have cleaned up the spill.

## Slide 19
Minor cuts and puncture wounds Vigorously wash injury with soap and water for several minutes. Obtain medical attention. Report incident to supervisor and safety Officer

## Slide 20
Emergency | Prevention/Mitigation | Preparation | Response | Remediation
Biological Spill | Good Laboratory practices | Understand Spill Kit procedure Training | Major Attend to injured or contaminated persons and remove them from exposure. Alert people in immediate area of spill. Close doors to affected area. Put on protective equipment. Cover spill with paper towels or other absorbent materials. Carefully pour a freshly prepared 1 in 10 dilution of household bleach around the edges of the spill and then into the spill. Avoid splashing. Allow a 20-minute contact period for the bleach solution to be effective. Use paper towels to wipe up the spill, working from the edges into the centre. Clean spill area with fresh towels soaked in disinfectant. Place towels in a plastic bag and decontaminate in an autoclave. Have person knowledgeable of the incident and laboratory assist emergency personnel. Minor Wear disposable gloves. Soak paper towels in disinfectant and place over spill area. Place towels in plastic bag for disposal. Clean spill area with fresh towels soaked in disinfectant. | Decontaminate area after clean up Dispose of all Material appropriately. Investigate cause of spill and review with Safety officer. Document spill, response and follow-up with staff. Replenish spill kit.

## Slide 21
Emergency | Prevention/Mitigation | Preparation | Response | Remediation
Biosafety Cabinet Failure | Have BSC inspected and certified annually | Understand the BSC operating procedure Plan to contain | Leave fans on Use disinfectant | Have BSC inspected
Fume Hood failure | Install Fume Hood alarm. Measure face velocity before using and check this periodically. | Plan to contain any vapors Understand operating procedures | Close containers. Close sash. | Contact facility
Medical/ First Aid | Good Work practices Wear proper PPEs | First Aid kit Emergency phone numbers Test emergency eye wash stations MSDS availability AED availability | Major Remain calm. Initiate lifesaving measures if required. Do not move person unless there is danger of further harm. Keep person warm. Call for emergency response. Minor Initiate first aid. Report incident. | Wash the area Dispose contaminated clothing Replenish first aid kit
Power Failure |  | Identify critical equipment. Ensure UPS or other emergency power supply is available. Update phone list. Post sign or communicate the staff on the failure | Shut off equipment. Secure all testing Close chemical containers, fume hood. Exit building. | 

## Slide 22
Emergency | Prevention/Mitigation | Preparation | Response | Remediation
Chemical Spill | Good Laboratory practices Wear appropriate PPE Secondary containment | Spill kits with instructions, absorbents, reactants, and protective equipment should be available to clean up minor spills. Training MSDS updates Understand MSDS before working with the material | Decide if spill is Minor or major. Clean up Minor spill. Call facility for major spill & evacuate area. Major Attend to injured or contaminated persons and remove them from exposure. Alert people in the laboratory to evacuate. If spilled material is flammable, turn off ignition and heat sources. Call for assistance. Close doors to affected area. Have person knowledgeable of incident and laboratory assist emergency personnel. Minor Alert people in immediate area of spill. Wear protective equipment, including safety goggles, gloves, and long-sleeve laboratory coat. Avoid breathing vapors from spill. Confine spill to small area. Use appropriate kit to neutralise and absorb inorganic acids and bases. Collect residue, place in container, and dispose as chemical waste. For other chemicals, use appropriate kit or absorb spill with vermiculite, dry sand, or diatomaceous earth. Collect residue, place in container and dispose as chemical waste. Note: A minor chemical spill is one that the laboratory staff is capable of handling safely without the assistance of safety and emergency personnel. All other chemical spills are considered major. | Decontaminate area after clean up Dispose of all Material appropriately. Investigate cause of spill and review with Safety officer. Document spill, response and follow-up with staff. Replenish spill kit.

## Slide 23
Chemical spill on body Flood exposed area with running water from faucet or safety shower for at least 5 minutes. Remove contaminated clothing at once. Make sure chemical has not accumulated in shoes. Obtain medical attention, if necessary. Report incident to supervisor and safety Officer
Biological spill on body Remove contaminated clothing. Vigorously wash exposed area with soap and water for one minute. Obtain medical attention, if necessary. Report incident to supervisor and safety Officer
If you need to use the emergency shower or eyewash: 1. Pull the handle to start the water flowing. 2. Hold your eyes open to get the water under your eyelids. 3. Remove all contaminated clothing and shoes. 4. Stay under the water for at least 15 minutes to get all the chemicals off.
Hazardous material splashed in eye Immediately rinse eyeball and inner surface of eyelid with water continuously for 15 minutes. Forcibly hold eye open to ensure effective wash behind eyelids. Obtain medical attention. Report incident to supervisor and safety Officer

## Slide 24
Emergency | Prevention/Mitigation | Preparation | Response | Remediation
Severe Weather |  |  | Secure all Hazardous materials. Move electrical equipment off floor & unplug. Backup/take critical data. | 
Water Loss |  | Update phone list. Post sign on lab door when running an unattended experiment. Include contact number, materials involved and directions in case of water or power failure. | Secure all Hazardous materials. Do not run Hazardous experiments until water service is returned. | Test emergency Eyewash station to ensure water is running.
Bomb Threat |  | Use the Bomb threat checklist | Inform to safety officer and line manager accordingly | 

## Slide 25: NRL Incident Reporting
All incidents must be notified to safety officer and line manager/supervisor
All incidents to initiate an OVR in q-pulse CAPA module
Safety officer to initiate a team of investigation about the incident
occupational accident, injury or illness incident investigation, corrective and preventive action report (NRL-OHS-FRM-016)
Report of unsafe condition or hazard in NRL-QA-FRM-090

## Slide 26: FOR REFERENCE AND READING
NRL Disaster Management SOP- Refer Q-pulse for NRL-OHS-SOP-023
OSHAD-ELEMENTS-SF