## Slide 1: Laboratory Chemical Hygiene Plan
By Lai Ming Woo

## Slide 2: Why?
OSHA Hazard communication standard (HCS) 29 CFR 1910.1200 states employee has the right-to-know…
-The standard (CHP Appendix B)
-Hazardous chemicals & products in the workplace
-Methods of protecting themselves from exposure

## Slide 3: Why? (Cont’d)
Under OSHA, employer is responsible for providing a safe & healthful workplace
-but employees are responsible for their own safety &
the safety of the others
VS
Mad Scientist
Proper PPE

## Slide 4: Hazard Communication GHS Elements
  1. Labels

## Slide 6
2. 16 sections Format Safety Data Sheets (SDSs) (Appendix M)
Non-mandatory Sections 12- 15 for OSHA are regulated by EPA or DOT

## Slide 7
Bleach SDS

## Slide 8
Pulmonary edema is a condition caused by excess fluid in the lungs

## Slide 9
Current inventory & SDSs are accessible on:
G:/drive & MSDS Online link

## Slide 10: Hazardous Chemical SOPs (CHP Appendix E)
Aspiration Toxicity Irritant and Sensitizer
Carbon Dioxide (Dry Ice) Liquid Nitrogen
Carcinogens Nitric Acid
Chloroform Oxidizers
Compressed Gases Peroxide Forming Chemicals
Corrosives Phenol
Cyanide Reproductive Toxins
Flammables Sodium Azide
Formaldehyde Sulfuric Acid
Germ Cell Mutagen Target Organ Toxicity
Glacial Acetic Acid Toluene
Hydrogen Gas Toxic or Highly Toxic

## Slide 11
Ordering
Purchasing the smallest amount required for work
Disposal $$$/Hazards Not cheaper to purchase in bulk
Ensuring proper storage available
Ensure capability to cleanup if the amount ordered is spilled; e.g. amount of absorbent & PPE

## Slide 12
Storage
University of California, Santa Barbara
Household/laboratory refrigerators have electrical components inside
Flammable liquid in an open container/incompletely sealed container evaporate to concentration of lower explosive limit
Spark inside

## Slide 13
Secondary Containment
Can be used to segregate chemicals or store chemicals on the floor
Should be
-sturdy, chemical resistant
plastic AND
-able to hold the total
volume of chemical inside
Contact QA if you need one

## Slide 14
Storage- What wrong with this picture?

## Slide 15: Chemical Spill Response Guidelines CHP Appendix F

## Slide 16: What kit is where?
CHP-Appendix F.1: Spill Kits and Safety Equipment Maps

## Slide 17: Hazardous Waste Management

## Slide 18
Incompatible Chemicals
Here at ODHL
Dispose down the drain with plenty of water
NEVER put bleach right after
Toxic gases which can include chloramines, chlorine & hydrogen cyanide

## Slide 19
G:\LABORATORY PROCEDURES\Quality Assurance and Compliance\Chemical Inventory
Name of Chemical | Chemical Resistance Materials SDS = Recommend in SDS Blank = No Info Red = Poor/Not Recommend Orange = Fair Green = Good |  |  |  |  |  | Chemical Used in
 | Butyl | Neoprene | PVC | Nitrile | Latex | Other | 
Acetaldehyde |  |  |  |  |  |  | BADT
Acetone | SDS |  |  | 10 mins | 10 mins |  | VIR/BADT/Rad Chem
Acetonitrile |  |  |  |  |  |  | NBS
Chloroform |  |  |  |  |  |  | PARA
Ethyl Acetate |  |  |  | 8 mins |  |  | PARA/NBS
Formic Acid |  |  |  |  | SDS |  | NBS
Methanol |  |  |  | 32 mins |  |  | BADT/BT/NBS/PARA/TB
Nitric acid |  |  |  | 12 mins |  |  | Rad Chem
Phenol Liquid |  |  |  | 39 mins |  |  | BT
Sulfuric acid |  |  |  | 1.9 hrs |  |  | Rad Chem
Toluene | 6 mins |  |  | 11 mins |  | Viton >16 hrs | BADT
Xylene |  |  |  | 21 mins |  | Viton >8 hrs | BT

## Slide 20
Acids with cyanide highly toxic hydrogen cyanide gas
Acids (Vinegar) with bleach highly toxic chlorine gas
Nitric acid or solid oxidizer (Nitrates)
with combustible materials (Paper/alcohols/solvents)
May result in
Hydrogen peroxide/sulfuric acid mixtures
May spontaneously detonate
Incompatible Chemicals (Cont’d)

## Slide 21
Current CHP:
G:\LABORATORY PROCEDURES\Safety and Security\Laboratory Chemical Hygiene Plan
MediaLab # 51793.768