## Slide 1: Chemical Inventory, Ordering and Labeling
By Lai Ming Woo

## Slide 2: Why Chemical Inventory and Labeling?
OSHA Hazard communication standard (HCS) 29 CFR 1910.1200 states employee has the right-to-know…
-The standard (CHP Appendix B);
-Hazardous chemicals & products in the workplace; AND
-Methods of protecting themselves from exposure

## Slide 3: Why? (Cont’d)
Under OSHA, employer is responsible for providing a safe & healthful workplace
-but employees are responsible for their own safety &
the safety of the others
VS
Mad Scientist
Proper PPE

## Slide 4: Why Chemical Inventory? (Cont’d)
Important to the safety of employees, first responders & visitors
- Obtain SDSs
- Anticipate hazard control
- Spill responses/ Cleanup requirements

## Slide 5
Current inventory & SDSs are accessible on:
G:/drive & MSDS Online link
Current CHP:
  G:\LABORATORY PROCEDURES\Safety and Security
  MediaLab # 51793.768

## Slide 6
Ordering
Purchasing the smallest amount required for work
Disposal $$$/Hazards Not cheaper to purchase in bulk
Ensuring proper storage available
Ensure capability to cleanup if the amount ordered is spilled; e.g. amount of absorbent & PPE

## Slide 7
Secondary Containment
Can be used to segregate chemicals or store chemicals on the floor
Should be
-sturdy, chemical resistant
plastic AND
-able to hold the total
volume of chemical inside
Contact QA if you need one

## Slide 8
What happened at OSU?
Destroyed lab after April 8th, 2005 explosion & fire
Took firefighters >1 hour to extinguish
Student recalled, “I was loading solvent bottles to the top shelf of a flammable cabinet...I put the 12th bottle up, the shelf collapsed…large amounts of hexane spilled on the floor & my jeans were soaked…”

## Slide 9
What happened at OSU? (Cont’d)
“This has happened before & it's not something where you get too alarmed…more concerned about breathing the vapors & a small cut on my arm…within 5 minutes, the explosion occurred.”
Luckily, all 11 students evacuated because of the fumes
Lesson Learned:
DO NOT overload the shelves (weight limit?)
Investigation- the cabinet was properly vented but located close to a freezer
Vapor + Spark

## Slide 10
Lesson Learned (Cont’d):
Safety Culture Issues
- 95% grad students interviewed said they won’t report a
safety hazard due to fear of reprisals
-”happened before & it's not something where you get
too alarmed” Hexane shower should never be a norm!
Lack of training on chemical SDS, handling, spill responses…

## Slide 11: Hazard Communication GHS Elements
  1. Labels

## Slide 12
2. 16 sections Format Safety Data Sheets (SDSs) (Appendix M)
Non-mandatory Sections 12- 15 for OSHA are regulated by EPA or DOT

## Slide 13: Chemical labeling
Supervisor will ensure primary & secondary chemical container labels meet GHS standards
Product arrives w/ improper/mutilated labels contact LSO
Received & opened dates are required on all; including containers inside a kit
Upon request, QA will provide labels

## Slide 15: How to read your SDSs? (Appendix M)
Section 2 Signal word, hazard & precautionary
statements
Section 4 First aid measures & symptoms/effects
Section 7 Handling & storage conditions
Section 8 Exposure control limits, engineering controls
& PPE selection recommendations
Section 10 Stability, reactivity, conditions to avoid &
incompatible materials. Store away from incompatibles
Section 11 for toxicological effects
https://time.com/5722129/buffalo-wild-wings-employee-dies-fumes/

## Slide 16: Spotcheck Neonatal GALT Microplate Reagent Kit
GALT MP Color Reagent SDS Section 2

## Slide 17: What does mean?
Appendix E: ODHL Hazardous Chemical SOPs-Toxic or Highly Toxic
Exposure ≠ 100% Death
Lethal Dose, 50% (LD50)- amount given all at once causes death of 50% of a group of test animals
Lethal Concentration, 50% (LC50)- concentration of a chemical in air/water causes death of 50%
= Highly Toxic = Low LD50 and LC50

## Slide 18: Hazardous Chemical List and SOPs
Hazardous Chemical List
G:\LABORATORY PROCEDURES\Quality Assurance and Compliance\Chemical Inventory-hazards info from SDSs
-Updates by QA
-When receive newer version/new SDS
SOPs for each hazard on the list & some highly hazardous chemicals (CHP Appendix E)
-SOPs & SDSs together provide instructions to work
with hazardous chemicals safely

## Slide 19: Hazardous Chemical List and SOPs (Cont’d)
Uncheck ‘(Blanks)’ from Filter of the hazard column to view the list of chemicals with that hazard

## Slide 20
Acids with cyanide highly toxic hydrogen cyanide gas
Acids (Vinegar) with bleach highly toxic chlorine gas
Nitric acid or solid oxidizer (Nitrates)
with combustible materials (Paper/alcohols/solvents)
May result in
Hydrogen peroxide/sulfuric acid mixtures
May spontaneously detonate
Incompatible Chemicals

## Slide 21
G:\LABORATORY PROCEDURES\Quality Assurance and Compliance\Chemical Inventory
Name of Chemical | Chemical Resistance Materials SDS = Recommend in SDS Blank = No Info Red = Poor/Not Recommend Orange = Fair Green = Good |  |  |  |  |  | Chemical Used in
 | Butyl | Neoprene | PVC | Nitrile | Latex | Other | 
Acetaldehyde |  |  |  |  |  |  | BADT
Acetone | SDS |  |  | 10 mins | 10 mins |  | VIR/BADT/Rad Chem
Acetonitrile |  |  |  |  |  |  | NBS
Chloroform |  |  |  |  |  |  | PARA
Ethyl Acetate |  |  |  | 8 mins |  |  | PARA/NBS
Formic Acid |  |  |  |  | SDS |  | NBS
Methanol |  |  |  | 32 mins |  |  | BADT/BT/NBS/PARA/TB
Nitric acid |  |  |  | 12 mins |  |  | Rad Chem
Phenol Liquid |  |  |  | 39 mins |  |  | BT
Sulfuric acid |  |  |  | 1.9 hrs |  |  | Rad Chem
Toluene | 6 mins |  |  | 11 mins |  | Viton >16 hrs | BADT
Xylene |  |  |  | 21 mins |  | Viton >8 hrs | BT