## Slide 1: Hazardous Chemical SOP-Compressed Gases
By Lai Ming Woo
My toes…

## Slide 2: Why? OSHA 1910.101 - Compressed gases
Each employer shall determine that compressed gas cylinders under his control are in a safe condition to the extent that this can be determined by visual inspection…(49 CFR parts 171-179 and 14 CFR part 103)…Compressed Gas Association Pamphlets C-6-1968 and C-8-1962
The in-plant handling, storage, and utilization of all compressed gases in cylinders, portable tanks…shall be in accordance with Compressed Gas Association Pamphlet P-1-1965
Need safety relief devices for compressed gas containers
[61 FR 9236, March 7, 1996]

## Slide 3: Why? University of Hawaii explosion
March 16, 2016
https://www.dailymail.co.uk/news/article-4142300/Researcher-lost-arm-blast-sues-University-Hawaii.html
http://www.hawaii.edu/news/wp-content/uploads/2016/07/Report-2-University-of-Hawaii.pdf
A student lost an arm
Used a gauge not intrinsically safe to combine
Extremely flammable hydrogen, carbon dioxide & oxygen

## Slide 4: University of Hawaii explosion
Warning Signs ignored by the lead researcher:
-“Small internal explosion” not reported to University
-Tank not grounded occasion static shocks
-Several leaks were detected

## Slide 5
Safety training requested but refused
University of Hawaii faces $115,500 fine
Lesson learned:
- Training, competency & reinforcement
- ≥ 2 Swing out Exit Doors
- Check for potential ignition sources
in areas with flammable gases
- Risk assessment for appropriate PPE
- Hazardous Chemical SOPs

## Slide 6: What do we have? (Compressed Gas Hazards)
May explode if heated
Simple asphyxiant that displaces oxygen
Argon, Carbon Dioxide, Helium, Hydrogen,
Liquid Nitrogen, Nitrogen, P-10
Desk and Office Cleaner, Spray mount & Dry Ice
Also

## Slide 7: What do we have? (Cont’d)
Frostbite, cryogenic burns or injury
- Refer to SDS
Extremely flammable or flammable
-Black Flag, Chewing Gum Remover, Gas duster
-Disinfecting Office Cleaner, Lysol Disinfectant Spray…
-Hydrogen Compressed Gas
Additional safety measures for Flammables, Cryogenic Liquid Nitrogen & Asphyxiant (Hazardous Chemical SOPs)

## Slide 8: Receiving
Check if:
-Without heavy rust or pitting
-Safety caps on
-Container labels legible
Bonus Question: Why?
If yes, ACCEPT

## Slide 9
DOT Regulation
Serial #
Manufacture Date
Ring of original manufacturer
Retest Date
Tracking # Barcode
Manufacturer Inspection Mark
Weight of the unfilled cylinder

## Slide 10: Receiving (Cont’d)
Hydrostatic Pressure Test Date
Vendor’s responsibility to do the test
All ( ) 10 years (49 CFR §180.209)
Carbon Dioxide 5 years (49 CFR §180.207)
EXCEPT

## Slide 11: Personal Protective Equipment (PPE)
Additional if needed:
Lab apron & Tychem sleeves
Safety goggles and face-shield
Appropriate gloves for the Compressed Gas
e.g. Long cryogenic gloves

## Slide 12: Transporting
Chain on specially designed carts & never dragged… OR rolling long distance
Do not allow to strike each other/other surface violently
Do not lift or move by the safety cap
Keep safety cap in place
Bonus Question 2: Why bother?

## Slide 14: Mark your cylinders
LMW 5-31-19

## Slide 15: Assembly
Do Not use the tubing/cylinder top as a storage area
Do Not use oil/lubricant in a tubing system with oxygen
Use regulators approved for the specific gas
Check for leak after installation & periodically
with Snoop Leak Detector

## Slide 16: Assembly (Cont’d)
Mount pressure gauges to be easy to read & pressure-relieving devices pointing away from people
Open cylinder valves slowly & carefully after connected to the process
- Stand clear of the regulator/valve outlet while opening
If a cylinder valve is difficult to operate
Discontinue Use,
Contact QA to return to supplier

## Slide 17: General Safety
Remove metal jewelry/watches b4 working cryogen
Protect containers against physical damages & away from corrosives
Secure above the midpoint
Do not use excessive force or a plier to open a valve
When not in use: Shut valves, relieve pressure, remove gas regulators & put safety cap on

## Slide 18: General Safety (Cont’d)
Keep flammables away from combustible materials
Order cylinders so they wouldn’t be stored 4 a long time
Must return b4 next Hydrostatic Pressure Test Date
- Required by DOT
- Retest Between 3-10 years
2007 Test Date

## Slide 19: Oxygen Diffusion Gas Monitors
Used to monitor air quality in confined spaces with asphyxiating gas cylinders
Check oxygen content before entering area

## Slide 20: Emergency Procedure
A leak of the cylinder or orange/red alarm on Oxygen Diffusion Gas Monitor
Stop the leak if safe to do so
Isolate area w/ ‘Chemical Spill Keep Out’ OR ‘Do Not Enter’
Do not re-enter until approved by Supervisor/LSO

## Slide 21
The 101 wrong ways?

## Slide 22
The 101 wrong ways (Cont’d)?

## Slide 23
What’s wrong with this picture?
Direct contact with liquid nitrogen, uninsulated pipes/equipment can cause cryogenic burns
Eye fluids will freeze on contact causing permanent eye damage
A jet of cryogen vapor can freeze the skin/eye faster than liquid/metal contact

## Slide 24
Take Home Messages
Store near sink could lead to rust and explode
Store in hot car