## Slide 1: Chemical Spill Response Guidelines CHP Appendix F
By Lai Ming Woo

## Slide 2: Why chemical spill kits?
Under OSHA, employer is responsible for providing a safe & healthful workplace
-but employees are responsible for their own safety &
the safety of the others
Chemical spill kits are used
-for the safety of you & others
-to protect lab equipment

## Slide 3: What kit is where?
QA Guideline: Laboratory Chemical Hygiene Plan- Appendix F.1: Spill Kits and Safety Equipment Maps

## Slide 4: Who is responsible?
Employee Responsibilities
-Ensure access to Spill Kits/Emergency Safety
Equipment like sink eye washes are not blocked
-Be familiar with location & use of spill kits (Appendix F.1)
QA oversees monthly check of all spill kits

## Slide 5: Spill-X Kit
2 Shaker Bottles each
-Spill-X-A Agent
-Spill-X-C Agent
-Spill-X-S Agent
Accessories-safety goggles, chemical gloves, plastic scoops, disposal bags, scraper, pH test papers & pick-up pans
Spill-X Spill Kit Treatment Guide & Placard
2 ODH Chemical Spill Signs & a roll of Do Not Enter tape

## Slide 6: Spill-X Kit EXTRA
Pink PIG Hazmat Absorbent Pads
Chemical Inventory for Spill

## Slide 7: Spill-X Spill Kit Treatment Guide 2009
SPILL-X-A/SPILL-X-C agents neutralize acid/base
-Test representative samples of spill residue for final pH
-Add more agent if necessary
SPILL-X-S agent adsorbs solvent to form a dry & powdery spill residue
SPILL-X-FP agent polymerizes formaldehyde but may not solidify the waste

## Slide 8: Spilfyter Mercury Spill Kit
https://www.youtube.com/watch?v=8jY_sKyPT9k (25ml/337g)
No mercury thermometer/hydrometer/mercury
containing equipment at ODHL
Evacuate, isolate & ventilate the area
-Mercury vaporizes at room temperature
-Non-irritating odorless vapor is absorbed directly
through skin & inhalation
Contact QA/LSO if you need a thermometer/hydrometer

## Slide 9: BioRem-2000 Solvent Safety Spill Kit > 2L
2 Gal. BioRem-2000 Super Absorber
32 oz BioRem-2000 Surface Cleaner
User Directions
Accessories-1 Pair 18 mil. Latex Gloves, 2 Pairs Goggles, 1 Broom/Pan & Wipes
Directions for use is printed on the 5-gallon container label
Check Current Chemical Inventory

## Slide 10: Ultimate Acid Eater Safety Spill Kit > 2L
Two 1-gal. Neutralizer
User Directions
Accessories-2 Goggles, 2 Aprons, 4 PVC Gloves, 4 Hazmat Boot Covers & a 20' Barrier Tape
Directions for use is printed on the 5-gallon container label
Check Current Chemical Inventory

## Slide 11: General Guidelines
Immediately shake Spill-X-FP on 37% Formaldehyde & Formalin to suppress vapor
-Room 143
-Under Enterics laboratory sink
Encircle then cover

## Slide 12: General Guidelines (Cont’d)
DO NOT absorb:
Strong oxidizers (Nitric/Sulfuric acid) with saw-dust or combustible absorbents
Flammable liquid with paper towels
Evaporation rate Vapor concentration around the spill

## Slide 13: General Guidelines (Cont’d)
Unknown Spills
-Evacuate & Isolate the area
-Contact QA/LSO
-Do not re-enter until notified
No QA member/LSO is available notify Supervisor
Evacuate & isolate the area until the spill is cleaned

## Slide 14
3 Tools for Cleanup
#1
Spill Cleanup Determination Flowchart
#2 + 3
Chemical Inventory +
Appendix F.2.

## Slide 15: Spill Cleanup Determination Flowchart
PPE is not available or adequate? OR
Spill results in a fire or explosion? OR
Immediate risk for a fire or explosion? OR
Spill results in personnel requiring medical attention?
Yes
NO
Evacuate &
isolate the area

## Slide 16: Spill Cleanup Determination Flowchart (Cont’d)
Quantity:
> 100 ml of 37% Formaldehyde/10% Formalin? OR
> 1L of the list below?
Acetone Lancer Clean Acid
Acetonitrile Lancer Clean Detergent
Ammonium hydroxide Methanol
Chloroform Mineral Oil Scintillator
Ethyl Acetate NeoBase Assay Solutions
Ethyl Alcohol Nitric acid
Filter Count N-Propanol
Hydrochloric acid Sodium Hydroxide Solution
Insta-gel XF Succinate Extraction Buffer
2-Propanol Sulfuric acid
Isopropanol Ultima Gold LLT
Yes
NO
Evacuate &
isolate the area

## Slide 17
≥ Quantity limit
Leave nearby fume hood sash opens (If inside fume hood, shut the sash)
Close doors/turn off any ignition sources
Evacuate all personnel
Isolate area w/ ‘Chemical Spill Keep Out’ OR ‘Do Not Enter’
Bonus question 1: Where do you find the spill sign and caution tape?
Spill-X Kit

## Slide 18: Spill Cleanup Determination Flowchart (Cont’d)
Not trained on spill cleanup? AND No other trained staff available?
OR Unknown spill?
Determine Spill Type and Proceed with Spill Response
Contact LSO/QA
for Assistance
Yes
No
Next Up Spill Response Determination

## Slide 19: Spill Cleanup PPE
Don Proper PPE
Bonus Question 2: Why chemical handling gloves?
Use PPE provided in kits for > 2L Solvent/Acid spills

## Slide 20
Bonus #2 Answer: Contact time/compatibility for gloves
Name of Chemical | Chemical Resistance Materials SDS = Recommend in SDS Blank = No Info Red = Poor/Not Recommend Orange = Fair Green = Good |  |  |  |  |  | Chemical Used in
 | Butyl | Neoprene | PVC | Nitrile | Latex | Other | 
Acetaldehyde |  |  |  |  |  |  | BADT
Acetone | SDS |  |  | 10 mins | 10 mins |  | VIR/BADT/Rad Chem
Acetonitrile |  |  |  |  |  |  | NBS
Chloroform |  |  |  |  |  |  | PARA
Ethyl Acetate |  |  |  | 8 mins |  |  | PARA/NBS
Formic Acid |  |  |  |  | SDS |  | NBS
Methanol |  |  |  | 32 mins |  |  | BADT/BT/NBS/PARA/TB
Nitric acid |  |  |  | 12 mins |  |  | Rad Chem
Phenol Liquid |  |  |  | 39 mins |  |  | BT
Sulfuric acid |  |  |  | 1.9 hrs |  |  | Rad Chem
Toluene | 6 mins |  |  | 11 mins |  | Viton >16 hrs | BADT
Xylene |  |  |  | 21 mins |  | Viton >8 hrs | BT

## Slide 21: Spill Response Determination
See Appendix E-ODHL Hazardous Chemical SOPs for compressed gases, hydrogen gas & liquid nitrogen leak responses
Section 2 of SDS, Chemical Inventory List & the label
Non-hazardous spills
Sweep up solid spill
Absorb liquid spill
Use forceps/tongs to pick up sharps

## Slide 22: Spill Response Determination (Cont’d)
“Hazardous-minor” Chemical Spill-
Hazardous-minor Spill Response (No Spill Kit)
Spill of Disinfectant; Household/office chemicals; OR
Hazardous chemical < 50 ml
Sweep up solid spill
Absorb liquid spill
Use forceps/tongs to pick up sharps

## Slide 23
Hazardous-minor Spill Response (Spill Kit Needed)
Hazardous chemicals not on Spill Flowchart; OR
High-risk chemical spill < listed volume
If solid, sweep up to place in disposal bag from the kit
Use forceps/tongs to pick up sharps
Follow Appendix F.2

## Slide 24: Hazardous-minor Spill Response (Spill Kit Needed) (Cont’d)
Warn others & evacuate all personnel
Isolate the area with ‘Chemical Spill Keep Out’ OR ‘Do Not Enter’
For spills ≥ 2 L (Follow kit’s User Directions):
BioRem-2000 Solvents
Ultimate Acid Eater Acids
Check Current Chemical Inventory

## Slide 25
Instructions from different manufacturers ‘Encircle then cover’

## Slide 26: Minor Spill Response with Spill-X Kit
Use Chemical Inventory in the spill kit & Spill-X Spill Kit Treatment Guide
-Type/size of spill Choice/amount of SPILL-X
-The Table is a list of chemicals which have been tested
by the company

## Slide 27
Remove sources of ignition if spill is flammable
Shake Spill-X agent to encircle then cover the spill
Test Spill-X-A/Spill-X-C residue pH to range 2.0-12.5
Record spill type/treatment on bag provided
Neutralized (name of acid/base); pH = ?
Adsorbed solvent: (name)
Minor Spill Response with Spill-X Kit (Cont’d)

## Slide 28
Let reaction cools, collect residue & place in
labeled bag
Decontaminate area, collect materials & gloves in the same bag
Call QA immediately to report the spill
Bonus question 3: Why?
Neutralized Acetic acid; pH 4
Minor Spill Response with Spill-X Kit (Cont’d)
To refill the kit

## Slide 29
Appendix G-Chemical Spill Report
DO NOT re-enter until approved by Supervisor
Fill out in 24 hours

## Slide 30
Thank you