## Slide 1: Safe Use of Chemical Fume Hoods CHP Appendix H
By Lai Ming Woo

## Slide 2: Why?
Engineering Control
Protects from chemical vapors, dust or radionuclides
Only when use appropriately
Safety is everyone’s responsibility
- Contact LSO if you have any concern

## Slide 3: Know Your Chemical Fume Hood
User Manuals for fume hoods/Variable Air Volume (VAV) Controller:
G:\LABORATORY PROCEDURES\Lab Equipment\User Manuals for Fume Hoods

## Slide 4: Where can you find Appendix H?
Current version of the Chemical Hygiene Plan is here:
G:\LABORATORY PROCEDURES\Safety and Security\Laboratory Chemical Hygiene Plan
Also on MediaLab

## Slide 5: Certification and Performance Checks
Certified by LCS annually
Fume Hood Controller Calibration/Hood Performance Check by Siemens annually

## Slide 6: Check Before Use
Check before EACH use
- Certification Dates within 1 year (LCS & Siemens)
- Acceptable face velocity value is 80-120 ft/min
No Audial Alarm
Green LED on Operator Display Panel
If not, IMMEDIATELY report to Supervisor
DO NOT USE until it has been repaired & within range

## Slide 7: Check Before Use (Cont’d)
Document everyday in Chemical Fume Hood Air Flow Record
95
LW

## Slide 8: Air Flow Issue?
Initials/Date in Chemical Fume Hood Air Flow Record for out of range face velocity value
- Notify Supervisor
- Supervisor will submit a maintenance request and
follow up
10/11/19 LMW

## Slide 9
Bonus Question: Why can’t You use it?
Protect you from the hazard with airflow
Low flow could cause chemical to escape into the lab

## Slide 11: CDC Fundamentals of Chemical Fume Hood Safety
Airflow, Airflow and Airflow
Work at least 6 inches from the front
Sash height the arrow (Certification Height)
Place large items on 2-3 inches’ legs
Opening/Closing sash slowly
Minimize personnel traffic past the hood
Move arms slowly perpendicular to sash

## Slide 12
Good Work Practices Video

## Slide 13: Good Work Practices
Yellow LED/Red LED with audial alarm stays on
Finish the task at hand & close sash
IMMEDIATELY report to Supervisor
Never put your head inside
Keep everything out except what you need…Clutter?
10/11/19 LMW

## Slide 14: Good Work Practices (Cont’d)
DO NOT block the back vent
Keep the hazards inside
Close sash & sliding glasses when unattended
After work, clean surfaces & close sash
Weigh fine chemical (highly toxic/reproductive toxin) or specimens ONLY with horizontal sash open to arrows
Airborne fine particulate could leak outside

## Slide 15: What’s wrong with this picture?

## Slide 16
Together We Can Do It