## Slide 1
Abbott i-STAT® System Operation

## Slide 2: Abbott i-STAT® System Operation
The following slides contain video segments for instruction on i-STAT usage.

## Slide 3: Abbott i-STAT® System Operation
CMH does NOT use glucose test strips with the i-STAT system

## Slide 4: Abbott i-STAT® System Operation
*********NOTE*********
CMH does not utilize the glucometer strip function with the i-STAT analyzers.
Use Barcode Scan for:
1. User ID (employee badge)
2. Patient ID (armband)
3. Cartridge Lot Number
4. Control Lot Number
5. External Simulator

## Slide 5: Abbott i-STAT® System Operation

## Slide 6: Abbott i-STAT® System Operation

## Slide 7: Abbott i-STAT® System Operation

## Slide 8: Abbott i-STAT® System Operation Cartridge Handling
Standard precautions must be used when handling patient specimens and quality control material
Cartridges are stored refrigerated at 2°-8°C until manufacturer’s expiration OR at room temperature for time designated on individual cartridge package (example 14 days or 2 months).
Cartridges may not be returned to refrigerator after warming to room temperature.
At temperatures < 2° C, cartridges must be discarded
At temperatures > 8° C, cartridges expire at room temp expiration.

## Slide 9: Abbott i-STAT® System Operation
The chamber in the cartridge should be filled to the blue triangle mark without spilling over the sample well.

## Slide 10: Abbott i-STAT® System Operation
For Creat, Chem8+ and Troponin testing we will be using a light green lithium heparin tube and a Saf-Evac™ device to load the cartridges.

## Slide 11: Abbott i-STAT® System Operation
*********NOTE********
For CMH i-STAT analyzers, you may be prompted to enter the user ID, cartridge information and patient ID or quality control information BEFORE inserting the cartridge.
Follow the prompts on the analyzer.

## Slide 12: Abbott i-STAT® System Operation NOTES:
Patient identification is obtained by scanning the patient’s armband where applicable.
For Troponin cartridges, a Chem8+ cartridge must be run first to screen for hemolyzed specimens. (Hemolysis will cause an increase in potassium and a decrease in troponin.)
Analyzers must be cleaned between patients with a Super-Sanicloth.
Printed results from the i-STAT1 printer are not acceptable as a permanent chartable record. The results are printed on heat sensitive paper and will fade with time.

## Slide 13: Abbott i-STAT® System Operation NOTES:
An internal electronic simulator automatically runs every 8 hours to determine if the analyzer is working properly.

## Slide 14: Abbott i-STAT® Quality Control
ACT Controls
CHEM8+ Controls
Troponin Controls
ABG, Creat Controls

## Slide 15: Abbott i-STAT® Quality Control
Liquid Quality Control is required in the following intervals:
  CHEM8+, Crea, Troponin:
    Monthly
    With each new lot/shipment
  ABG and ACT:
    Every 8 hours during times of testing
    With each new lot/shipment