## Slide 1: Recap
Anti-A | Anti-B | Anti-D | Control | Ac | Bc
4+ | 0 | 0 | 0 | 0 | 2+
Anti-A | Anti-B | Anti-D | Control | Ac | Bc
0 | 0 | 3+ | 0 | 4+ | 3+
Anti-A | Anti-B | Anti-D | Control | Ac | Bc
0 | 4+ | 3+ | 0 | 4+ | 0
Anti-A | Anti-B | Anti-D | Control | Ac | Bc
4+ | 4+ | 4+ | 4+ | 0 | 0

## Slide 2
Agglutination Testing and Antibody Detection
Max Louzon, MLS(ASCP)CM

## Slide 3: Objectives
Describe the indirect antiglobulin test and its role in unexpected red cell antibody detection
Describe the process of performing an antibody screen using tube, gel and solid phase techniques
Outline the steps for producing antihuman globulin
Define the terms unexpected antibody and clinically significant antibody.

## Slide 4: Objectives (cont.)
List causes of red cell alloimmunization
Identify potentiators used in antibody detection testing
Define prozone, equivalence, postzone
Discuss the purpose of IgG coated red cells in antiglobulin testing
List limitations of antibody detection techniques
Differentiate the stages of agglutination
Recognize the differences between a direct antiglobulin test and an indirect antiglobulin test

## Slide 5: History
Notes: Early research based on IgM and immediately visible agglutination. 1908 Moreschi first described the principle. 1945 Robin Coombs, Race, and Mourant outlined the procedure. Test is occasionally referred to as the Coombs test. AHG is made by injecting rabbits with human IgG

## Slide 6
Expected Antibodies
Clinically Significant Antibodies
Notes: IATs detect unexpected IgG antibodies. These can lead to hemolysis and reduced RBC survival. These originate through antigen exposure (transfusion, pregnancy) disease state, drugs, chemcials or parasites

## Slide 7: IgM, IgG and RBCs
Harmening DM
Modern blood Banking and
Transfusion Medicine, 5th ed

## Slide 8: AHG Antisera
Picture from bio-rad.com
Notes: AHG can be monoclonal or polyclonal. Directed towards immunoglobulins or complement system. Originally produced from animals; labs made their own. Now commercially made and purchased

## Slide 9: AHG Reaction

## Slide 10: Potentiators
Temperature
Time
Medium
Concentration
pH
Enzymes (?)

## Slide 11: Prozone, Equivalence, Postzone

## Slide 12: Zeta Potential

## Slide 13: Enhancement
Standard saline incubation 37C – 30-60 min
LISS – Low Ionic Strength Saline
  0.2% saline
  Decreases negative repulsion (Zeta Potential)
  Decreases incubation time to 5-15 min
22% Albumin
  Also decreases zeta potential
  Incubation time 15-60 min

## Slide 14: Enhancement (cont.)
PEG – Polyethylene Glycol
  Decreases water between RBCs
  Decreased hydrophobic repulsive force
  Brings cells closer together
  Incubation time at 37C is 10-30 min

## Slide 15: Indirect Antiglobulin Test Principle
Central question for IATs: does this patient have antibodies to antigens present on red blood cells?
Notes: Patient sample is the unknown while the screening cells are the known. If antibodies are present, cells will be sensitized. This is an in vitro test and does not reflect patient status.

## Slide 16: Tube Method
Patient plasma is incubated with screening cells in an enhancement media
Cells are than washed to removed excess IgG
AHG is added and sample is centrifuged
Test is positive if cells agglutinate
If no agglutination is seen, check cells are added and should agglutinate upon centrifugation
  Check cells are sensitized RBCs

## Slide 17: Was this a good wash?

## Slide 19: Check Cells
Also known as control cells, Coombs cells
RBCs coated with IgG antibody
  Usually Rh pos RBC coated with anti-D
  Also available in RBCs coated with C3
They are added to every AHG reaction tube with a negative result
  They are a guard against false negatives
    Bad washing, no AHG added

## Slide 20: Check Cells (cont.)
Mixed field appearance
  Checks will agglutinate, screening cells will not
  Two different cell populations
Test is valid if CC agglutinate
If CC do not agglutinate
  Bad washing
  No AHG added
  Test is invalid and must be repeated

## Slide 21: Tube Grading

## Slide 22: Tube Method Pros and Cons
Pro
  Gold standard
  Inexpensive
  Flexible
Con
  Labor intensive
  Not stable

## Slide 23: Gel
Patient plasma, LISS and screening cells are incubated in a microtube
Microtube is filled with gel which is laced with AHG
If cells are sensitized, red cells will be held in gel, otherwise will form pellet at bottom

## Slide 24
Ortho Clinical Diagnostics
Raritan, NJ 10/01

## Slide 25: Gel Pros and Cons
Pro
  Smaller sample size
  No cell washing step
  Clear, stable endpoint
  Sensitivity comparable
  Can be automated
Con
  Expensive
  More false positive

## Slide 26: Solid Phase
Patient plasma, LISS and screening cells added to microtiter well lined with Protein A which has a high affinity for Fc portion of AHG and incubated.
Wash
AHG added
Centrifugation
Graded via computer system.
Positive will show as cells lining entire well

## Slide 27: Solid Phase Grading
Immucor Gamma
Norcross, GA 5/02

## Slide 28: Solid Phase Pros and Cons
Pro
  Reduced volume needed
  Increased sensitivity
  Less technique needed
Con
  Learning curve
  Expensive
  Reagent expiration

## Slide 29: Situations

## Slide 30: Direct Antiglobulin Test Principle
Central question for DATs : does this patient have antibodies or complement already stuck to their red cells?
Test Procedure: Washed patient red blood cells + AHG
http://www.pathologystudent.com/?p=1003
Notes: Historically known as a direct Coombs test. When would this be positive?