## Slide 1: EVALUATE A POSITIVE DIRECT ANTIGLOBULIN TEST (DAT)
DAT results with:
  Polyspecific AHG
  Anti-IgG
  Anti-C3
  Control
Is the antibody screen positive?
Is the antibody auto or allo?
  Perform elution

## Slide 2: EVALUATE CLINICAL HISTORY
Diagnosis
Medications
Transfusions

## Slide 3: WHY PERFORM ELUTIONS?
Mostly used in the investigation of a positive DAT caused by:
  hemolytic disease of the fetus and newborn (HDFN)
  hemolytic transfusion reaction (HTR)
  hemolytic anemia (immune or drug-induced)

## Slide 4: COMBINED ADSORPTION-ELUTION
When used in combination with an in-vitro adsorption technique, elution procedures are also used to:
  detect weakly expressed antigens
  isolate a specific antibody from multiple antibody specificities in a single specimen
  purify and concentrate blood group antibodies

## Slide 5: PARTIAL ELUTION
This technique dissociates bound immunoglobulin from red blood cells without impairing surface antigen reactivity, thus allowing antigen typing with antisera that require the indirect antiglobulin test. This aids in the identification of any underlying alloantibodies in patients with warm-reactive autoantibodies.

## Slide 6: RED CELLS SENSITIZED BY ABO ANTIBODIES
Possible sources of ABO antibodies coating red cells include:
  Non-ABO-type-specific plasma-containing products
  Maternally derived ABO antibody
  IVIG and other IV medications derived from pooled human plasma
  Passenger lymphocytes of donor origin from peripheral stem cell and solid organ transplants

## Slide 7: ELUTION TECHNIQUES
Elution is a procedure that involves the removal of antibody from coated red cells and its recovery for identification by serological techniques.
Alteration of thermodynamics, membrane structure and reversal of binding forces between red cell antigens and the coating antibody causes the dissociation of the antibody from the red cells.

## Slide 8: ELUTION TECHNIQUES
Methods include:
  1. Alteration in temperature
    Heat
      investigation of ABO HDFN
      detection of weak A and B antigens on RBCs
    Freeze-thaw
      Investigation of ABO HDFN
      detection of weak A and B antigens on RBCs

## Slide 9: ELUTION TECHNIQUES
  2. Chemical
    ZZAP (partial elution)
      Used to remove bound autoantibody in order to free antigen sites for use in autoadsorption
      RBCs cannot be used for typing Kell, Duffy and MNSs antigens. Rh antigens are enhanced.
    Chloroquine diphosphate (partial elution)
      Used to remove bound autoantibody
      Will not destroy RBC antigens
      RBCs can be antigen typed (Rh antigens may be weakened after treatment)

## Slide 10: ELUTION TECHNIQUES
  3. Organic solvents – rarely used
    Lipids in the red cell membrane are dissolved by the solvent and antibody dissociation occur as a result
    Also used to decrease surface tension and disrupt the binding forces that hold antigen and antibody together
    Solvents used include ether, xylene, chloroform and dichloromethane (DCM)

## Slide 11: ELUTION TECHNIQUES
  4. Alteration of pH
    Antibody attachment to RBCs is dependent on many factors, pH being one of them (normal range is pH 6.5-7.5)
    By lowering the pH (acidification to pH 3.0), the structural complementarity between antigen and antibody is lost resulting in antibody dissociation.
      Gamma ELU-KIT II utilizes total elution of bound immunoglobulin from intact red blood cells by the addition of a low pH solution to dissociate the antibodies. The recovered eluate is then adjusted to pH 7.0 ± 0.5 by adding a buffering solution. The deposited red cells cannot be used for antigen typing.

## Slide 12: ELUTION TECHNIQUES
      Gamma EGA Kit utilizes partial elution to dissociate bound immunoglobulin from intact red blood cells. RBCs are briefly suspended in acid solution to dissociate bound antibody, and then immediately brought to a neutral pH by the addition of a buffer.
        This procedure renders DAT-positive RBCs DAT-negative so treated RBCs can be further antigen typed or used in serological testing.
        Note: Antigens of the Kell blood group system are destroyed by this treatment.

## Slide 13: GAMMA ELU-KIT™ II

## Slide 14: GAMMA ELU-KIT™ II
Preparation of Working Wash Solution
  Label a wash bottle with lot number, preparation date and expiration date of the concentrated wash solution.
  Add the entire bottle of concentrated wash solution to the wash bottle and fill to the 500 ml mark with reagent-grade water (1 volume concentrated wash to 9 volumes water).
  Mix well and store at 1-10C.
  Do not use beyond expiration date of concentrated wash.
  Do not use if it shows marked turbidity and is causing hemolysis of the red cells.

## Slide 15: GAMMA ELU-KIT™ II
Washing Before Eluting
  The sensitized RBCs must be washed THOROUGHLY before performing the elution procedure.
  This is achieved by washing once with isotonic saline and an additional four times with cold working wash solution. The purpose of the cold working wash solution is to minimize antibody dissociation.
  Reserve an aliquot of the last wash as a control.
  If serum contains a high-titer antibody, additional washes may be needed.
  Thorough washing ensures that the antibody recovered in the eluate is derived from the RBC membrane and does not represent unbound antibody from serum or plasma due to inadequate washing.

## Slide 16: GAMMA ELU-KIT™ II
Testing the Last Wash
  To determine the efficacy of the washing process, an aliquot from the last wash phase should be tested for antibody activity and should be non-reactive.
  If antibody activity is detected, additional washes will be required before proceeding to eluate preparation.

## Slide 17: GAMMA ELU-KIT™ II
Preparation of Eluate
  Transfer 1 ml (20 large drops) of washed packed cells to a CLEAN glass tube.
  Add 20 drops (or an equal volume, since the volumes delivered in a dropwise fashion might not be exact) of eluting solution and mix GENTLY by inverting the tube four times. Adjust accordingly if less than 20 drops of packed red cells is available.
  Centrifuge IMMEDIATELY for 45-60 seconds at 3400 rpm. Prolonged immersion of the cells in the eluting solution will cause the cells to hemolyse.
  Transfer the supernatant to a CLEAN glass tube.

## Slide 18: GAMMA ELU-KIT™ II
Preparation of Eluate (cont.)
  Add buffering solution drop by drop until a pale blue color appears and persists after mixing.
  Note: Excessive buffering solution may result in dilution of antibody in the eluate.
  Centrifuge to remove precipitate and cellular debris.
  Transfer to another CLEAN tube and repeat if debris is still visible in the eluate.
  The presence of a blue indicator in the buffering solution aids in the determination of whether the eluate has been adjusted to the appropriate neutral pH. Do not use if the buffering solution is not blue.
  Transfer eluate to a CLEAN properly labeled tube.

## Slide 19: GAMMA ELU-KIT™ II
Testing the Eluate
  Due to the limited amount of eluate available, panel cells should be selected based on antibody/antibodies identified in the plasma and on the patient’s phenotype, if available.
  If the panel is non-reactive, A and B cells should also be included in the testing of the eluate and last wash if patient is non-group-O and was transfused with plasma products containing anti-A and/or anti-B.
  Only IgG antibodies will be recovered in the elution procedure. It is not necessary to rule out IgM antibodies during antibody identification unless otherwise instructed by the Transfusion Service Medical Director or Manager.

## Slide 20: TECHNICAL FACTORS AFFECTING ELUTION
Incorrect technique
  Failure to restore the pH of the eluate to neutral. This may cause hemolysis of reagent cells used for testing or may inhibit antibody activity.
  Addition of excessive buffering solution resulting in the dilution of antibody present in eluate.
  Cellular debris not completely removed from eluate. This may interfere with the results of subsequent testing.

## Slide 21: TECHNICAL FACTORS AFFECTING ELUTION
Incomplete washing
  Last wash should be tested to ensure no antibody activity.
  Antibody activity in the last wash indicates that there is contaminating free unbound serum antibody.
Binding of protein to glass
  Antibodies can be adsorbed nonspecifically on to the surface of a glass test tube during the washing process and may dissociate from the glass during the elution procedure.
  To avoid this contamination, transfer the washed red cells to a clean glass tube before starting the elution procedure.

## Slide 22: TECHNICAL FACTORS AFFECTING ELUTION
Dissociation of antibody before elution
  Some antibodies, especially low affinity IgG antibodies, may spontaneously dissociate from the red cells during the wash phase.
  To minimize this dissociation, wash with cold (1 - 10C) working wash solution.

## Slide 23: PERFORMANCE LIMITATIONS
A number of factors affect the yield of antibody obtained from an elution procedure:
  The amount of antibody bound to the cells
  The degree of dissociation that occurs during the wash phase
  The degree of recombination of antibody that occurs before the eluate is separated from the cells – minimal
  The degree to which immunoglobulin is denatured by the low pH during dissociation
  RBCs having a positive DAT due to bound complement alone will usually yield an eluate showing no antibody activity
  In drug-induced hemolytic anemias, the eluate will show no antibody activity
  Age of sample