## Slide 1: Tango Infinity
Instrument Hazards
By: Brennan Katchatag MT (ASCP)
July 2017
Notes: This powerpoint is designed for awareness of the potential hazards present with the Tango Infinity after conducting an instrument hazard analysis.

## Slide 2: Chemicals Used
Please review all MSDS and package inserts for chemicals used by the Infinity including:
  Bromelin
  LISS
  AHG
  Microcide

## Slide 3: Hazards Identified
Biohazard Exposure
Eye Tissue Damage
Moving Instrument Parts
Earthquake Hazard
Electrical Hazard

## Slide 4: Biohazard Exposure
Test Samples
  Pathogenic Viruses such as HBV, HIV, HCV, etc.
Instrument Liquid Waste
  High volume of biological waste
Instrument Solid Waste
  High volume of contaminated test strips
Notes: Always wear appropriate laboratory personal protective equipment while performing patient testing or instrument maintenance. Examples include donning of lab coat, disposable gloves, eye wear or face shield. Use PPE, compliance with applicable policies and procedures regarding biohazardous materials should minimize any potential biohazardous exposures.

## Slide 5: Eye Tissue Damage
Laser Beam Light Hazard
  Laser beam lights when directed to your eyes can cause serious or permanent eye tissue damage
  Observe any precautionary signs indicated on the instrument where potential laser light hazards are present
Notes: There should not be direct access to the laser lights used to read barcode labels, just be aware of their presence while performing patient testing or instrument maintenance.

## Slide 6: Moving Instrument Parts
Crush injuries may occur while closing instrument compartments or covers or by moving instrument parts
Observe any precautionary signs indicated on the instrument where potential crush injury is present
Avoid opening the main instrument cover while instrument is in operation
Notes: The Tango Infinity has an improved design in that the instrument operator will not be exposed to any moving instrument parts, unlike the Tango Optimo.
In addition, there is “Kill Switch” technology designed to stop instrument movements when the main instrument cover is opened during instrument operations.
The instrument hinge covers are designed not to slam shut, if you suspect wear and tear of these parts request for repair.

## Slide 7: Earthquake Hazard
The potential for displacement of instrument during an earthquake is present
Be aware of engineering controls designed to mitigate movement of instrument
Notes: The Tango Infinity has an instrument table designed for its use. It is constructed to be less than 4 feet tall with wheel brakes, please ensure that the wheel brakes are in the locked position while the instrument is stationary. In addition, the feet of the instrument are rubberized to resist movement on the table. In the event of an earthquake, leave the immediate area of the instrument to avoid any potential crush injuries while the ground is in motion.

## Slide 8: Electrical Hazard
Electrical shock injury is present when the instrument is connected to an electrical outlet or source
Be aware of any potential electrical hazards while in the vicinity or operation of the instrument
Notes: The Tango Infinity poses an electrical hazard as with any instrumentation or device requiring electric power. Engineering controls and plans are designed to minimize electric shock injury. All instruments should be inspected for electrical current leakage and ground integrity before initial use, after major repair or modification, or if problems are suspected. Report any damaged equipment or electrical outlets, unusually hot equipment, frayed electrical cords, and even minor shocks to management for further evaluation. Follow policies and procedures provided regarding electrical safety.

## Slide 9: Conclusion
Be aware of the potential risks while operating the Tango Infinity, further information should be provided in the operating manual
Follow all policies and procedures provided regarding hazards potentially present in the workplace
If you have further questions or concerns regarding the mentioned hazards, direct them to your lead or manager
Notes: The Tango Infinity operator manual should be able to list any potential risks while operating the instrument, refer to it for further information.
Follow all policies and procedures provided to you to minimize exposure to hazards in the workplace, a good resource available to you is the Accident Prevention Program and Exposure Control Plan in the Workplace Safety Manual.