## Slide 1: The BAD,BMT and PAS
Identifying the BMT patient
and their needs

## Slide 2: Changes to BMT Pt comments
With implementation of interfaced orders, use of PAS and the ability to add specific Rh types to the patient’s Sunquest Blood Bank Adminstrative Data (BAD) file record, we will be making changes to the comments entered in SQ for BMT patients.

## Slide 3: SCCA BMT Reduced Volume Platelet Requirements
Platelets with plasma that is ABO incompatible to the recipient require volume reduction to 100 mL
SCCA has agreed that full volume PAS platelet is an appropriate substitute for volume reduced ABO plasma incompatible platelets
The reduced volume comments will be changed as follows:
Current Comment | New Comment
RV out of group PLT | RV out of group PLT or PAS
RV PLT A/O | RV PLT A/O or PAS
RV PLT B/O | RV PLT B/O or PAS
RV PLT A/B/O | RV PLT A/B/O or PAS

## Slide 4: Interpreting comments for platelets
New Comment | What type of platelet is acceptable
RV out of group PLT or PAS | Any ABO full volume PAS Platelets Full volume ABO plasma compatible platelets in plasma Reduced volume ABO plasma incompatible platelets in plasma
RV PLT A/O or PAS | Any ABO full volume PAS Platelets Full volume B/AB platelets in plasma Reduced volume A/O platelets in plasma
RV PLT B/O or PAS | Any ABO full volume PAS Platelets Full volume A/AB platelets in plasma Reduced volume B/O platelets in plasma
RV PLT A/B/O or PAS | Any ABO full volume PAS Platelets Full volume AB platelets in plasma Reduced volume A/B/O platelets in plasma

## Slide 5: Identifying BMT patients before the transplant information is entered in SQ
The acronym BMT will be added to the beginning of the platelet comments to help identify pre-transplant
Pre-BMT patient:
  EXAMPLE: BMT RV PLT A/O or PAS
When the patient is group O, only BMT will be added to the comments filed
The ABO type of RBC and plasma will no longer be entered in the comment field. The ABO group of RBC and plasma is determined by the permanent BAD file and test results ABO
Post-BMT patient:
The type of transplant, date, recipient ABO/Rh and donor ABO/Rh will still be entered in the SQ comment field
  EXAMPLES: ALLO TX. 5/12/18: REC APOS/DONOR BPOS
  AUTO TX. 6/15/18

## Slide 6: ABO Group of RBC and Plasma Compatible for the Post BMT Patient
Acceptable RBC and plasma ABO will no longer be entered in the comments field (Yea!)
That said, the following apply…….
  Group AB BMT patients should be provided group O RBCs
    You will start seeing NTD added to the BAD file to help remember to allocate & issue only group O RBCs

## Slide 7: NTD – what does this mean
NTD may be used as:
  Interpretation of an ABO/Rh test when there is a discrepancy as in the case of a post ABO incompatible transplant
  Entered as a historical BAD file ABO for a patient requiring the issue of group O positive RBCs – Nina or Christine will change the BAD file to NTD when notified of an incompatible BMT

## Slide 8: NTD POS & NTD NEG – what does this mean
NTD POS and NTD NEG may not be used as a test interpretation!
This two interpretations may only be utilized for the patient’s historical ABO/Rh in the BAD file.
NTD = ABO
POS & NEG = Rh type
-The ability to add the Rh type along with NTD, provides a hardstop if attempting to issue a Rh positive platelet to an Rh negative patient.
If you receive an QA failure when trying to allocate or issue a blood component, you need to stop and read the QA failure carefully. Do not assume!
You needto be 100% sure you understand why you know why you are overriding a hardstop before overriding it. The reason for overriding must address the actual failure.
Be sure you know if you are overriding an ABO hardstop (NTD = ABO) or an Rh hardstop (POS or NEG).

## Slide 9: Is there a standard protocol for entering comments? Yes!
Recipient | Pre Transplant Comment | Donor | BAD File | Post Transplant Comment
A | BMT: RV PLT B/O or PAS | A | A | Allo TX 3/27/17: Rec APOS/Donor APOS
 |  |  |  | BMT: RV PLT B/O or PAS
 |  | B | NTD | Allo TX 3/27/17: Rec APOS/Donor BPOS
 |  |  |  | BMT: RV PLT A/B/O or PAS
 |  | O | NTD | Allo TX 3/27/17: Recip APOS/Donor OPOS
 |  |  |  | BMT: RV PLT B/O or PAS
 |  | AB | NTD | Allo TX 3/27/17: Recip APOS/Donor ABPOS
 |  |  |  | BMT: RV PLT A/B/O or PAS
B | BMT: RV PLT A/O or PAS | A | NTD | Allo TX 3/27/17: Recip BPOS/Donor APOS
 |  |  |  | BMT: RV PLT A/B/O or PAS
 |  | B | B | Allo TX 3/27/17: Recip BPOS/Donor BPOS
 |  |  |  | BMT: RV PLT A/O or PAS
 |  | O | NTD | Allo TX 3/27/17: Recip BPOS/Donor OPOS
 |  |  |  | BMT: RV PLT A/O or PAS
 |  | AB | NTD | Allo TX 3/27/17: Recip BPOS/Donor ABPOS
 |  |  |  | BMT: PAS or RV PLT A/B/O
O | BMT | A | NTD | Allo TX 3/27/17: Recip OPOS/Donor APOS
 |  |  |  | BMT: RV PLT B/O or PAS
 |  | B | NTD | Allo TX 3/27/17: Recip OPOS/Donor BPOS
 |  |  |  | BMT: RV PLT A/O or PAS
 |  | O | O | Allo TX 3/27/17: Recip OPOS/Donor OPOS
 |  |  |  | BMT
 |  | AB | NTD | Allo TX 3/27/17: Recip OPOS/Donor ABPOS
 |  |  |  | BMT: RV PLT A/B/O or PAS
AB | BMT: RV PLT A/B/O or PAS (Convert BAD file to NTD) | A | NTD | Allo TX 3/27/17: Recip ABPOS/Donor APOS
 |  |  |  | BMT: RV PLT A/B/O or PAS
 |  | B | NTD | Allo TX 3/27/17: Recip ABPOS/Donor BPOS
 |  |  |  | BMT: RV PLT A/B/O or PAS
 |  | O | NTD | Allo TX 3/27/17: Recip ABPOS/Donor OPOS
 |  |  |  | BMT: RV PLT A/B/O or PAS
 |  | AB | NTD | Allo TX 3/27/17: Recip ABPOS/Donor ABPOS
 |  |  |  | BMT: RV PLT A/B/O or PAS
Any type | As above | > 2 types not identical to recipient | NTD | Allo TX: 3/27/17: Recipient X/Donor X&X
 |  |  |  | BMT: RV PLT A/B/O or PAS
Rh POS | NA | Rh NEG | NEG | NA
 |  | Rh POS | POS | NA
Rh NEG | Give Rh NEG | Rh NEG | NEG | NA
 |  | Rh POS | POS | NA
Example comment for Rh NEG requirement - BMT: Give Rh NEG: PAS or RV PLT B/O |  |  |  | 
NTD can only receive O RBC and AB plasma. |  |  |  | 
Pre-transplant AB patients will be converted to NTD after testing and receiving attribute form. |  |  |  | 
Currently, there is still work going on for streamlining the process of notifying the Blood Bank when a patient becomes a BMT candidate followed by the date of transplant and the donor type.
At some point in the future, their will be an SOP covering the process and this protocol. Until that time, Nina and Christine will continue updating the patient’s BAD file per this protocol.

## Slide 10: Be Aware!
Patient records will include comments in both the former and new comments.
  In the near future, the current NTD BAD file ABO’s of BMT patients will be updated to NTD POS or NTD NEG
  Platelet comments and RBC/plasma comments will continue to be in both formats for some time. If you get an order and it would be helpful to update the comments to the new format, bring the order to Christine or Nina and they will be happy to make the update if appropriate.