## Slide 2: ANNUAL SAFETY BRIEF
Lab General
Fire Safety
Electrical Safety
Biological Hazards
Biological Safety Cabinets
Compressed Gases
Radiation Safety
Chemical Hazards
Chemical Hygiene
HAZCOM
TB Exposure
Lab/Regulated waste Disposal
Hazardous Waste reduction
Accident Reporting
Internal/External Disaster Preparedness
Evacuation Plan
Latex Precaution
Shipping Infectious Substances
Lab Ergonomics
Formaldehyde Program
Noise Exposure

## Slide 3: Lab General
Personal Safety
  Safe environment for patients as well as personnel
  Report hazards and accidents to supervisors
  Follow policies and procedures
  Recommend improvements to provide a safer environment

## Slide 4: Lab General
Personal Safety
  No Smoking
    Designated areas only
  Eating and Drinking
    Prohibited in work areas
    Food and beverage not allowed in laboratory refrigerators or freezers
  Application of cosmetics
    Application of cosmetic/lip balm or contacts are prohibited in the work area.
  Hair/beard jewelry
    Hair/beards must be neat and can not come in contact with contaminated materials or equipment. Do not wear jewelry that can be caught in equipment or hang in infectious material

## Slide 5: Lab General
Personal Safety
  Specimens
    Are potentially infectious.
    Handle appropriately
    Place specimens in containers that prevents leakage during collection, handling, processing, storage transport or shipping.

## Slide 6: Lab General
Protective Wear
  Full Face Shield
  Clothing (Lab coat)
  Shoes
  Gloves
  Respirators

## Slide 7: Lab General
Frequent Hand Washing
  Wash all surfaces of hands and wrists for at least 20 seconds
  Rinse, blot dry w/paper towels
  Turn off faucet with paper towels
NO Mouth Pipetting
Aisles and Exits
  Do Not Block Aisles and Exits
  Do not cover or block Fire extinguishers/alarms, safety showers/eyewash stations

## Slide 8: Lab General
Standard /Universal Precautions
  Memorandum IC-001, “Precaution for infection Control”
House keeping
  Accidental spills clean up immediately with approved disinfectant
  All Blood/Body fluid, Microbiology and tissue waste must be placed in Red Biohazard Bags

## Slide 9: Lab General
Laboratory Equipment
  Glassware
    Do not use if broken or chipped
    Don’t leave pipettes in bottle/flask/breaker
    Hot glassware-handle with protective gloves
    Handle broken glassware with mechanical devices

## Slide 10: Lab General
Laboratory Equipment
  Centrifuges
    Never operate with cover open
    Specimens must have lids
    If breakage occurs-allow aerosols to settle before cleaning
    Maintain rotor balance when centrifuging sample.

## Slide 11: Lab General
Laboratory Equipment
  Autoclaves
    Do not open until temp and pressure have returned to ambient
    Use insulated water repellent gloves and aprons when loading and unloading autoclave

## Slide 12: Lab General
Contaminated Needle Disposal
  Do not
    Cut
    Bend
    Break
    Detach from syringe or needle holders (except for blood transfer devices)
    Manipulated by hand in any way
  Dispose syringes/holders with needles.
  Lancets and other blood letting devices are to be used once and appropriately discarded

## Slide 13: Lab General
Emergency Equipment
  Emergency Showers
    Located in:
      Histology
      Microbiology
  Eye Wash Stations
    Located in:
      Histology
      Chemistry
      Morgue
      Microbiology
      Hematology
    Flush eyes for 15 minutes or longer
  Eye Wash Bottles
    Located in:
      Central Accessioning
      Blood Bank
      Special Chemistry

## Slide 14: Lab General
Warning Signs
  Must be posted in areas of hazardous substances
    Areas
    Storage cabinets
    Refrigerators
    Shipping containers
  Technical areas are considered a “Moderate Risk”
    No visitors may enter the work area
    Must have approval of the Chief pathologist and Clinical Lab Manager

## Slide 15: FIRE SAFETY
Fire Emergency Plan
  Notify everyone in immediate area by saying “CODE RED”
  R.A.C.E.
    Rescue
      Remove those in immediate danger
    Alarm
      Pull the nearest fire alarm
      Call 3333 give exact location of the fire
    Contain
      Confine by closing doors
    Extinguish/Evacuate
      Extinguish with fire extinguisher if possible, if not evacuate
      Assist others
      Do not use elevators
Call
3333

## Slide 16: FIRE SAFETY
Fire Alarm
  When alarm sounds
    Listen for location, location will be announced as an overhead page.
    Close door if fire in in the main Hospital building or the Research building
    If fire is in the immediate area or if smoke is sighted. Evacuate
    Evacuation routes are posted in each section/Supervisor will be responsible for assuring everyone has been evacuated
    If the Fire is located in a different fire zone (East side) Be alert to the possibility that the fire may spread to our area. BE PREPARED TO EVACUATE.

## Slide 17: FIRE SAFETY
Fire Drill (Quarterly/Each Shift)
  When alarm sounds, Code RED is announced or condition warrants
    Follow the fire drill procedures
    Certain personnel will be allowed to stay (determined by supervisor)
    Section supervisor or designee will assure that all personnel have evacuated

## Slide 18: FIRE SAFETY
Fire Prevention
  Flammable mixture and open flames don’t mix.
  Flammables must be properly contained. No more than a gallon may be out in a section.
  Use carriers when transporting.
  Items must be 18” from ceiling.

## Slide 19: FIRE SAFETY
Fire Prevention Training
  RACE
    Rescue
    Alarm
    Contain
    Extinguish/Evacuate
  PASS
      Pull Pin
      Aim
      Squeeze
      Sweep

## Slide 20: ELECTRICAL SAFETY
  All Electrical shocks (including small tingles) must be reported.
    Power off/Unplug instrument.
    Do not try to use or repair
    Instruments must be repaired by qualified personnel
    Building electrical will be repaired by the Engineering Department

## Slide 21: ELECTRICAL SAFETY
  Extension cords
    Will be avoided if possible
    Should be temporary, non-repetitive situations.
    Should have same size wiring as the instrument/Appliance.
    Should not be in the path of a walkway
    Must be in good condition and have proper grounding wires.

## Slide 22: BIOLOGICAL HAZARDS
  Disposal Containers
    Sharps containers
      Needles, scalpels or other rigid sharp items that may cause a puncture wound or cut
      All sharps whether contaminated or not should be placed in Sharps container
    Rigid-Sided leak proof infectious waste receptacles
      Used for collection of broken glass, tubes of blood, liquid specimens and cultured media
    Infectious waste bags.
      Should be double bagged and used for waste with no risk of puncturing the outer layer of the bag.

## Slide 23: BIOLOGICAL HAZARDS
  Disposal Containers
    All containers for incineration are colored RED and have the Biohazard symbol on the container
  Glassware
    Glassware that is to be reuse, must be steam sterilized (autoclaved).
  Hand washing and use of alcohol hand sanitizer should be done frequently throughout the day.

## Slide 24: BIOLOGICAL HAZARDS
  No open specimens in the centrifuge, must be capped to prevent aerosol droplets.
  Clean work areas.
  Grossly contaminated specimens will not be processed-notify delivery person, contact physician
  Dispose sample cups and containers in the infectious waste containers.

## Slide 25: BIOLOGICAL SAFETY CABINETS
  Process any suspicious pathogenic patient specimens (Mycobacterium) in the Biological Safety Cabinet.
    During the processing of TB/Fungus, allow no other person in the room – Lock the door
    Disinfect work area with Tuberculocidal disinfectant
    UV germicidal lights will be left on overnight after use of hood.
    Centrifuge of mycobacteria, must have double containment.

## Slide 26: COMPRESSED GASES
  General
    Cylinders must be secured in an upright position
    Valve safety covers will be left on until tanks are secured and regulators attached.
    Valve safety covers will be replace when regulators are remove and during transport.
    Hand trucks will be used to transport cylinders.
    Do not oil or grease regulators
    Do not attempt to repair or force tank valves open.

## Slide 27: COMPRESSED GASES
  Pressure Regulator and Valves
    Do not interchange valves.
    Threads should be clean and tightly fitted, do not lubricate the valves.
    Use proper size wrench to tighten.
    Open valves slowly.
    Do not force frozen valves.

## Slide 28: COMPRESSED GASES
  Acceptance and Return of Cylinders
    Cylinder lacking permanent ID will not be accepted.
    New Tanks should be marked as “FULL” upon receipt
    Empty tanks must be label “EMPTY”, secured upright with cap replaced.

## Slide 29: RADIATION SAFETY
  Operational Checks performed by Blood Bank
    Leak test every 6 months by Medical Center Radiation Safety Officer
    Measurement of dose determination checked annually be BB Supervisor
    Area is monitored weekly for irradiation leak with a Geiger counter by BB Personnel

## Slide 30: RADIATION SAFETY
  Blood Irradiator
    A pocket dosimeter is not required to be worn when working with the blood irradiator; however one maybe requested from the Hospital Radiation Safety Officer if an employee would like to wear one or is pregnant
    Door to irradiator room must be kept locked with alarm armed 24/7
    Room is under camera surveillance by VA police
    When irradiator is in use the RED RADIATION light must be turned on.
    Any malfunction needs to be reported to the Hospital Radiation Safety Officer Immediately (ext 3440/page 13-224)
    The Wanrad-2 Gamma Radiation Alarm will sound an alarm if readings are >5mR/hr-Notify Hospital Radiation Safety Officer Immediately!

## Slide 31: CHEMICAL HAZARDS
  Corrosives-Acids, Anhydrides, Alkalis, Dehydrating agent, Oxidizing agents
    Can damage equipment
    Storage
    May cause burns on skin, mouth or eyes
      Store in approve containers
      Store in cool dry place, well ventilated, away from direct sunlight
      Segregate acids form bases
      Never store above eye level
      Working quantities may be stored under sinks, bulk storage in approved acid cabinets
      Carriers must be use when handling bottles of acid greater then 500mls

## Slide 32: CHEMICAL HAZARDS
  Corrosives
    Handling
      Use a shield barrier or work in a sink (spill can be controlled).
      Wear a protective apron, gloves and eyewear.
      Do not sniff reagents.
      Diluting Acid into water like you ought to!
      Must use carriers for containers with more than 500ml.

## Slide 33: CHEMICAL HAZARDS
  Toxic Substances-Poisons, Irritants, Asphyxiates
    Do not react with human tissue
    They may be sensitizers that produce cytotoxic effect resulting in skin irritation or illicit an allergic reaction.
  Storage
    Store in cool dry place, well ventilated, away from direct sunlight and any fire hazards
    Segregate toxic chemicals form acids and oxidizing agents
    Containers should be sealed as tightly as possible.

## Slide 34: CHEMICAL HAZARDS
  Toxic Substances
    Handling
      Wear protective apron, glove, and eyewear
      Use fume hoods
      Wash glassware, work area and hands thoroughly
      Exposure to the sensitizer formaldehyde is monitored as least annually by the Medical Center’s Safety Manager.

## Slide 35: CHEMICAL HAZARDS
  Carcinogen Substances
    Chemicals capable of causing cancer. (will be discussed in later section)

## Slide 36: CHEMICAL HAZARDS
  Ignitable
    Chemicals that can burn, combustible/flammable
    Handling
      Use approved metal can for volumes of 1 quart or more.
      Glass containers use a protective carrier for transport.
      Eliminate all sources of ignition from the flammable area.

## Slide 37: CHEMICAL HAZARDS
  Explosives
    Reactive an unstable substances
    that readily undergo violent chemical change
  Cryogenics
    Fluids(liquefied gases) or solids characterized by extreme low temperatures such as Dry ice
    Handling
      Handle in well ventilated area, can cause light headedness and extreme cases, asphyxiation.
      Use insulated gloves to prevent contact burns.
      Protective eyewear must be worn when breaking up chunks of solid ice or ice pellets.

## Slide 38: CHEMICAL HAZARDS
  Accident and spills
    Eye contact
      Promptly flush eyes with water for a prolonged period ( 15 minutes) and seek medical attention.
    Ingestion
      Follow SDS instruction on case of ingestion and seek medical attention
    Skin contact
      Promptly flush the affected area with water and remove any contaminated clothing. Use the safety shower when contact is extensive. Seek medical attention

## Slide 39: CHEMICAL HAZARDS
  Accident and spills
    Clean-Up
      Promptly clean up small spills using the appropriate Spill Clean-Up Kit located in:
        Histology
        Urinalysis
        Microbiology
        Hematology
      Hazardous chemicals should be contained using the think CLEAN plan:
        Contain
        Leave
        Emergency (eye wash,shower, medical)
        Access the SDS
        Notify a supervisor
      Large spills (gallon or more), the Hospital Safety Manager must be called to clean up the spill

## Slide 40: CHEMICAL HYGIENE PLAN
  Your Responsibility
    Planning and conducting each procedure in accordance with the chemical hygiene procedures detailed in sectional written procedures
    Develop good personal chemical hygiene habits
    Promptly reporting accidents and spills that result in chemical exposure to VA patients or personnel.
Chemical
Hygiene
Plan

## Slide 41: CHEMICAL HYGIENE PLAN
  Standard Operating Procedure
    General precautions for handling all laboratory chemical should be adopted.
    Minimize exposure
    Assume any mixture is hazardous and toxic
Chemical
Hygiene
Plan

## Slide 42: CHEMICAL HYGIENE PLAN
  Chemical Inventory
    Conducted bi-annually by section supervisor
    Chemicals used, produced, or stored must be identified.
    Defined policies and procedures for specific handling requirements.
      Any chemicals classified as hazardous by Dept. of Transportation, EPA, chemicals displaying a 2 or greater in any section of the National Fire Protection Association diamond, Potential Carcinogens or reproductive toxicity
Chemical
Hygiene
Plan

## Slide 43: CHEMICAL HYGIENE PLAN
  Manufacturer, Importer or Distributor Labeling:
    Required for all hazardous chemicals according to Hazard Communication Standards (HCS)
    Use the United Nations Globally Harmonized System of Classification and Labeling of Chemicals, otherwise known as GHS.
    Labels are required to have:
      Product Identifier: is how the hazardous chemical is identified. This can be (but is not limited to) the chemical name, code number or batch number.
      Supplier Identification: name, address and telephone number of the chemical manufacturer, importer, or other responsible party.

## Slide 44: CHEMICAL HYGIENE PLAN
  Manufacturer, Importer or Distributor Labeling:
    Labels are required to have:
      Signal Word: are used to indicate the relative level of severity of hazard and alert the reader to a potential hazard on the label. There are only two words used as signal words, “Danger” and “Warning”. “Danger“ is used for the more severe hazards, while “Warning“ is used for less severe hazards.
      Hazard Statement(s): describe the nature of the hazard(s) of a chemical, including, where appropriate, the degree of hazard.
      Precautionary Statement(s): describe recommended measures that should be taken to minimize or prevent adverse effects resulting from exposure to the hazardous chemical or improper storage or handling. There are four types of precautionary statements: prevention (to minimize exposure); response (in case of accidental spillage or exposure emergency response, and first-aid); storage; and disposal.

## Slide 45: CHEMICAL HYGIENE PLAN
  Manufacturer, Importer or Distributor Labeling:
    Labels are required to have:
      Pictogram(s): are graphic symbols used to communicate specific information about the hazards of a chemical. Each pictogram consists of a different symbol on a white background within a red square set on a point (ie a red diamond).
      Supplementary Information: (Not required) The label producer may provide additional instructions or information that it deems helpful.
      **Note: The GHS standard rating system is opposite the NFPA rating system. In GHS, lower numbers indicate more severe hazards. While in NFPA, lower numbers indicate less severe hazards.

## Slide 46: CHEMICAL HYGIENE PLAN
  Manufacturer, Importer or Distributor Labeling:
    There are nine pictograms, but HCS requires eight of these pictograms, the exception being the environmental pictogram as environmental hazards are not within OSHA’s Jurisdiction. The hazard pictograms and their corresponding hazards are shown below.

## Slide 47: CHEMICAL HYGIENE PLAN
  Manufacturer, Importer or Distributor Labeling:
    The hazard pictograms and their corresponding hazards are shown below.

## Slide 48: CHEMICAL HYGIENE PLAN
This diagram shows which pictograms represent physical hazards, health hazards or environmental hazard.

## Slide 49: CHEMICAL HYGIENE PLAN
  Manufacturer, Importer or Distributor Labeling:
    Sample label is shown below.

## Slide 50: CHEMICAL HYGIENE PLAN
  Secondary/Workplace Labeling
    Required for all hazardous chemicals according to Hazard Communication Standard
    Label using the National Fire Protection Association (NFPA) Diamond
    General numbering classification
      Zero (0)-Minimal
      One (1)-Slightly Hazardous
      Two (2)-Hazardous
      Three (3)-Extreme Danger
      Four (4)-Deadly
      **Note: The NFPA rating system is opposite the GHS standard rating system. In GHS, lower numbers indicate more severe hazards. While in NFPA, lower numbers indicate less severe hazards.

## Slide 51: CHEMICAL HYGIENE PLAN
  Per the HCS, Safety Data Sheet (SDS) for hazardous chemical will provide the following information
    Section 1, Identification includes product identifier; manufacturer or distributor name, address, phone number; recommended use; restrictions on use.
    Section 2, Hazardous Identification includes all hazards regarding the chemical; required label elements.
    Section 3, Composition/information on ingredients includes information on chemical ingredients; trade secret claims.
    Section 4, First-aid measures includes important symptoms/effects, acute, delayed; required treatment.
    Section 5, Fire-fighting measures lists suitable extinguishing techniques, equipment; chemical hazards from fire.

## Slide 52: CHEMICAL HYGIENE PLAN
  Per the HCS, Safety Data Sheet (SDS) for hazardous chemical will provide the following information
    Section 6, Accidental release measures lists emergency procedures; protective equipment; proper methods of containment and cleanup.
    Section 7, Handling and storage lists precautions for safe handling and storage, including incompatibilities.
    Section 8, Exposure controls/personal protection lists OSHA’s Permissible Exposure Limits (PELs); Threshold Limit Values (TLVs); appropriate engineering controls; personal protective equipment (PPE).
    Section 9, Physical and Chemical properties lists the chemical’s characteristics.

## Slide 53: CHEMICAL HYGIENE PLAN
  Per the HCS, Safety Data Sheet (SDS) for hazardous chemical will provide the following information
    Section 10, Stability and reactivity lists chemical stability and possibility of hazardous reactions.
    Section 11, Toxicological information includes routes of exposure; related symptoms, acute and chronic effects; numerical measures of toxicity.
    Section 12, Ecological information*
    Section 13, Disposal considerations*
    Section 14, Transport information*
    Section 15, Regulatory information*
    Section 16, Other information, includes the date of preparation or last revision.
    *Note: Sections 12-15 may be included in the SDS, but are not required by OSHA.

## Slide 54: CHEMICAL HYGIENE PLAN
  Training-What everyone should be able to do!
    Locate the potentially hazardous chemicals in your workplace.
    Recognize the chemical labeling and it’s meaning
    Locate the SDS book in the workplace.
    Locate the health hazard, physical hazard, environmental protection and special protection sections of the SDS and explain their use.

## Slide 55: CHEMICAL HYGIENE PLAN
  Training-What everyone should be able to do!
    Identify the Laboratory Chemical Hygiene Officer by name and title.
    Discuss the major components of the facilities standard labeling system.
    Identify the protective clothing for the area and demonstrate its use.
    Demonstrate emergency procedures in the event of a hazardous chemical spill.

## Slide 56: TUBERCULOSIS EXPOSURE CONTROL PLAN
  Goal is to aid in minimizing/eliminating the transmission of TB
    PPD Skin test on new employees
    Patient with suspected or confirmed active TB will be placed in Airborne Precautions.
      Room with negative air pressure
      The patient’s door must be kept closed.
      You must wear fit tested particulate respirators (Training and fit testing done by Medical Center’s Safety Manager)

## Slide 57: TUBERCULOSIS EXPOSURE CONTROL PLAN
  Minimizing/eliminating the transmission of TB
    TB Testing in microbiology will be performed in a Biosafety Class III hood.
      Negative pressured room
      Must wear disposable gowns and gloves while processing, handling, and evaluating potential infectious TB specimens.
      You must use the aerosol-proof containers when centrifuging specimens.

## Slide 58: TUBERCULOSIS EXPOSURE CONTROL PLAN
  Minimizing/eliminating the transmission of TB
    Pathologist/residents must handle unfixed tissues in the Biosafety Class II hood
      Glove and disposable gowns are required during the processing and handling of these specimens
      Everyone in morgue must wear fit tested particulate respirator masks during an autopsy of suspect patient, and clean up after.
      Fit tested particulate respirator masks must be worn whenever the Stryker saw is used and for 5 air exchanges following the use (5-10minutes)

## Slide 59: TUBERCULOSIS EXPOSURE CONTROL PLAN
  Minimizing/eliminating the transmission of TB
    Responsibility of Health Care worker
      Seek medical evaluation of a PPD test conversion occurs.
      If symptoms develop that may be due to TB, see medical evaluation.
        You must receive appropriate evaluation
        Receive therapy if required
        Prevent the transmission of TB to patients and other health care workers.

## Slide 60: LABORATORY WASTE DISPOSAL
  Lab responsibility
    Identify waste and give special handling for transport or disposal.
    Four broad categories of hazardous waste
      Chemical
        Follow guidelines in MSDS
        Xylene store for recycling
        Formaldehyde neutralize prior to disposal
      Infectious
        Cultures, blood products, contaminated waste etc.
      Radioactive
      Physical
        Managing and disposal of discarded sharps
Drip
Pour
Flake

## Slide 61: LABORATORY WASTE DISPOSAL
  Regulated waste defined by Dept of Labor
    Liquid or semi solid or other potentially infectious materials (OPIM)
    Items contaminated with blood or OPIM (able to drip)
    Items that are caked with dried blood or OPIM that may flake off
    Contaminated sharps
    Pathological and Microbiological wastes containing blood or OPIM
Drip
Pour
Flake

## Slide 62: LABORATORY WASTE DISPOSAL
  Regulated waste –Put into red bags
    OSHA/City of Omaha Regulated waste is disposed as infectious waste.
    All regulated waste will be placed in red disposal bags or sharps containers.
Drip
Pour
Flake

## Slide 63: LABORATORY WASTE REDUCTION
The purpose of the hazardous waste program is to maintain a comprehensive control over the production, handling , transporting, storage, disposal and monitoring of all waste originating in the clinical laboratory to ensure that the health of exposed employees and the surrounding environment is properly maintain.

## Slide 64: LABORATORY WASTE REDUCTION
We generate all sorts of waste and we need to be aware of how to reduce and properly dispose of the waste.

## Slide 65: LABORATORY WASTE REDUCTION
Lab waste divided into these groups
  Hazardous chemical waste
  Infectious waste
  Radioactive waste
  Hazardous physical waste
  Non-hazardous waste

## Slide 66: LABORATORY WASTE REDUCTION
Minimization of waste hazards
  Buy smaller quantities, reusable items, recycling, substitution of less hazardous materials
Waste segregation
  Hazardous waste separated from non-hazardous waste
Waste handling
  Handle waste with care, your safety is a prime concern.

## Slide 67: Accident Reporting
Duty hours 0730-1600 notify supervisor of any occupational injury or accident.
  The supervisor will notify Employee Health Secretary or Employee Health Nurse
  If you need to be examined a “Report of Employee Treatment form will be initiated by supervisor
  Take this form to the Admitting/ER
  A CA17 form should be completed if you are restricted to “Light Duty”.

## Slide 68: Accident Reporting
Non-Duty hours/weekends
  You should go directly to to Admitting/ER
  After being examined a “Report of Employee Treatment form will be initiated by physician/PA/Health Nurse
  The form is then submitted to supervisor when employee returns to work area

## Slide 69: Accident Reporting
All Accidents must be recorded in the Automated Safety Incident Surveillance Tracking System (ASISTS) in VISTA
Lab supervisor is responsible for reviewing with you the corrective action planned or taken

## Slide 70: INTERNAL AND EXTERNAL DISASTER PREPAREDNESS
In the event of a disaster we need to assist members of the medical staff in carrying out their responsibilities-care and treatment of casualties

## Slide 71: INTERNAL AND EXTERNAL DISASTER PREPAREDNESS
Clinical Lab Manager
  Will assume responsibilities for overall coordination of laboratory activities.
  Assesses staffing needs

## Slide 72: INTERNAL AND EXTERNAL DISASTER PREPAREDNESS
Blood Bank Lead Tech
  Notifies Red Cross of disaster and obtain current blood and blood component inventory
  Assesses staffing needs

## Slide 73: INTERNAL AND EXTERNAL DISASTER PREPAREDNESS
Phlebotomy Lead
  Dispatches two phlebotomists to triage area
  Recalls staff if necessary
    Act as runners for the Blood Bank and lab specimens
    Answer and route phone calls
    Assign staff to Central Accessioning Area to receive specimens
  Responsible for proper receipt of specimen and disposition. Communicates with triage area (Collection and Identification of patients)

## Slide 74: INTERNAL AND EXTERNAL DISASTER PREPAREDNESS
Laboratory Supervisor
  Recalls staff accordingly
Morgue Contract Service/Lab Personnel
  Receives bodies and personal belongings
  Maintain record of all deceased
  Records receipt and release of bodies from morgue

## Slide 75: INTERNAL AND EXTERNAL DISASTER PREPAREDNESS
Pathologists/Resident pathologist on call
  Assures that adequate pathology staff is available for consultation by lab staff and Medical Center clinicians

## Slide 76: INTERNAL AND EXTERNAL DISASTER PREPAREDNESS
Lab Orders
  Non-computer generated requisition forms if VISTA is disabled
    Patient location
    Patient Identification same as the Emergency Medical Tags supplied by triage personnel

## Slide 77: INTERNAL AND EXTERNAL DISASTER PREPAREDNESS
Patient specimens
  Properly labeled with Emergency Medical Tag Information
  Patient’s name (if available)
  Initials of person who obtained the specimen.
  Date and time drawn

## Slide 78: INTERNAL AND EXTERNAL DISASTER PREPAREDNESS
Patient Reports
  Results of all STAT request will be called to the location listed on the requisition form.

## Slide 79: INTERNAL AND EXTERNAL DISASTER PREPAREDNESS
VISTA Results Entry
  Volume allows and adequate information entered into VISTA (Patient Info)
  Lab will order request sent on the non-computer generated requisition forms.
  Results will be entered into the system as they are available.

## Slide 80: EVACUATION PLAN
In an Emergency we may have to Evacuate
Each section has a fire evacuation route posted
You are responsible for knowing the alternate routes

## Slide 81: EVACUATION PLAN
Simple evacuation
  Remove yourself and others persons from immediate area of danger
  Priorities for moving patients/staff/visitors
    First-persons in imminent danger
    Second-wheelchair and walking persons

## Slide 82: EVACUATION PLAN
Total evacuation
  Lateral or vertical movement of all patients, visitors and employees from a wing or entire facility to outside grounds.
    Blankets, beds, mattresses, litters, and any other means for removing non-ambulatory patients.

## Slide 83: EVACUATION PLAN
Total evacuation
  All rooms, including bathrooms
    Will be search upon completion of evacuation by Lab Safety Officer or designee.
    Ensure all have been evacuated

## Slide 84: EVACUATION PLAN
Total evacuation
  Handicapped individuals (Wheelchairs, crutches, canes, etc.)
    We will assist these people to the safest part of the same floor (toward an exit)
    During a total evacuation the elevators may be utilized ONLY if instructed to do so by the Omaha Fire Department.
    It may be necessary to carry handicapped individuals to the first floor for evacuation.

## Slide 85: LATEX PRECAUTIONS PLAN Some items that contain Latex
  Markers
  Adhesives
  Gloves
  Diazosensitized photo copy paper
  Electrical appliance cords
  Telephone receiver headset, shoulder rest
  Finger cots
  Glue, envelopes, stamps, plastic
  Ink, tape, erasers
  Mouse pad
  Plants
  Rubber bands
  Rubber button pads on phones, calculators
  Tubing
  Gowns
  Butterflies
  Co-flex
  Latex tourniquets
  Needles (rubber end)

## Slide 86
  3M transparent tape
  Ependorf combo tips
  Pipette tips
  Parafilm
  Sed-rate tubes
  Vacutainer holders
  10cc, 20cc syringes
  Stopper on monoject tubes
  Needle banks
  Beral transfer pipettes
  UA cap, tubes, pipettes, V-tech Brand
  Fisher brand serum filters
  UA test strips
  TDX sample cups
LATEX PRECAUTIONS PLAN Some items that contain Latex

## Slide 87: LATEX PRECAUTIONS PLAN
Employee identification
  If you know you have a latex allergy/sensitivity you must communicate this information to your immediate supervisor
  You are responsible for maintaining proper latex allergy precautions
  If you suspect you have a latex allergy/sensitivity, you need to report it to your supervisor and to the Employee Health for further screening.

## Slide 88: LATEX PRECAUTIONS PLAN
Employee identification
  Your immediate supervisor document your latex allergy/sensitivity in your employee records.
  Your department will then employ all reasonable efforts to accommodate your latex allergy/sensitivity to provide you with a latex-safe working environment
    Purchase of latex-free supplies
    Check equipment and replace with latex-free materials if economically feasible

## Slide 89: LATEX PRECAUTIONS PLAN
In-Patient identification
  All patients should be identified during their admitting screening and assessment
    If patient is latex sensitive, latex sensitive cart will be assign to the patient.
      You should identify the patient as being latex sensitive by the Latex Sensitive Isolation posted.
      Use only the latex free items found on the cart or those provide by the lab.

## Slide 90: LATEX PRECAUTIONS PLAN
Out-Patient identification
  All patients should be identified by an orange tag “Latex Sensitive” attached by outpatient registration Desk Personnel
    When you view the patient’s order in the computer, you should get a “Latex Allergy’ Alert
    Use only latex free items on this patient.

## Slide 91: LABORATORY EROGNOMICS POLICY
We need to provide a work environment that reduces or eliminates your exposure to conditions that lead to cumulative trauma disorders (CTD) and musculoskeletal disorder (MSD)
It is your responsibility to recognize the signs and symptoms associated with these ergonomics risk factors and notify your supervisor.
The NWIHCS Ergonomic Committee will do an assessment.

## Slide 92: Noise Exposure
OSHA guideline
  When an employee’s exposure to noise may equal or exceed 85 decibels for 8 or more hours, the employer shall develop and implement a monitoring program.
  Baseline testing and monitoring will be repeated whenever a change in production, process, equipment, or controls cause an increase in noise exposures.

## Slide 93: NWIHCS LAB FORMALDEHYDE PROGRAM
We need to ensure formaldehyde is handled in the safest possible manner and in compliance with all applicable codes and standards.
Limit contact
  Protective clothing (lab coats)
  Gloves
  Eye shields/goggles if dispensing
  Eyewash and safety shower near by

## Slide 94: NWIHCS LAB FORMALDEHYDE PROGRAM
If you come in contact with formaldehyde
  Immediately flush the exposed areas
  Notify your supervisor and proceed to Employee Health
During grossing
  Specimens will be handled in exhaust fume hood
  Any other handling of containers with formaldehyde solutions should be handled in a well-ventilated area

## Slide 95: NWIHCS LAB FORMALDEHYDE PROGRAM
Health hazards you should be aware of
  Cancer
  Irritation and sensitization of the skin
  Affects respiratory system
  Eye and throat irritation
  Acute toxicity
If you experience irritation of your eyes, throat, skin due to exposure, report to Employee Health

## Slide 96: Shipping Infectious Substances
Our responsibility
  For the shipments
  Training others on shipping procedures
  Classifying, identifying
  Marking, labeling
  Packaging and documentation of dangerous goods
  Ends when package reaches its destination safely

## Slide 97: Shipping Infectious Substances
9 Classifications (We only have 2)
  #6 Infectious substances
    Cause serious health effects
    Bacteria, virus, parasite, human samples
  #9 Dry Ice

## Slide 98: Shipping Infectious Substances
Packaging
  Triple packaging
    Primary receptacle
    Secondary receptacle
    Outer shipping package

## Slide 99: Shipping Infectious Substances
Hazard labels
  Specific hazard labels must be affixed to the outside of each package.
    Biohazard Label for infectious substances
    Miscellaneous for Dry Ice
      Allow for pressure to be released
      Write down the number of pounds used

## Slide 100: Shipping Infectious Substances
Packing
  Place sample into biohazard bag with absorbent packing material

## Slide 101: Shipping Infectious Substances
Packing
  Place bag into secondary container (screw top plastic jar)

## Slide 102: Shipping Infectious Substances
Packing
  Place secondary container into Styrofoam container with corrugated cardboard box
  Add Room Temp/Cold/Frozen Packs to maintain specimen temp.
  Enclose an itemized list of contents between secondary packaging and the outer packaging

## Slide 103: Shipping Infectious Substances
Packing
  Seal box and place OSHA Biohazard Label on the outside of the package
  Mail to appropriate reference lab

## Slide 104
You made it through!