## Slide 1: APHERESIS EDUCATION
EST. 8/2025

## Slide 2: Calcium
Calcium is administered to patient in attempt to counteract hypocalcemia caused by the ACDA that is received during treatment
AC Infusion rate
  The amount of AC that the patient is receiving. This may be lowered if the patient is experiencing calcium issues
  The lower the rate, the less calcium the patient is receiving
AC Ratio
  The amount of AC that is running through the kit
  This may be lowered if clumping is an issue
  The lower the ratio, the more AC is running through the kit
Calcium Gluconate doses differ between hospitals
  MH and UH
    There is 1GM of calcium gluconate in 35mL of IV fluids
  RH
    There 1GM of calcium gluconate in 20mL of IV fluids
When programming the IV pump for a bag of calcium to be infused, be sure to subtract 15mL of IV fluids from the total volume to be infused to account for the amount that it requires to prime the IV tubing (ex. If there is 105mL in you IV bag, your volume to be infused should be 90mL). If you get a syringe of calcium gluconate from Riley, you will be able to see directly how much calcium is in the syringe and that is the volume that you will program.
Pay close attention to calcium orders in Cener as sometimes the provider will order extra calcium for the first couple of procedures in case the rate needs to be increased during the run. This will ensure that you do not run out of calcium and need to pause while waiting for another bag.
  Example: The provider may order a 5GM bag of calcium and order for the calcium to be started at a 3GM dose. This means that you will program your volume to be infused as followed:
    90mL at UH and MH with a calcium bag (35x3=105mL then subtract 15mL to make 90mL)
    60mL at Riley (when using a syringe) or 45mL (when using a bag) (20x3=60mL then subtract 15mL to make 45mL if using a bag).
CALCIUM CHLORIDE IS NOT THE SAME INFUSION RATE AS CALCIUM GLUCONATE.

## Slide 3: Blood Pressures
Blood Pressure drops can occur for many reasons during Apheresis
  Fluid Shifts
  ACE inhibitors (check all patient medication lists for medications ending in “pril.”)
  Rapid cell loss
  Transfusion reaction
  Patient condition
Check patient call orders for guidelines
If a blood pressure drop is noted, PAUSE the procedure immediately
  For inpatient procedures, inform the inpatient team immediately (press the call light if needed).
  For outpatients, send a Diagnotes in the provider chat immediately
Blood pressure should be checked more often on inpatients and even more often for patients with known blood pressure issues.

## Slide 4: ECMO
Pay close attention to Apheresis provider orders for AC ratio
  The ECMO circuit is typically anticoagulated so will titrate the AC ratio so that there is less AC in the Apheresis circuit
The ECMO RN will hook up and unhook the Apheresis lines
  You will not need to utilize the blood warmer or blood warmer tubing
The ECMO RN will collect the samples for the ionized calciums
Inlet speed may have to be lowered for return pressure alarms due to the blood running through the ECMO circuit at the same time

## Slide 5: CRRT
Check with providers to verify if you will run in tandem with CRRT or if the inpatient team will pause during Apheresis

## Slide 6: Custom Prime
Custom Prime can be ordered when the Apheresis MD or APP deems necessary. Situations can include:
  The patient’s blood volume, that is drawn into the Apheresis circuit, is greater than or equal to 15% of the patient’s total blood volume.
  The patient has low hemoglobin
Step by step instructions are provided in the Blood_Blood Component Prime of Spectra Optia SOP in policy tech.
Things to remember:
  DO NOT walk away from the machine during custom prime
    If air enters the circuit, a new set-up with more blood products will be required.
    The rinseback feature toggles off when custom prime is selected. ONLY toggle back on if provider orders specify.
  Custom Prime Volume
    240 mL for Exchange sets (200mL for the set and 40mL for the warmer tubing if used)
    340 mL for IDL sets (300 mL for the set and 40mL for the warmer tubing if used). If you are using blood, this may require 2 units. You can press the pause button while switching to the next unit.
  You MUST select the custom prime option before you confirm priming of the inlet and return lines. You will be unable to change it at this point and will have to set up a new machine.
If the provider has ordered a partial rinseback when utilizing an IDL set, monitor the rinseback volume on the screen and pause once the ordered rinseback volume is reached. You will disconnect from there.
A Saline Rinse of the kit can be ordered if a patient has hypersensitivity to the sterilizing agent ethylene oxide.
  This will be done after machine prime and prior to hooking up the patient.
  Step by step instructions are provided in the Blood_Blood Component Prime of Spectra Optia SOP in policy tech.

## Slide 7: Low Blood Volume
Inlet Speed
  Spectra Optia- At least 10mL/min
    The AC infusion rate can be increased to achieve this speed with provider orders
    Increasing the AC infusion rate is standard with pediatric stem cell collections if necessary
  CellEx- At least 15mL/min
Pediatric code sheets are required if the patient is less than 17 years old
For patients that weigh 25kg or less, the patient’s weight will have to be manually calculated by utilizing the values below and multiplying by the patient’s weight.
  Preterm neonate= 100mL/kg
  Term neonate= 85mL/kg
  >1 month=75mL/kg

## Slide 8: FFP for TPE
In stable patients, AC infusion rate can be increased to 1.0.
Half and Half
  Albumin is utilized first
  A time out is performed when switching to FFP
    Vital signs checked
    A set of numbers should be documented in the Apheresis flowsheet
    Calcium infusion rate should be recalibrated to reflect the new end time
    A comment should be placed on the flowsheet that states that the operator has switched to FFP
    Ensure that the FFP is scanned into Cerner Bridge is applicable (this can be done earlier)
    Ensure that the start time of the FFP is documented in Cerner Bridge or the blood slip if necessary

## Slide 9: Access
NS flushes
  Ports
    Each lumen should be flushed with 20mL during access and de-access
    Only 10mL syringes should be used to flush to prevent port rupture due to high pressure
    Flush with a constant pushing method
  Lines
    Each lumen needs to be flushed with 10mL during access and 20mL during de-access
    Flush with a push-pause method
    If at Riley, check with the inpatient team to verify if they will be required to access the lines (some floors prefer to access their patients)
Troubleshooting
  Ports
    Rule out obstructions such as kinks or clots
    Reposition the patient
    Ensure that the cannula is positioned at the back of the port and in the center
    If there is no aspiration, try flushing
    Ensure that the port is correctly positioned
    Port re-access may be necessary if there is malposition
    If a stopcock is being used, they may need to be aseptically changed as sometimes the tubing may be clotted (during the procedure).
    If all troubleshooting fails, contact the provider for TPA. TPA is costly and may cause huge delays. It should only be utilized as a last resort.
Heparin
  Pay close attention to heparin orders
  Stem cell collection patients will use the low dose heparin
  If there is no heparin ordered, check with Apheresis providers. Sometimes they may not have the dwell volumes, or the patient may not require heparin

## Slide 10: Transfusion Reactions
Signs/Symptoms
  Temperature increase of at least 2 degrees Celsius or 3.6 degrees Fahrenheit
  Dyspnea/Shortness of breath
  Wheezing
  Hypoxemia
  Hypotension
  Suspected hemolysis or hemoglobinuria
  Urticaria/rash/Itching
  Chills/Shaking
  Increased Heart Rate
  Vomiting
  Headache
If transfusion reaction is suspected
  Stop immediately and leave patient accessed.
  Disconnect and cap transfusion set. DO NOT DISCARD. Also, save the Apheresis kit.
  Start 0.9% normal saline infusion at a KVO rate (new saline bag, new tubing).
  Take a set of vital signs and document in Bridge or the I/O flowsheet.
  Notify the Apheresis provider (outpatient) or inpatient team if on the inpatient unit.
  If provider agrees that transfusion reaction workup is necessary, draw post-transfusion blood sample (lavender top 6mL) and label with patient ID, time, and date.
  Confirm that all blood product details match with patient information.
  Inform Blood Bank of transfusion reaction. If any discrepancies in product/patient information discovered, alert Blood Bank.
  Confirm the “Transfusion Complication” is ordered STAT. Send previously drawn blood sample as well as the remainder of blood product with the connected administration set, including in-line IV fluid to Blood Bank.

## Slide 11: Communication
Pay close attention to the patient’s call orders
  If IP, the call orders should be based on the IP team and out of range vital signs should be reported to the IP team first
In the AM prior to the procedure, please contact the IP unit and provide an ETA in case the patient has other tasks
Contact the IP RN immediately upon arrival to the IP unit (even if the call light needs to be pressed) and inform them of the procedure time and that they will need to be available if complications arise
Things typically managed by the inpatient team
  Vital signs
  Some lab values
  Patient clinical status
The IP team should be the first contact, unless it is regarding the Apheresis machine, or Icals managed by the Apheresis provider.