## Slide 1: Flow Cytometry
Specimen Requirements

## Slide 2: Specimen Types used for Flow Cytometry Testing
Bone Marrow Aspirates and/or Trephines
Tissue Samples – Some of the more common tissue samples received are Lymph Nodes, Tonsils, and Spleen
Blood
Body Fluids – CSF, Pleural Fluids, Bronchial Lavages and Washings
Fine Needle Aspirate(FNA)/Core Biopsies

## Slide 3: Bone Marrow Requirements
Collect aspirate in 4.0 ml green Na Heparin or directly into RPMI container – no gel
Minimum 2.0 ml of specimen
Transfer sample to RPMI
Transport aspirates ambient
Sample stability – 72 hours
Unacceptable specimens:
  Frozen samples
  Samples received in formalin or any other preservative
If unable to obtain aspirate, submit a trephine sample in RPMI and transport refrigerated.

## Slide 4: Blood Specimen Requirements
Two 3ml lavender EDTA top tubes. – DO NOT send 6 ml lavender top tubes; they cannot be fully processed.
Transport ambient
Minimum Volume – 2ml
Stability 72 hours for Flow Cytometry. CBC must be performed within 24 hours.
CBC with manual differential required. Make 2 wedge smears and 2 albumin or spun smears.
Unacceptable samples: Frozen samples and samples not received in EDTA

## Slide 5: Tissues and FNA sample requirements
Place specimen directly into RPMI. If no RMPI is available, saline is acceptable, but not preferred.
  (If RPMI is needed at your site, call Flow Cytometry at 414-649-7859)
Transport refrigerated
Stability is 72 hours
Unacceptable specimens: Specimens received in alcohol, formalin or Cyto-Lyte

## Slide 6: Body Fluid Specimen Requirements
Collect in a sterile container
Transfer to RPMI
Submit as much fluid as possible up to 50 ml
Transport ambient
Stability 72 hours
Unacceptable specimens: Specimens received in alcohol, formalin or Cyto-Lyte