## Slide 1: Hazardous Waste “Cradle-to-grave” responsibility
Laboratory 2017

## Slide 2: Overview
What is waste?
When to evaluate?
How to evaluate?
Hazardous or Not?
Waste Types- Listed, Characteristic, Dual
Managing waste
Accumulation waste
Segregation of waste
Waste containers in Lab
Hazardous waste spills
Common deficiencies

## Slide 3: What is waste??
A material not needed, wanted or used.
Unusable.
Intended to be discarded.

## Slide 4: When is waste evaluated?
Must evaluate waste within 60 days of first producing.
Must evaluate prior to sewering.
New product must be collected as hazardous waste until evaluation results determine they are not hazardous.

## Slide 5: How to evaluate ?
By Knowledge
SDS
Manufacturer certification
Vendor letters
Keep all documentation used in evaluation whether waste is hazardous or non-hazardous

## Slide 6: Is waste Hazardous or Not?
The Environmental Protection Agency established the Resource Conservation and Recovery Act (RCRA) in 1980 for the purpose of regulating the proper handling, storage, and disposal of HW.

## Slide 7: Is waste Hazardous or Not?
RCRA Hazardous Waste includes:
Listed waste
Characteristic waste
Dual waste

## Slide 8: Listed waste
F list
K list
P list
U list

## Slide 9: F listed waste
F-listed wastes:
degreasing solvents
paint/lacquer thinners
brake/carburetor cleaners
dry clean solvents
Many common laboratory solvents- Methanol, Acetone, Xylene

## Slide 10: K listed
K-listed wastes:
wood preserving
pesticide manufacturing
iron and steel industries
Healthcare providers are not listed K-List waste generators.

## Slide 11: U listed
U-listed wastes:
Toxic and others
Examples: Formaldehyde, Mercury, Methanol

## Slide 12: P listed
P-listed wastes:
Acutely hazardous
Fatal to humans in low doses (arsenic, strychnine, cyanides)
Examples: Sodium azide

## Slide 13: Note:
Listed waste is collected if they are the sole active ingredient of the product. Most P listed chemicals used in Lab are used as preservatives- they are NOT the sole ingredient. Therefore we do not collect.

## Slide 14: Characteristic Waste
Corrosive
Ignitable
Lethal
Oxidizers
Reactive
Toxic

## Slide 15: Corrosive
Corrosive wastes:
any liquid able to corrode 1/4 inch of steel per year (battery acid)
pH <2
pH > 12.5
able to burn or destroy living tissues
Examples: Acids (hydrochloric, acetic, phosphoric, etc.)

## Slide 16: Flammable
Ignitable wastes:
flash point of <140 degrees F
spontaneously combustible
includes ignitable, compressed gas
Solution contains >24% alcohol by volume.
Examples: Methanol, Isopropyl Alcohol, Ethanol

## Slide 17: Lethal
Lethal: can cause severe health effects or death when ingested, inhaled, or absorbed through the skin.
Example: arsenic, poisons

## Slide 18: Oxidizing
Oxidizing wastes:
wastes that add oxygen to a fire.
often have “per” at the beginning of the name, “oxide” at the end of the name, or “ate” in its chemical name.
Example: perchloric acid

## Slide 19: Reactive
Reactive wastes:
unstable or explosive wastes (lithium batteries)
react violently with water (lithium, sodium)
form toxic or explosive gasses (cyanide, sulfide)
Example: Picric Acid

## Slide 20: Toxic
Toxic waste:
capable of causing injury or death through ingestion, inhalation, or absorption
capable of causing cancer (carcinogens), genetic damage (mutagens), and fetal harm (teratogens)
Example: Formaldehyde, Gram stains & Aerospray stains- Methanol

## Slide 21: Lethality
Lethality: Median lethal dose less than limit= Hazardous waste.
Oral= LD50<= 500mg/kg
Inhalation= LD50<=1000mg/m3
LD50<=2000mg/kg gas/vapor
Dermal= LD50<=1000mg/kg

## Slide 22: Dual Hazardous Waste
Dual Waste is a term that defines waste that is both Hazardous and Infectious.
Laboratory has one Dual Alkaline Corrosive container in Microbiology- C. diff and Strep A cartridges.
One Dual flammable/MN01 in sendouts.

## Slide 23: Managing waste
Choose correct container:
Waste must be compatible.
Containers must close properly.

## Slide 24: Accumulating Waste
Lab is a Satellite Accumulation site:
Must be marked Satellite Accumulation.
Must have the words Hazardous waste.
Start and fill dates.
Must have a clear description of the waste

## Slide 25: Segregation of wastes
Incompatible wastes must be properly segregated.
Secondary containment is required to prevent uncontrolled spills.
Weekly inspections are required and documented for all storage areas.

## Slide 26: Hazardous Waste Containers in Lab
Hematology
Located by Sysmex
1- Ethylene Glycol containing waste container- Sysmex dye packs.
1- Flammable waste container- contains Aerospray stains (methanol, ethanol).

## Slide 27: Hazardous Waste Containers in Lab
Microbiology
1- Flammable waste container- contains Gram stains- ethanol and methanol.
1- Dual Alkaline Corrosive waste container- CDIFF cartridges and Strep A cartridges
Patient labels must be removed prior to disposal.

## Slide 28: Hazardous Waste Containers in Lab
Microbiology
Alkaline Corrosive Hazardous Waste-KOH vials, unused MRSA cartridges

## Slide 29: Hazardous Waste Containers in Lab
Chemistry
Located under Cellavision
Alkaline Corrosive Hazardous Waste
  Folate Pretreatment 1
  B12 Pretreatment 1
  Creatinine Reagent 1
  Lithium Reagent 1
  Total Protein Reagent 1
  Detergent B
  Alkaline Wash

## Slide 30: Hazardous Waste Containers in Lab
Chemistry
Located under Cellavision
Acid Corrosive Hazardous Waste
  Pre-Trigger
  Acid Wash
  Total Bilirubin Reagent 1&2
  Direct Bilirubin Reagent 1&2
  Phosphorous Reagent 1&2
  Testosterone Specific Diluent
  ACL Clean A

## Slide 31: Hazardous Waste Containers in Lab
General Lab
Located by sink in Sendouts
MN01 Dual Flammable Hazardous Waste
BD Affirm Substrate
Cytolyt
Hemoccult Developer
10% Buffered formalin

## Slide 32: What to do with full collection containers?
Containers should not be overfilled.
The accumulation or fill date should be recorded on the containers label.
Ensure container is closed.
Lab Safety Officer should be notified.
If Lab Safety Officer is not available call FM at Ext. 6508 or 6364.

## Slide 33: Spills
A major spill is a spill which is a threat to persons, property or the environment, and cannot be safely controlled or cleaned without assistance from Facilities Management Safety personnel.

## Slide 34: Spills
A minor spill is a spill which poses no threat to persons, property or the environment, and can be safely controlled and cleaned up by facility personnel

## Slide 35: Minor Spill
Any employee experiencing or finding a minor hazardous material or hazardous waste spill is to:
(1) Clear the affected area and isolate the spill area to prevent others from coming in contact with the spill.
(2) Call the Garage at extension 6452 to have drain covers brought to the spill location if the spill has or will affect a drain.
(3) Report the spill to FM at ext. 6364 or the GEMS Coordinator at ext. 6508 from 8:00 am to 4:30 pm and the Boiler Plant at ext. 6347 or Police at ext. 6224 during off tour hours.
(4) Obtain the MSDS for the spilled material and assess the hazard.
(5) Follow PPE and spill cleanup instructions found on the MSDS.
(6) Notify the supervisor of the area or employee’s supervisor.
(7) Ensure that a spill report (Attachment A) is properly completed and submitted to the FM. This is to be completed every time there is a hazardous material or waste spill.

## Slide 36: Major Spill
Any employee experiencing or finding a major hazardous material or waste spill is to:
(1) Clear the affected area and isolate the spill area to prevent others from coming in contact with the spill.
(2) Call the Garage at ext. 6452 to have drain covers brought to the spill location if the spill has or will affect a drain.
(3) Report the spill to FM at ext. 6364 from 8:00 am to 4:30 pm and the Boiler Plant at ext. 6347 or Police at ext. 6224 during off tour hours.
(4) Obtain the SDS for the spilled material and remain available to answer Safety personnel questions about the spill.
(5) Notify the supervisor of the area or employee’s supervisor.
(6) Ensure that a spill report (Attachment A) is properly completed and submitted to the Facilities Management Safety personnel. This is to be completed every time there is a hazardous material or waste spill.

## Slide 37: Common Deficiencies
Hazardous waste in sewer.
Hazardous waste in trash.
Wastes not evaluated (no label or MSDS).
Improper labeling.
Improper storage/segregation.
Containers not closed.
Lack of secondary containment.
Lack of weekly inspections.
No documented training.

## Slide 38
THE END

## Slide 39: References
Hazardous Waste & Healthcare: Laboratory waste. MPCA Industrial Division. April 2007.
www.mpca.org
www.epa.org
MCP FM-06 Hazardous Material and Waste Management Program.