## Slide 1: Red Blood Cell Viability At Different Temperatures Using Glycerol Based Cryopreservation Methods
Nina Sen
SBB Project 2013

## Slide 2: SBB Project
Request: Can a TSL store rare red cells?
Why: So we dont have to send some of the repeating antibody workups to PSBC such as anti-k
IRB: Application for approval of using samples for research
Research: lots and lots of it
Project Outline: Submission to Indiana for approval
Method: Design the method and reagent required
Cost: Submit cost analysis to manager

## Slide 3: Study Objective
This study will determine optimal technique and concentration of glycerol for freezing small volume of rare red cells in a hospital based transfusion services laboratory.
This study will also compare the capillary method and standard cryovial method of freezing small volumes of red cells with the different concentrations of glycerol and storage at -30C and -80C.

## Slide 4: Method
Two temperatures- -30C and -80C
Two concentrations- 30%w/v glycerol, 40%w/v glycerol
Two methods for storage- standard tube (3ml), capillary tubes
Storage Intervals- 2 and 6-weeks

## Slide 5: Samples and Reagents
Research samples- n = 21
Segments from in date units
Patient samples expired at day 4
Commercial reagent cells from BioRad and Immucor- could not use this due to low red cell volumes available
Reagents and Supplies
Glycerol 57%w/v
Sodium Chloride-12% and 1.6%

## Slide 6: Method
Freezing
Prepare 1:1 ratio of glycerol and red cells= 30%w/v
Prepare 2:1 ratio of glycerol and red cells= 40%w/v
Mix and store in the standard tubes and capillary at -30C/-80C for each sample for 2 weeks and 6 weeks
Thawing – 2weeks and 6-weeks
Wash the red cell/glycerol in decreasing concentrations of Sodium Chloride
Final wash with Normal Saline 0.85%
Reconstituted 3-5% red cell suspension

## Slide 7: Sample Analysis
Pre RBC and Post RBC- automated CBC analyzer
Pre and Post Antigen testing- C,E,c,e,K, Jka,Jkb, Fya,Fyb, M and S
Approximate % recovery calculated
Comparison of antigen strength pre and post

## Slide 8: Results

## Slide 9: Results

## Slide 10: Results

## Slide 11: Results

## Slide 12: Discussion
Twenty one samples thawed at 2-weeks and fifteen samples at 6-weeks demonstrated approximate 48-85% cell recovery.
Apparent recovery was equivalent with 30 or 40% w/v glycerol and the capillary method was at least as good as the cryovial method.
There was equivalent antigen reactivity pre and post thaw except in a single with diminished Fyb reactivity after 2 weeks at -30C.

## Slide 13: Discussion
Overall, 30% w/v glycerol using the capillary method and
-80C storage worked well.
This study demonstrated a simple method for hospital-based TS to freeze small aliquots of red cells antibody identification.
Additional validations with longer storage to be evaluated for 30%w/v glycerol at -80C