## Slide 1: Formaldehyde
Awareness Training for Histopathology

## Slide 2: Training Topics
Formaldehyde & Its Uses
Health Hazards
OSHA Expanded Standard Requirements
Spills
Eye/Skin Exposure Actions

## Slide 3: What is Formaldehyde
Colorless
Strong smelling gas
Often found in aqueous solutions
Formalin – mixture of formaldehyde, water and alcohol (typically methanol)
  Typically contains 37% formaldehyde
  Neutral Buffered Formalin is often 10% formaldehyde

## Slide 4: Uses of Formaldehyde
Preservative in Medical Laboratories and Mortuaries
Industrial fungicide, germicide and disinfectant
Found in particle board, glues, paper product coatings, plywood, fiber board and other household products

## Slide 5: Tasks involving Formaldehyde
Tissue Dump
Grossing
Tissue Processor
Fixing Tissue

## Slide 6: Health Hazards
Highly irritating to eyes, nose and throat.
Allergic reaction of the skin, eyes and respiratory tract
Ingestion can be fatal
Chronic exposure to low levels in air or on skin can cause asthma-like respiratory problems and skin irritation such as dermatitis/itching
Cancer
Concentration > 100 ppm are immediately dangerous to life and health
Sensitizing agent – can cause immune response

## Slide 7: How Formaldehyde can get into your body
Inhalation
  Primary route of exposure due to high volatility
Skin absorption
  Occurs via contact with liquid
Ingestion (rare)
  Eating or drinking without washing hands and face after working with formaldehyde

## Slide 8: OSHA Expanded Standard Requirements 29 CFR 1910.1048 Formaldehyde
Exposure Limits
Exposure Monitoring
Respiratory Protection/Controls
Medical Surveillance
Hazard Communication
Record Keeping

## Slide 9: Exposure Limits
8-hour Time Weighted Average (TWA) Permissible Exposure Limit (PEL)
  0.75 ppm
15-minute Short Term Exposure Limit (STEL)
  2 ppm
Action Level (AL)
  0.5 ppm

## Slide 10: Exposure Monitoring
Initial
  Air monitoring or objective data used to determine affected employee’s exposure
Periodic Monitoring
  If >STEL; monitor STEL annually under worst conditions
  If TWA ≥AL, monitor TWA every 6 months
Additional Monitoring
  Required if a change in workplace conditions cause increase in employee exposure

## Slide 11: Respiratory Protection
Respirators must be worn:
  Whenever employee’s exposure exceeds PEL or STEL
  Emergencies (unknown concentration) such as large spills
All employees required to wear a respirator must be enrolled in the VAMC Respiratory Protection Program
  Medical Center Memorandum 00S-158 Respiratory Protection Program

## Slide 12: Personal Protective Equipment (PPE)
PPE is used to prevent formaldehyde contact with eyes, nose, throat and skin. Respirators are used to prevent inhalation of formaldehyde where high concentrations of formaldehyde are possible (e.g. large spills)
  Impervious Apron or lab coat
  Tyvek Sleeves (pouring large quantities)
  Closed-toe shoes
  Chemical splash goggles (pouring)
  Face Shield (splash hazard)
  Nitrile Gloves
  Full Face Air Purifying Respirator (spill clean-up)

## Slide 13: Engineering Controls
Engineering controls are used to capture hazardous chemicals at or near the source of generation. Effective controls reduce minimize risk of exposure and reliance on PPE to protect workers
  Fume hood/sink (Morgue)
  Fume hood (Grossing, Rm 2638)

## Slide 14: Medical Surveillance
Must be available to affected employees who are:
  Exposed to Formaldehyde at/above the AL or STEL
  Develop signs or symptoms of overexposure to formaldehyde
  Exposed in an emergency

## Slide 15: Hazard Communication
Required for solutions containing greater than 0.1 ppm formaldehyde or materials capable of releasing formaldehyde into the air at concentrations exceeding 0.1 ppm
Review product specific Safety Data Sheet prior to using that product

## Slide 16: Records
You have the right to see any of your medical records related to formaldehyde
You also have the right to see results of any air sampling for formaldehyde we have done

## Slide 17: OSHA Standard
29 CFR 1910.1048 Formaldehyde and its appendices have more information in detail
A copy of this standard is available at www.osha.gov.

## Slide 18: Spills
Small Spill (e.g. small specimen cup)
  Use absorbent pads to mop up liquid
  Wear PPE while cleaning spill
  Place in double plastic bag
  Notify Safety to collect spill clean-up materials at 42933 or 46490

## Slide 19: Spills
Large Spill
  Leave the area immediately
  Don respirator, PPE and use spill kit to absorb formaldehyde (Do not attempt to clean spill unless you have been trained and fit tested with full face respirator)
  Place clean-up materials/PPE in double bag
  Notify supervisor and Safety at x42933
  After hours, notify graphics at x41010
  Complete ASISTS report

## Slide 20: Eye Exposure
If eyes are exposed to formaldehyde:
  Get to eye wash immediately
  Flush eye for at least 15 minutes
  Seek medical attention, after flushing
  Notify supervisor/employee health
  Complete ASISTS report

## Slide 21: Skin Exposure
Incidents involving skin exposure:
  Immediately wash affected area with water for 15 minutes
  If large area of the body is affected, use emergency shower-remain in shower for at least 15 minutes
  Be alert for signs of exposure
  Seek medical attention, after flushing
  Notify supervisor/employee health
  Complete ASISTS report