## Slide 1: i-STAT Total β-hCG 6-Month Competency
Ancillary Testing
August 2016
McGuire VAMC

## Slide 2: Quality Control
External controls are performed every 30 days:
  Levels 1 and 3 on all meters
  Stored in refrigerator
  Check expiration date
  Mix well
Staff are required to rotate performing QC
Controls are now programmed on a schedule
i-STAT screen will alert you when QC is due

## Slide 3: Quality Control cont.
Only select Option 2: Schedule 1
Due date: 2nd Tuesday of the month @ 0300
Grace period: 48 hours
Can not be performed before the due date
Analyzers will lock if QC is not performed within the grace period - you will NOT be able to perform patient testing!

## Slide 4: Specimen collection
Green top tube must be full
Under-filled tubes can cause inaccurate results
Sample is only acceptable for i-STAT testing up to 30 minutes after collection
Label all specimens with patient label

## Slide 5: Cartridges
β-hCG cartridges are stored in the counter near where the i-stats are.
Troponin = red
β-hCG = green
Crea = Pink

## Slide 6: Interpretation
Negative: <5.0 IU/L hCG QUAL ( - )
Indeterminate: 5.0 – 25.00 IU/L hCG QUAL ( )  consult with provider
Positive: >25.00 IU/L hCG QUAL ( + )