## Slide 1: Hematology Competency Review FY21

## Slide 2: Check the Label
All tubes should be labeled with:
  Full name
  SSN
  Date
  Time drawn
  Phlebotomist/nurse initials
Competency Element 1: Test Performance

## Slide 3: Specimen Requirements
Sysmex (CBC)
  Minimum volume: 300μl (open tube) or 1ml (closed tube)
Symex (BF)
  Minimum volume: 300μl (open tube) or 1ml (closed tube)
  Washes are unacceptable
  Fluids from wounds, cysts, etc. unacceptable
Stago (Coag)
  FULL 2.9mL 3.2% sodium citrate tube
iSed
  Minimum Volume: 500µL in EDTA-K2 (lavender top)
Tosoh
  Recommended Volume: 1mL in EDTA-K2 (lavender-top)
  Or a minimum 10 μl, must be diluted
Clotted samples are unacceptable for all testing, except A1Cs
Competency Element 1: Test Performance

## Slide 4: Specimen Rejection
Specimens must be rejected if they do not meet the sample requirements.
Causes for Specimen Rejection
  Mislabeled or insufficiently labeled specimens
  Insufficient volume of blood
  Expired collection tubes
  Improper specimen collection
  Clotted specimens
Providers must be notified of all rejected specimens, following the “How to cancel a test” SOP
Competency Element 1: Test Performance

## Slide 5: TATs and CRITs
All results are reviewed for accuracy before reporting.
Results are released in a timely manner
  1 Hour for STATs
  4 Hours for Routines (including diffs)
  24 Hours for A1Cs
Critical values are called to the patient’s provider.
**Acceptable: MDs, DOs, PharmDs, PAs, NPs**
**Unacceptable: RN (except in ICUs and ER)**
  Critical value notification documentation must include:
    canned comment “CRIT”
    clinicians full name and title
    turn around time
    time of call
    initials of the technologist
Competency Element 2:
Reviewing and Reporting Results

## Slide 6: Documentation
Manually entered results are placed in the designated location. ~10% reviewed daily by the lead tech.
MTS/TMS tests that assigned to the technologist, must be completed by the designated time frame.
QC is performed and documented:
  Symex (CBC): at the start of each shift
  Symex (BF): daily
  Coag: every 8 hours (when in use)
  Tosoh: daily (when in use)
  ISed: daily (when in use)
  Manual tests: daily (when in use)
Competency Element 3:
Review of Intermediate Test Results or Worksheets

## Slide 7: Maintenance
Document all (daily, weekly, monthly, and as needed) maintenance procedures on the appropriate log sheets and/or onboard the analyzers.
Document reagent changes on Sysmex (add your initials)
Perform and document Tosoh maintenance, such as column and filter changes
Perform as needed maintenance
Competency Element 4: Instrument Maintenance

## Slide 8: Troubleshooting
General Troubleshooting
  Consult relevant manuals, coworkers, lead, and/or supervisor.
  If all troubleshooting efforts have been exhausted, place a service call and fill out the instrument specific log note the issue
    action taken
    outcome
    reference number (if applicable)
    date
    initials
Troubleshooting QC issues
  Check the reagent levels and control volume then rerun control.
  Rerun fresh vial of control and/or reagent.
  Contact Lead, Supervisor, or technical support as available
  Once corrected, properly document error, include action take, outcome, date, and initials
All major issues whether resolved or not should be noted on the communication log as well as the instrument log
Competency Element 5:
Evaluation of Problem-Solving Skills

## Slide 9: CAP and MTS
Proficiency testing is provided by CAP
  CAP Surveys can also be used to assess a technologist’s competency
Competency tests for individual areas are assigned on MTS.
Other methods of assessing test performance include:
  Review of path reviewed slides
  Blind testing (i.e., slide competency)
  Direct observation
Competency Element 6: Assessment of Test Performance

## Slide 10: Competencies are due July 31st, 2021
  Documentation in the accordion folder
  Blind slide competencies (manual diffs) in accordion folder
  MTS tests